IEEE P802.11
Wireless LANs

| Sequence Number Exempt Management Frames |
| --- |
| Date: 2011-05-11 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Harish Ramamurthy | Marvell Semiconductor, Inc. | 5488 Marvell Lane, Santa Clara, CA-95054 |  | harishr@marvell.com |
| Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA 94086 | +1 408 543 3370 | mfischer@broadcom.com |

### Overview

## REV HISTORY:

R0 – initial revision

Add the following abbreviation in Section 3.3

SNE 	Sequence Number Exempt

Modify Section 9.3.2.11  as follows:

The sequence number, for management frames that are not SNE and for data frames with the(11n) QoS subfield of the Subtype field (#10128)equal to 0, is generated by the transmitting STA as an incrementing sequence of integers. In a QoS STA, the sequence numbers for QoS (+)data(11n) frames are generated by different counters for each TID

and receiver pair and shall be incremented by one for each new MSDU or A-MSDU(11n) corresponding to the

TID/receiver pair.

The sequence number for management frames that are SNE may be set to any value and are ignored on reception.

Add a new sub-clause 8.7

8.7 Sequence number exempt management frames

The sequence number for management frames that listed in Table 8-<TBD> are set to any value.

Table 8-<TBD>

| Description | Management Frame Sub-type from Table 8-1 | Category Value from Table 8-36 | Action Value | Comments |
| --- | --- | --- | --- | --- |
| HT Action | 1101 | 7 | 0-7 | Notify Channel Width SM Power Save PSMP Set PCO Phase CSI Noncompressed Beamforming Compressed Beamforming ASEL Indices Feedback |
| HT Action No ACK | 1110 | 7 | 4-7 | Noncompressed Beamforming Compressed Beamforming ASEL Indices Feedback |
| Unprotected WNM | 1101 | 11 | 0-1 | TIM Frame, Timing Measurement |