IEEE P802.11
Wireless LANs

| Management frames exempt from QMF service |
| --- |
| Date: 2011-05-11 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Harish Ramamurthy | Marvell Semiconductor, Inc. | 5488 Marvell Lane, Santa Clara, CA-95054 |  | harishr@marvell.com |
| Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA 94086 | +1 408 543 3370 | mfischer@broadcom.com |

### Overview

## REV HISTORY:

R0 – initial revision

Modify Section 8.2.4.4.2 as follows:

A management frame is an IQMF frame when all five of the following conditions are met:

1.The RA of the management frame corresponds to an individual MAC address.

2.The frame is transmitted by a QMF STA .

3.The sending STA has previously received an Extended Capabilities element from the STA corresponding to the RA of the frame to be transmitted.

4.The most recently received such Extended Capabilit i es element indicated that the STA is a QoS STA and has the value of one in the Q MFActivated subfield.

5. The frame is not exempted from QMF service as described in 10.ae.1.4

A management frame is a GQMF frame when all five of the following conditions are met:

1.The RA of the management frame corresponds to a group MAC address.

2.The frame is transmitted by a QMF STA .

3.The transmitting STA has received an Extended Capabilities element that has the QMFActivated subfield equal to one from every member of the group address that is also a member of the BSS corresponding to the BSSID of the management frame.

4.The BSSID of the management frame is not the wildcard BSSID.

5. The frame is not exempted from QMF service as described in 10.ae.1.4

Add Clause 8.7ae. Exemptions to QMF Service

8.7.ae Exemptions to QMF Service

Management frames that are exempted from QMF Service are listed in Table 8-ae-<TBD>

Table 10-ae-<TBD>—Management frames exempted from QMF service

| Description | Management Frame Sub-type from Table 8-1 | Category Value from Table 8-36 | Action Value | Comments |
| --- | --- | --- | --- | --- |
| HT Action | 1101 | 7 | 0-7 | Notify Channel Width SM Power Save PSMP Set PCO Phase CSI Noncompressed Beamforming Compressed Beamforming ASEL Indices Feedback |
| HT Action No ACK | 1110 | 7 | 4-7 | Noncompressed Beamforming Compressed Beamforming ASEL Indices Feedback |
| Unprotected WNM | 1101 | 11 | 0-1 | TIM Frame, Timing Measurement |