IEEE P802.11
Wireless LANs

| Management frames exempt from QMF service |
| --- |
| Date: 2011-05-11 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Harish Ramamurthy | Marvell Semiconductor, Inc. | 5488 Marvell Lane, Santa Clara, CA-95054 |  | harishr@marvell.com |
| Matthew Fischer | Broadcom | 190 Mathilda Place, Sunnyvale, CA 94086 | +1 408 543 3370 | mfischer@broadcom.com |

### Overview

## REV HISTORY:

R0 – initial revision

R1 – Use SNE management frame table

Modify Section 8.2.4.4.2 as follows:

A management frame is an IQMF frame when all five of the following conditions are met:

1.The RA of the management frame corresponds to an individual MAC address.

2.The frame is transmitted by a QMF STA .

3.The sending STA has previously received an Extended Capabilities element from the STA corresponding to the RA of the frame to be transmitted.

4.The most recently received such Extended Capabilit i es element indicated that the STA is a QoS STA and has the value of one in the Q MFActivated subfield.

5. The frame is not a SNE management frame

A management frame is a GQMF frame when all five of the following conditions are met:

1.The RA of the management frame corresponds to a group MAC address.

2.The frame is transmitted by a QMF STA .

3.The transmitting STA has received an Extended Capabilities element that has the QMFActivated subfield equal to one from every member of the group address that is also a member of the BSS corresponding to the BSSID of the management frame.

4.The BSSID of the management frame is not the wildcard BSSID.

5. The frame is not a SNE management frame