IEEE P802.11
Wireless LANs

| Comment Resolution for RLQP |
| --- |
| Date: 2011-05-10 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Eunsun Kim | LG Electronics | Mobile Comm. Lab, LG R&D Complex 533, Hogye1, Dongan, Anyang, Korea | +82-31-450-1860 | esun.kim@lge.com |
| Yongho Seok | LG Electronics | Mobile Comm. Lab, LG R&D Complex 533, Hogye1, Dongan, Anyang, Korea | +82-31-450-1947 | yongho.seok@lge.com |

Introduction

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor:  Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.   As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

Discussion:

Initially, GAS Initial Request frame can be transmitted in pre-association. However, due to security requirement, any request frame for getting enablement in TVWS must be transmitted after secure association/authentication.

GAS Initial Request frame in TVWS cannot be transmitted without association/authentication. STA (mode I device) does not need to take care of the functionality or information beyond the AP(mode II device). Therefore, propose to remove RLQP from TGaf draft

Proposed Resolution:

COUNTER. Remove the Registered Location Query Protocol from TGaf draft 1.01 based on the discussion in 11/765r0 and 793r0. Editing instructions are below.

## Editing instructions:

TGaf editor: Remove subclause 8.4.5 Registered Location Query Protocol elements and corresponding occurrence in the TGaf draft 1.01.

# Text boxes

Abstract

Submission for Draft P802.11af_D1.0 comment resolution. The document addresses various comments related to RLQP (Registered Location Query Protocol).

Submission addresses Draft P802.11af_D0.1 comments,  43,44,109,122,191,192,193,194,195,196,197,331,361,423,424,425,426,427,428,429,430,431,432,433,434,492,532,539,557,558,559,567,568,601,602,603,604,605,608,622,623,624,625,626,658,659,715,716,717,719,720,721,722,728,732,745,746,747,751,765,766,826,862,892,893,894,895,896,899,913,914,965,966,967,982,983,984,985,986,989,990,1016,1017,1018,1019,1078,1079,1080,1081,1082,1083,1084,1085,1086,1087,1088,1089,1090,1176,1183,1208,1237.