## Slide 1: BF Clarifications
Date: 2011-06-14
Authors:
Slide 1

## Slide 2: Summary
This document proposes resolutions to CIDs 3037 on Draft 3.0 of TGad.
The comment relates to responder RXSS sector sweep feedback in Clause 9.35.2.4 (Page 283, Line 15~17).

## Slide 3: DBand antenna select field
DBand antenna select field is used during RSS and Sector Sweep Feedback to feedback the best (highest received SNR) antenna sector ID and antenna ID.
The antenna sector ID is set to zero and antenna ID is undefined in DBand antenna select field during Sector Sweep Feedback if responder RXSS is performed. This is different from the feedbacks in RSS and if responder TXSS is performed.
James Wang, MediaTek

## Slide 4: CID 7098 DBand antenna select field
9.35.2.4 Sector Sweep Feedback (P283L15~17) When responder RXSS was performed during the preceding RSS, the initiator shall set the Sector select field in the ScS-Feedback frame it transmits to zero and the responder shall ignore the value of the Sector select field transmitted by the initiator in the ScS-Feedback frame. The initiator shall set the SNR Report field to zero. The ScS-Feedback frame shall be transmitted through the sector identified by the value of the Sector select field received from the responder during its most recently completed RSS with the initiator.
9.35.2.4 Sector Sweep Feedback (P283L5~8) When responder TXSS was performed during the preceding RSS, the initiator shall set the Sector select field and the DBand antenna select field in the ScS-Feedback frame it transmits to the value of, respectively, the Sector ID field and DBand Antenna ID field of the frame received with the best quality during the responder TXSS. from the responder during the preceding responder TXSS.
James Wang, MediaTek

## Slide 5: CID 7098 DBand antenna select field during RSS
9.35.2.3.2 Responder TXSS (P280L38~40) During a responder TXSS, the responder shall set the Sector select field and the DBand antenna select field in each transmitted ScS frame to the value of, respectively, the Sector ID field and DBand Antenna ID field of the frame received with the best quality during the ISS. The determination of which frame is received with best quality is implementation dependent and beyond the scope of this specification. The responder shall set the SNR Report field to the SNR measured for the frame received with highest SNR during the ISS.
9.35.2.3.3 Responder RXSS(P282L16~19) During the responder RXSS, the responder shall set the Sector select field and the DBand antenna select field in each transmitted ScS frame to the value of, respectively, the Sector ID field and the DBand Antenna ID field of the frame received with the best quality during the ISS. The determination of which frame is received with best quality is implementation dependent and beyond the scope of this specification.
James Wang, MediaTek

## Slide 6: Discussion on Dband Sector select field
In 3 out of 4 cases, the Dband Sector select field is set to be the antenna sector ID/antenna ID in the best quality received frame.
Make the sector/antenna feedback in the Dband Sector select field consistent regardless if it is in the initiator direction or the responder direction and if the RXSS or TXSS is performed.
Although the feedback is for responder RXSS, the antenna ID and received SNR is still of value to the initiator.
James Wang, MediaTek

## Slide 7: Proposed Resolution
9.35.2.4 Sector Sweep Feedback (P283L15~17) When responder RXSS was performed during the preceding RSS, the initiator shall set the Sector select field in the ScS-Feedback frame it transmits to zero and the responder shall ignore the value of the Sector select field transmitted by the initiator in the ScS-Feedback frame. The initiator shall set the SNR Report field to zero. Sector select field and the DBand antenna select field in transmitted ScS-Feedback frame to the value of, respectively, the Sector ID field and the DBand Antenna ID field of the frame received with the best quality during the RSS. The determination of which frame is received with best quality is implementation dependent and beyond the scope of this specification. The initiator shall set the SNR Report field to the SNR measured for the frame received with highest SNR during the RSS.
James Wang, MediaTek