## Slide 1: Power Saving in Beam Beamforming for 11ad
Date: 2011-06-16
Authors:
Slide 1

## Slide 2
Abstract: This document discusses the power saving in beacon beamforming
Purpose: This document propose resolution for CID3205 and CID3208.
Summary
CID | Page | Clause | Comment | Proposed Change
3205 | 335 | 10.2.4.1 | Does the STA needs to wake up for every directional beacon ? That is not good for power consumption | Create a power saving feature to listen to selected beacons only
3208 | 294 | 9.35.5.4 | Please clarify "regular schedule". Does beacon transmission with multiple DBand antennas has a 16 regular schedule as well ? | Clarify

## Slide 3: Beacon Transmission
Currently, TXSS is performed during beacon transmission
TXSS rotates beacon transmission through antenna sectors in random order in BTI during one or multiple beacon intervals
TXSS can contain up to 128 sectors/antennas. However, most likely only up to 16 or 32 sectors are used.
Stations acquire the best TX antenna sector/antenna by listening to one or multiple beacons through TXSS training (at BTI or SP)
Power save stations periodically wake up to receive a beacon but does not know when the best sector/antenna occurs
Power save station stays up longer than necessary to wait for the “good” beacons  this increases power consumption

## Slide 4: PS STAs know the transmission schedule ?
9.35.5.4 Beamforming in A-BFT with multiple DBand antennas (P294L16): “A PCP/AP shall have an A-BFT every k BIs, where k is the value indicated by the N-BIs A-BFT subfield in the beacon interval control field. In an A-BFT, the PCP/AP shall receive in a quasi-omni antenna pattern using the DBand antenna indicated by the value of the DBand Antenna ID subfield within the ScS field transmitted in the DBand Beacon. A PCP/AP with multiple DBand antennas has a regular schedule of receiving through each DBand antenna. The PCP/AP shall switch RX DBand antenna every N A-BFT in Ant A-BFTs allocations, where N A-BFT in Ant is the value of the N A-BFT in Ant subfield within the beacon interval control field.
Does this imply PCP/AP has a regular schedule of transmitting each beacon through each antenna as well ? And only one antenna should be used in a beacon ? - needs clarifications
If this is the case, power save station can predict the schedule of the transmit antenna. However, power save station still cannot predict transmit sector schedule (thus, needs to stay awake longer during beacon reception).

## Slide 5: Wake Up Duration for Power Save Stations
Power save stations might need to be awake for all the BTI’s in a complete transmission of all sectors/antennas to receive a beacon
This increase the power consumption and could be a significant impact on the standby time of the battery-based devices
Lengthening the sleep period too long to save power can introduce latency
BTI (TXSS)
Beacon Interval
Complete Transmission of all Sectors/Antennas
Wake Up
Wake Up
Wake Up
BTI (TXSS)
BTI (TXSS)

## Slide 6: Desired Low Power Operation
Allow power save stations to predict the next time beacon will be transmitted through a selected sector/antenna.
Power save stations wake up to receive the desired beacon and go back to sleep
Reduces the wake up duty cycle (from up to 16 or 32 to 1)
BTI (TXSS)
Beacon Interval
Complete Transmission of all Sectors/Antennas
Wake Up
Earlier possible beacon transmission time
(Note: Receiver PLL can be turned on earlier to allow for sufficient time to settle)
TBTT
BTI (TXSS)
BTI (TXSS)

## Slide 7: Proposed Solution
PCP may send the parameters of the random Sector ID pattern to enable the power save stations to predict the schedule of sector/antenna to be used

## Slide 8: Random Antenna Sector ID Pattern
Desired property: rotate through all antenna sector IDs in N beacon transmissions (N= total number of antenna sectors) to provides good spatial coverage and low latency

## Slide 9: Random Sequence Generator 1
Sequence Generator 1 is shown in Figure and is defined as follows:
  Generate the sector IDs for subsequent DBand Beacons by advancing the Sequence Generator 1, which is initialized using Tap 1 and State 1 contained in the Antenna Sector ID Pattern element received from the PCP/AP.
  Advance the Sequence Generator 1 by one shift for each anticipated DBand Beacon transmission thereafter.
  After advancing the Sequence Generator 1, if the next state equals the initial state for the second time, overwrite the state with an all-zero state. The next state following the state following all zero-state uses the first 6 bits of the state of Sequence Generator 2 as the initial state.
  If the STA’s total number of sectors is not equal to the period of the Sequence Generator 1, ignore state(s) greater than or equal total number of sectors and continue advancing Sequence Generator 1 until the state is less than the total number of sectors.
NOTE – The taps are selected from the set of sequences with maximal length property.
0
1
2
3
4
5
0
1
2
3
4
5
Tap 1
State 1 (= Sector ID )
Sequence Generator 1

## Slide 10: Random Sequence Generator 2
Sequence Generator 2 is shown in Figure and is defined as follows:
  Sequence Generator 2 is initiated with the value of the Tap 2 and State 2 fields contained in the Antenna Sector ID Pattern element received from the PCP/AP.
  Sequence Generator 2 is advanced by one shift when a new initial state is needed from Sequence Generator 1.
NOTE – The taps are selected from the set of the sequences with maximal length property.
0
1
2
3
4
5
0
1
2
3
4
5
Tap 2
State 2
Sequence Generator 2
6
6
7
7

## Slide 11: Antenna Sector ID Pattern IE
Antenna sector ID pattern Response IE
Bits:
4
Type
6
Tap 1
8
Element ID
The Element ID field is equal to the value for the Antenna Sector ID Pattern, specified in Table 8-53 (Element IDs).
The Length field for this element indicates the length of the Information field.
The Type field is set to 0 for Random Sequence Generator. Values 1 to 15 are reserved.
  The Tap 1 field indicates the taps for Sequence Generator 1.
  The State 1 field indicates the state for Sequence Generator 1.
  The Tap 2 field indicates the taps for Sequence Generator 2.
  The State 2 field indicates the state for Sequence Generator 2.
6
State 1
8
Tap 2
State 2
8
Length
8

## Slide 12: Changes in 10.2.4.1
(P335L15 Insert text) PCP/AP may transmit Antenna Sector ID pattern element to non-PCP/non-AP station during transmission of the power save configuration response, probe response, during the PS mode set up, or other management frame exchanges.

## Slide 13: Changes in 10.2.4.1
(P335L23) - Active mode: A STA shall be in the Awake state, except that when in Active mode the STA can switch to Doze state in an Awake BI in the A-BFT and in all SPs/CBAPs in which the STA is allowed to Doze in as indicated in Table 51. During BTI, Each non-PCP/non-AP STA may only wake up to receive beacon(s) transmitted through the selected antenna sector ID(s), including the sector mostly recently transmitted to PCP/AP in the TXSS, using the information provided in the Antenna Sector ID pattern element.
(P335L26) - Power Save (PS) mode: A STA alternates between the Awake and the Doze states, as determined by the rules defined in this subclause. During BTI in the awake state, Each non-PCP/non-AP STA may only wake up to receive beacon(s) transmitted through the selected antenna sector ID(s), including the sector mostly recently transmitted to PCP/AP in the TXSS, using the information provided in the Antenna Sector ID pattern element.

## Slide 14: Changes in 10.2.4.1
(P335L41) Table 68 Power management states for an Awake BI
    BI portion | PPS PCP PS | non-PCP/non-AP STA
  BTI: BTI | Awake | Awake or Doze

## Slide 15: 8.5.16.4 Power Save Configuration Response
  (P188L28) Table 37 Power Save Configuration Response frame Action field format
  (Insert after P189L12)
  The Antenna Sector ID Pattern is defined in 8.4.2.xxx .
Order Information
1 Category
2 Action
3 Dialog Token
4 Status Code
5 Wakeup Schedule element (optional)
6 Antenna sector ID Pattern (optional)

## Slide 16: 8.3.3.10 Probe Response frame format
P110L12
40 | Multi-band | The Multi-band element is optionally present if dot11MultibandActivated is true.
41 | DBand Capabilities | The DBand Capabilities element is present when dot11DBandCapable is true.
42 | DBand Operation | The DBand Operation element is present when dot11DBandCapable is true.
43 | Multiple MAC address | The Multiple MAC addresses element is present when dot11MultipleMACActivated is true.
44 | Antenna Sector ID Pattern | The Antenna Sector ID Pattern element is optionally present.

## Slide 17: Clarifications of Beacon Transmission DBand antenna
(9.35.4 Beamforming in BTI, P289L12) When a PCP/AP has more than one DBand antenna, the TXSS shall cover all the sectors in all Dband antennas. A PCP/AP with multiple DBand antennas has a regular schedule of transmitting through each DBand antenna. Only one DBand antenna shall be used in a BTI.
(9.35.5.4 Beamforming in A-BFT with multiple DBand antennas, P296L16) A PCP/AP with multiple DBand antennas has a regular schedule of receiving through each DBand antenna corresponding to the Dband antenna in which the beacon is transmitted through.