## Slide 1: Discussion on WSM length comments
Date: 2011-06-21

## Slide 2: Abstract
This presentation shows proposed resolutions for comments75, 169, 171, 274, 383, 384 and 822.

## Slide 3: Comments
CID | Page (C) | Clause | Comment | Proposed Change
75 | 138.17 | E.3.1.5 | The "Length" column states that the Map Version is 7 bits long, but the "Value" column states 6 bits. | Make both consistent
169 | 32.27 | 8.4.2.1 | The minimum value of the specified lenth (=4) seems to contradict with the spec. Given in 8.2.4.af1. There, on page 29, lines 41--42, the WSM Information may have a length of zero. As a result, the total (minimal) length of the WSM element would be 3 and not 4. | Change "4" to "3" or adjust the description of the value of the length field within the WSM element such that the WSM Information within the WSM element is at least 1 octett long.
171 | 29.42 | 8.4.2.af1 | Why should I have a WSM element if it does not contain any WSM information? I would suppose the WSM Information within the WSM element should be at least 1 octett long which then would require to change the minimum value of the Length value. | Change the minimum value of the Length field to "2" and the minimum length for the WSM information field to 1. Attn: Note that if you do not change this accordingly, there is a change required to table 8-51 in 8.4.2.1 (see separate comment to change 4 to 3 in the table).

## Slide 4: Comments
CID | Page (C) | Clause | Comment | Proposed Change
274 | 27.32 | 8.4.2.1 | Max element lengths do not look right. | Figure out what the real maximums are and correct the table. Either every entry includes ID and Length fields, or they do not. Make it explicit. Figure it out. Fix it. Now. E.g. first entry should be 257, as baseline implies that ID and length are included in the length given in this table - i.e. the length in this table is NOT the max length field value, but the max total length of the element.
383 | 29.00 | 8.4.2.af1 | The text "The minimum value of the Length field is 1 (based on a minimum length for the WSM Information field of 0 octets)" is wrong. If the minimum length of the WSM information field is 0, the field is not present. In this case, only the Element ID and Length fields are present. Then, the Length field is 0. | Replace "The minimum value of the Length field is 1 (based on a minimum length for the WSM Information field of 0 octets)" with "The minimum value of the Length field is 0 (based on a minimum length for the WSM Information field of 0 octets)"

## Slide 5: Comments
CID | Page (C) | Clause | Comment | Proposed Change
384 | 27.32 | 8.4.2.1 | In 8.4.2.af1 you state that the WSM information field may not be present. In this case, the length field becomes 0. Thus, the whole IE has a length of two octets (one for the Element ID, one for the Length field). See 8.4.2.1 in 802.11-REVmb/D7.0 that reads "The Length field specifies the number of octets in the Information field. See Figure 8-65 (Element format)." | Replace "White Space Map (see 8.4.2.af1) <ANA> 4 to 255 […]" with "White Space Map (see 8.4.2.af1) <ANA> 2 to 257 […]"
822 | 27.33 | 8.4.2.1 | Length of White Space Map doesn't agree with description in 8.4.2.af1. | Change length to “3-257”.

## Slide 6: Proposed Resolutions
Agree CID 75 and 274
Agree in Principle 169, 171, 383, 384 and 822

## Slide 7: Format of WSM IE
WSM IE
WSM Information
 | Element ID | Length | WSM Type | WSM Information
Octets: | 1 | 1 | 1 | Variable
 | Device Class | Map ID | Channel Number | Maximum Transmit Power | Validity (Optional)
Octets: | 1 | 1 | 1 | 1 | 1

## Slide 8: Changes in the text
In Table 8-54
  Minimum Length should be 5 including Element ID and Length field
  Maximum Length should be 257 including Element ID and Length field
In sub-clause 8.4.2.129
  The minimum value of the Length field is 3 (based on a minimum length for the WSM Information field of 2 octets).