## Slide 1: Proposed resolutions for WSM announcement comments
Date: 2011-06-21

## Slide 2: Abstract
This presentation shows proposed resolutions for comments 499, 525, 555, 571 and 917

## Slide 3: Comments
CID | Page (C) | Clause | Comment | Proposed Change
499 | 64.31 | 10.af2.2 | The rational of white space map announcement frame in this clause is not clear. A Fixed or Mode II station should obtain the channel map directly from the database, whereas, a mode I device can receive it from the Mode II/Fixed device using channel availability query. | Clarify. This clause should only consider signaling of WSM as required by regulations. The reasons behind defining too many options of signaling WSM using beacons, probe response, WSM announcement, DSE enablement frame and channel availability query should be either clearly explained, or it should be limited to essential usage scenarios.

## Slide 4: Comments
CID | Page (C) | Clause | Comment | Proposed Change
525 | 48.00 | 8.5.11.1 | White Space Map Announcement frame should also be "protected dual of Public Action frame, because it delivers White Space Map, which should be transmitted securely. | Add Protected White Space Map Announcement frame and allocate a action field value for White Space Map Announcement frame.
555 | 48.00 | 8.5.11.1 | WSM announcement frame should be also a secure tranmission, due to its importance | make appropriate changes to make a secure WSM announcement frame
571 | 48.00 | 8.5.11.1 | White Space Map Announcement frame should also be "protected dual of Public Action frame, because it delivers White Space Map, which should be transmitted securely. | Add Protected White Space Map Announcement frame and allocate a action field value for White Space Map Announcement frame. See forthcoming document 11-11/xxxxr0.
917 | 48.00 | 8.5.11.1 | White Space Map Announcement frame should also be "protected dual of Public Action frame, because it delivers White Space Map, which should be transmitted securely. | Add Protected White Space Map Announcement frame and allocate a action field value for White Space Map Announcement frame. See forthcoming document 11-11/xxxxr0.

## Slide 5: Proposed Resolutions
Agree 525, 555, 571 and 917
Agree in Principle 499
  Need to clarify the rationale of WSM announcement and modify its behaviors appropriately.

## Slide 6: Rational of WSM Announcement Frame
WSM announcement frame comes from a GDC Enabling STA
Signaling method of update of channel list
  CVS frame may be a way to signaling of the update
    However, CVS with different Map ID means that a STA receiving the CVS should perform CAQ request
  WSM Announcement frame is proposed for this purpose
    When the GDC Enabling STA obtains a new channel list, it should be able to signal the updated channel list
    In this case, GDC Enabling STA decides to transmit WSM Announcement frame or not

## Slide 7: Protected Dual of WSM Announcement
Security Requirements by FCC
  WSM Announcement carries a WSM which need to be transmitted in secure manner
  Especially in USA, WSM Announcement frame should be transmitted in secure, i.e. Protected Dual of WSM Announcement Frame
  Propose WSM Announcement frame to be transmitted in a form of Protected Dual of Public Action frame