IEEE P802.11
Wireless LANs

| Duration Size Fixes |
| --- |
| Date: 2011-06-30 |
| Author(s): |
| Name | Company | Address | Phone | Email |
| Gaius Wee | Panasonic |  |  | yaohuang.wee@sg.panasonic.com |
| Michael Sim | Panasonic |  |  |  |
| Masataka Irie | Panasonic |  |  |  |

| 3037 |  |  |  | General | T | Some subclauses in the spec need clarification | Submissions will be made |
| --- | --- | --- | --- | --- | --- | --- | --- |

7.3.2.95 Extended Schedule element

Modify paragraph fourteen as follows:

The Allocation Block Duration field indicates the duration, in microseconds, of a contiguous time block for which the SP or CBAP allocation is made and cannot cross BI boundaries. Possible values range from 1-32767 for an SP allocation and 1-65535 for a CBAP allocation.

8.4a.2 Allocation Info field

Modify paragraph six as follows:

When the Allocation Info field is transmitted within an SPR frame, the Allocation Duration field contains the duration requested in microseconds. When the Allocation Info field is transmitted within a Grant frame, the Allocation Duration field contains the duration of the SP or CBAP allocation (see 9.23.7, 9.23.8, 9.23.9). Possible values range from 0-32767 for an SP allocation and 1-65535 for a CBAP allocation.

8.4.2.117 Extended DBand TSPEC element

Modify Table 17 as follows:

Table 17 Allocation Period values

| B0-B14 | B15 | Meaning |
| --- | --- | --- |
| 0 | 0 | Reserved |
| 0 | 1 | Not periodic or periodicity unknown |
| 1-32767 | 0 | The allocation period is a multiple of the BI, i.e., allocation period = n x BI where n is the value represented by B0-B14 |
| 1-32767 | 1 | The allocation period is a fraction of the BI, i.e., allocation period = BI/n where n is the value represented by B0-B14. |

Modify paragraph thirteen as follows:

For isochronous requests, the Allocation Period, Minimum Allocation and Maximum Allocation fields are set as follows:

- The Allocation Period field indicates the period over which the allocation repeats.

- The Minimum Allocation field is set to the minimum acceptable allocation in microseconds in each allocation period.

- The Maximum Allocation field is set to the desired allocation in microseconds in each allocation period.

For asynchronous requests, Maximum Allocation field is reserved and the Allocation Period and Minimum Allocation fields are set as follows:

- The Allocation Period field indicates the period over which the minimum allocation applies. The Allocation Period is an integral multiple of the Beacon Interval.

- The Minimum Allocation field specifies the minimum allocation in microseconds that the STA expects within the allocation period.

Insert the following after paragraph thirteen as the new paragraph fourteen:

The Minimum SP Duration field specifies the minimum acceptable SP duration in microseconds. Possible values range from 0-32767. A value of 0 indicates no minimum specified.

Modify the new paragraph nineteen as follows:

The TSCONST Period field is specified as a fraction or multiple of the Beacon Interval as defined in Table XYZ . This field is used to indicate a periodic scheduling constraint.

Insert the following table after the new paragraph nineteen:

Table XYZ TSCONST Period values

| B0-B14 | B15 | Meaning |
| --- | --- | --- |
| 0 | 0 | Reserved |
| 0 | 1 | Not periodic or periodicity unknown |
| 1-32767 | 0 | The TSCONST period is a multiple of the BI, i.e., TSCONST period = n x BI where n is the value represented by B0-B14 |
| 1-32767 | 1 | The TSCONST period is a fraction of the BI, i.e., TSCONST period = BI/n where n is the value represented by B0-B14. |

# Text boxes

Abstract

This document proposes corrections for duration size inconsistencies.