IEEE P802.11
Wireless LANs

| TGah Functional Requirements and Evaluation Methodology Rev. 1 |
| --- |
| Date: 2011-07-11 |
| Author: |
| Name | Company | Address | Phone | Email |
| Minho Cheong | ETRI | 161 Gajeong-dong, Yuseong-gu, Daejeon, Korea | +82 42 860 5635 | minho@etri.re.kr |

ABSTRACT

This document describes the functional requirements and the evaluation methodology for TGah. These requirements are derived from the document “11-10-0001-13-0wng-900mhz-par-and-5c”. All proposals submitted in response to the IEEE802.11 TGah call for proposal must address the functional requirements that are shown as mandatory in this document.

# Contributors

This will grow to reflect those providing explicit contributions / review comments of this document. (Please let Minho know if any name is conspicuously missing from this list.)

| Name | Company | Address | Phone | Email |
| --- | --- | --- | --- | --- |

# Revision History

| Revision | Comments | Date |
| --- | --- | --- |
| R0 R1 | Initial draft of functional requirements Reflected discussions on June 27 and filled EM section | 27 June 2011 11 July 2011 |

# 1. Overview

This document specifies the functional requirements for TGah as stated in the Sub 1GHz license-exempt PAR and 5C’s. The emphasis is on the following aspects of TGah amendment.

- System performance

- Maintaining the 802.11 user experience

- Coexistence with 802.15.4 and 802.15.4g devices

- Enhanced power saving

- Compliance to PAR

This document also specifies the evaluation methodology and simulation scenarios for TGah devices.

# 2. Functional Requirements

# 2.1 System Performance

2.1.1 Supporting band

TGah R1 – The TGah amendment shall describe operation  in the license-exempt band below 1 GHz excluding the TV White Space bands. Example operating bands could include one or more of the following: 863-868.6 MHz (Europe), 950.8 MHz -957.6 MHz (Japan), 430-434 MHz, 470-510 MHz and 779-787 MHz (China), 917 – 923.5 MHz (Korea) and 902-928 MHz (USA).

2.1.2 Coverage and data rate

TGah R2 – The TGah amendment shall support mode of operation in which PHY data rate at least 100 Kbps is provided with coverage of 1km under regulatory transmission power limits.

2.1.3 OFDM PHY modulation

TGah R3 – The TGah amendment shall use an Orthogonal Frequency Division Multiplexing (OFDM) PHY modulation.

2.1.4 Number of associations

TGah R4 – The TGah amendment shall support a mode of operation that supports the number of associations beyond 2007 for outdoor applications.

# 2.2 Mainintaining the 802.11 User Experience

TGah R5 – The TGah amendment shall maintain the network architecture of the 802.11 system for fixed, outdoor, point-to-multi-point applications and support compability to 802.11 management plane defined in the existing 802.11 standard and its amendments.

# 2.3 Coexistence with 802.15.4 and 802.15.4g devices

TGah R6 – The TGah amendment shall provide a mechanism to enable coexistence with other systems in the bands including 802.15.4 and 802.15.4g.

# 2.4 Enhanced Power Saving

TGah R7 – The TGah amendment shall provide an enhanced power saving mechanism to support battery-powered operation with long replacement cycle.

# 2.5 Compliance to PAR

TGah R8 - The proposal complies with the PAR and 5 Criteria [1].

# 3. Evaluation Methodology

The evaluation methodology defines PHY performance, conditions for PAR compliance and a limited set of simulation scenarios and comparison criteria for TGah evaluatation.

It is recommended to exploit the evaluation methodology defined in this document when it is needed to submit a technical proposal which has a meaningful impact on network performance and only checking the PHY link performance may not be enough.

Each TGah proposal may use a PHY abstraction method. If a PHY abstraction method is used, the method must be described and disclosed.

# 3.1 PHY Performance

3.1.1 PHY channel model

Channel models defined in 802.11n channel model document [9] shall be used for indoor simulation scenarios with propoer modifications to large-scale path loss model.

3GPP-based outdoor channel models shall be used for outdoor simulation scenarios.

Channel model document will soon get an approval in TGah.

3.1.2 PHY impairments

This table is derived from the one used for TGac impairments modeling.

Please let Minho know if there is any need to change for TGah.

Table 1. PHY impairments

| Number | Name | Definition | Comments |
| --- | --- | --- | --- |
| IM1 | PA non-linearity | Simulation should be run at an oversampling rate of at least 2x. To perform convolution of the 2x oversampled transmit waveform with the channel, the channel may be resampled by rounding each channel tap time value to the nearest integer multiple of a sample interval of the oversampled transmit waveform. Use RAPP power amplifier model as specified in document 00/294 with p = 3. Calculate backoff as the output power backoff from full saturation: PA Backoff = ­10 log10(Average TX Power/Psat). Total TX power shall be limited to no more than 17 dBm. Disclose: (a) EIRP and how it was calculated, (b) PA Backoff, and (c) Psat per PA. Note: the intent of this IM is to allow different proposals to choose different output power operating points. Note: the value Psat = 25dBm is recommended. |  |
| IM2 | Carrier frequency offset | Single-user simulations for all comparisons except Offset Compensation shall be run using a fixed carrier frequency offset of –13.675 ppm at the receiver, relative to the transmitter. The symbol clock shall have the same relative offset as the carrier frequency offset. Simulations shall include timing acquisition on a per-packet basis. Downlink multi-user simulations for all comparisons except offset compensation shall be run using a fixed carrier frequency offset selected from the array [N(1) ,N(2),……,N(16) ], relative to the transmitter, where N(j) corresponds to the frequency offset of the j-th client and is randomly chosen from [-20,20] ppm with a uniform distribution. | . |
| IM3 | Phase noise | The phase noise will be specified with a pole-zero model. PSD(0) = -TBD dBc/Hz pole frequency fp = TBD kHz zero frequency fz = TBD kHz Note, this model results in PSD(infinity) = -TBD dBc/Hz Note, this impairment is modeled at both transmitter and receiver. | It is inevitable to change pole/zero frequency and PSD level. |
| IM4 | Noise figure | Input referred total noise figure from antenna to output of the A/D will be 10dB. |  |
| IM5 | Antenna Configuration | The TGn antenna configuration at both ends of the radio link shall be a uniform linear array of isotropic antennas with separation of one-half wavelength, with an antenna coupling coefficient of zero. The TGah antennas can be assumed to either be all vertically polarized or a mix of vertical and horizontal polarizations or dual polarization at ±45 degree, as specified in the TGac channel model addendum document [11] |  |
| IM6 | Fluoroscent Light Effects | The fluoroscent light effects specifed in the TGn Channel model shall not be considered for the TGah indoor simulation scenarios. |  |
| Other impairments |  |  | Please let Minho know if there are other PHY impairments to consider specifically for TGah. |

3.1.3 Interference modeling

Interference modelling for TGah network simulation will be introduced here.

3.1.3 Comparison criteria

- PER vs. SNR curves

- all MCS’s

- Simulate all of channel models

- Simulation must include:

- updated PHY impairments

- timing acquisition on a per-packet basis

- preamble detection on a per-packet basis

# 3.2 Traffic Models

TGah evaluation shall consider traffic models for TGah-specific applications such as smart grid, sensor networks and so on define in 802.11ah usage model document [15], as well as some of conventional 802.11 traffic models [4] which are applied to the extended range Wi-Fi in TGah.

Table 2. Traffic models

| Num. | Application | Offered Load per link (bps) | Protocol | MSDU Size (Byte) | Max. PLR | Max. Delay (ms) | Replacement cycle (sec.) | Source [ref] |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Smart Grid | TBD (1.6-37.4 bps at PHY) | TBD (2 way periodic/burst) | 16808 | TBD (PER <10%) | TBD | an hour to a day (3600-86400 sec.) | [16-18] |
| 2 | Sensor networks (IoT) | TBD (70-420 bps at PHY) | TBD (2 way periodic/event-based) | 512 | TBD (PER <10%) | TBD | 10-60 | [17,18] |
| 3 | Healthcare/clinic | TBD (65 Kbps at PHY) | TBD (2 way periodic/event-based) | 2048 | TBD (PER < 10%) | TBD | 0.25 | [17,18] |
| 4 | Fitness/elderly care | TBD (70 bps at PHY) | TBD (2 way periodic/event-based) | 512 | TBD | TBD | 60 | [17,18] |
| 5 | Home/building automation | TBD (70 bps at PHY) | TBD (2 way periodic/event-based) | 512 | TBD | TBD | 60 | [17,18] |
| 6 | Industrial process automation | TBD (51.2 bps – 5.12 Kbps at PHY) | TBD (2 way periodic/burst) | 64 | TBD (PER <1%) | 200 | 0.1-10 | [18] |
| 7 | Cellular offloading (web browsing) | 256K | TCP | 64 | N/A (PER < 10%) |  | N/A | [17,18] |
| 8 | Cellular offloading (video/audio streaming) | 100K–4M | UDP | 512 | 10^-4 (PER < 10%) | 200 | N/A | [17,18] |
| 9 | Cellular offloading (audio streaming) | 64K-256K | UDP | 418 | 10^-4 (PER < 10%) | 200 | N/A | [17,18] |
| 10 | SDTV | 4M-5M | UDP | 1500 | 5*10^-7 | 200 |  |  |
| 11 | VoD control channel | 60K | UDP | 64 | 10^-2 | 100 | N/A | Guess |
| 12 | Video Conf | 128K-2M | UDP | 512 | 10^-4 | 100 | N/A |  |
| 13 | Internet Streaming video/audio | 100K–4M | UDP | 512 | 10^-4 | 200 | N/A |  |
| 14 | Internet Streaming audio | 64K-256K | UDP | 418 | 10^-4 | 200 | N/A | Group guess |
| 15 | VoIP | 96K | UDP | 120 | 5% | 30 | N/A | ITU-T G.114 300ms round-trip delay G.711 Codec |
| 16 | MP3 Audio Other formats are taking over (AAC/MPEG-4, OggVorbis, etc) | 64K–320K | UDP | 418 | 10^-4 | 200 | N/A |  |
| 17 | Video phone | 500K | UDP | 512 | 10^-2 | 100 | N/A | Aps guess |
| 18 | Remote user interface (X11, Terminal Server Client) (remote display/keyboard/mouse) | 500K-1.5M (peak) | UDP | 700 | N/A | 100 | N/A | 11-03-0696r0 |
| 19 | Content download (photo camera) | Max. 10Mbps | TCP | 1500 | N/A |  | N/A | Corresponds to USB and flash speed |
| 20 | Internet File transfer (email, web, chat) | Max. 10Mbps | TCP | 300 | N/A |  | N/A |  |
| 21 | Clicking on web link | 256K | TCP | 64 | N/A |  | N/A | desribed in 11-03-0802r23 (pp.27) |
| 22 | Infinite Source Model | Infinite (transmit buffer always full) | TCP | 1500 or 1000 or 300 | N/A |  | N/A | Popular model in network analysis |

# 4. Simulation Scenarios

The simulation scenarios define a limited set of simulation scenarios for network simulation considering traffic model, location of STAs, interference modelling and overlapped BSS effect for TGah evaluation.

Simulation scenarios for TGah evaluation are summarized as:

Table 3. Simulation scenarios

| Scenario Number | Purpose | Note |
| --- | --- | --- |
| 1 | Test compliance to PAR. | Aggregated PHY data rate at least 100 Kbps is provided with coverage of 1 km under regulatory transmission power limits. |
| 2 | Outdoor application with an extremely large number of stations for smart grid | Includes smart grid specific data flows. Aligns with Category 3 applications. |
| 3 | Outdoor application with a moderately large number of stations for sensor network | Includes sensor network specific data flows. Aligns with Category 3 applications. |
| 4 | Indoor application with dozens of nodes for healthcare and building automation | Stress test for TGah operation. Scenario with large number of flows. Aligns with Category 1 and Category 3 applications. |
| 5 | Outdoor application with dozens of nodes for extended range Wi-Fi | Stress test for TGah operation. Scenario with large number of flows. Aligns with Category 1, Category 2 and Category 3 applications. |

# 4.1 Test for Compliance to PAR

4.1.1 Point-to-multi-point link test (scenario #1)

Synthetic test case to demonstrate multi-STA aggregated PHY data rate at least 100 Kbps with coverage of 1 km during some time interval.

This scenario is motivated by the scenario #19 defind in 802.11n usage model document [4] and scenario #1,2 defined 802.11ac functional requirements and evaluation methodology document [9].

Number of stations (AP + STAs): at least 11

One TGah AP is source

Number of TGah STAs which are sinks : at least 10

Traffic from AP to STA

Protocol: UDP

Offered load : infinite

MSDU size: 512

PHY channel model

TBD (outdoor channel model for TGah)

Locations of stations

Fixed locations are represented as 3-dimensional coordinates.

Meet requirements in [functional requirements Sections 2.1.2]

Table 4. Flows in scenario #1

| Flow No. | Source | Source Location (meters) | Sink | Channel Model | Sink Location (meters) | Application | Application Load (Mbps) | Rate Distribution | MSDU Size (B) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |
| 1 | AP | (0,0,5) | STA1 | TBD | 1000x | Data |  | Infinite Backlog , UDP | 512 |
| 2 | AP | (0,0,5) | STA2 | TBD | 1000x | Data |  | Infinite Backlog , UDP | 512 |
|  | : : | : : |  | : : | : : | : : |  | : : | : : |
| N | AP | (0,0,5) | STAN | TBD | 1000x | Data |  | Infinite Backlog , UDP | 512 |

Note) Different bit rate can be offered to each flow.

# 4.2 Outdoor Application with an Extremely Large Number of Stations for Smart Grid (scenario #2)

Test case to demonstrate smart grid application with smart grid specific data flows.

6001 stations

One TGah AP is source and sink.

6000 STAs are souces and sinks.

Traffic from AP to STAs

Metering data

Traffic from STAs to AP

Control data

Traffic STAs to STAs

None

PHY channel for each link

Channel model type applied : TBD (outdoor channel model for TGah)

Locations of stations

Fixed locations with AP elevation of 2-30 m and STA elevation of 1-10 m

AP’s location : (0,0,10)

STAs’ locations : randomly distributed with normal distribution within a coverage 1km.

Meet requirements specified in PLR and Max. Delay per each flow

Total throughput condition

It is available to offer infinite load for this scenario with TCP flows if there is any TCP flows defined in this scenario.

Table 5. Flows in scenario #2

| Flow No. | STAs (Source/Sink) | Source Location (meters) | Sink Location (meters) | Channel Model | Application (Forward Traffice / Backward Traffic) | Application Load (Mbps) (Forward / Backward) | Rate Distribution (Forward / Backward) | MSDU Size (B) (Forward / Backward) | Max. Delay (ms) (Forward / Backward) | Max. PLR (Forward / Backward) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Total Throughput |  |  |  |  |  |

# 4.3 Outdoor Application with a Moderately Large Number of Stations for Sensor Network (scenario #3)

Test case to demonstrate sensor network application for environmental and agricultural monitoring with their specific data flows.

201 stations

One TGah AP is source and sink.

200 STAs are souces and sinks.

Traffic from AP to STAs

Moniroting data

Traffic from STAs to AP

Control data (very few)

Traffic STAs to STAs

None

PHY channel for each link

Channel model type applied : TBD (outdoor rural channel model for TGah)

Locations of stations

Fixed locations with AP elevation of 5-10 m and STA elevation of 1-2 m

AP’s location : (0,0,10)

STAs’ locations : randomly distributed with normal distribution within a coverage 1km.

Meet requirements specified in PLR and Max. Delay per each flow

Total throughput condition

It is available to offer infinite load for this scenario with TCP flows if there is any TCP flows defined in this scenario.

Table 6. Flows in scenario #3

| Flow No. | STAs (Source/Sink) | Source Location (meters) | Sink Location (meters) | Channel Model | Application (Forward Traffice / Backward Traffic) | Application Load (Mbps) (Forward / Backward) | Rate Distribution (Forward / Backward) | MSDU Size (B) (Forward / Backward) | Max. Delay (ms) (Forward / Backward) | Max. PLR (Forward / Backward) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Total Throughput |  |  |  |  |  |

# 4.4 Indoor Application with Dozens of Stations for Healthcare and Building Automation (scenario #4)

Test case to demonstrate indoor application with over 30 flows for healthcare and building automation.

Locations of stations can be derived from well-defined indoor scenario #4 (enterprise network) defind in 802.11n usage model document [4] or indoor scenario #5 defined in 802.11ac functional requirements and evaluation methodology document [20].

31 stations

One TGac AP is source and sink.

30 STAs are souces and sinks.

Traffic from AP to STAs

Monitoring data for healthcare, fitness, elderly care and building automation

Traffic from STAs to AP

Control data for healthcare, fitness, elderly care and building automation

PHY channel for each link

Channel model type applied : TBD (Indoor model D based on 802.11n channel model)

Channel model break point between LOS and NLOS : unchanged from 802.11n

Shadowing term is TBD dB

In 802.11n channel model document [8], shadow fading std. dev. is specified for each channel model between 3dB and 6dB at page 7.

But in 802.11n usage model document [3], shadowing term applied to all the 802.11n simulation scenarios is set to 0dB for generating a channel realization at page 22.

Locations of stations

Fixed locations with AP elevation of 2-5 m and STA elevation of 1-2 m

AP’s location : (0,0,5)

STAs’ locations : 2-dimensional locations are unchagend from 802.11n scenario #4.

Meet requirements specified in PLR and Max. Delay per each flow

Total throughput condition

It is available to offer infinite load for this scenario with TCP flows if there is any TCP flows defined in this scenario.

Figure 3: STA locations for scenario #4.

Table 7. Flows in scenario #4.

| Flow No. | Source | Source Location (meters) | Sink | Sink Location (meters) | Channel | Application | Application Load (Mbps) | Rate Distribution | MSDU Size (B) | Max. Delay (ms) | Max. PLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |  |  |
| 1 | AP | (0,0) | STA1 | (5,-9.5) |  |  |  |  |  |  |  |
| 2 | AP | (0,0) | STA2 | (3.5,7.5) |  |  |  |  |  |  |  |
| 3 | AP | (0,0) | STA4 | (-4.5,0.5) |  |  |  |  |  |  |  |
| 4 | AP | (0,0) | STA5 | (-1.5,6) |  |  |  |  |  |  |  |
| 5 | AP | (0,0) | STA7 | (-9,-5) |  |  |  |  |  |  |  |
| 6 | AP | (0,0) | STA8 | (-8.5,8.5) |  |  |  |  |  |  |  |
| 7 | AP | (0,0) | STA10 | (-3,0.5) |  |  |  |  |  |  |  |
| 8 | AP | (0,0) | STA11 | (-0.5,8) |  |  |  |  |  |  |  |
| 9 | AP | (0,0) | STA13 | (-4,-4) |  |  |  |  |  |  |  |
| 10 | AP | (0,0) | STA14 | (7.5,-1) |  |  |  |  |  |  |  |
| 11 | AP | (0,0) | STA16 | (8,-6) |  |  |  |  |  |  |  |
| 12 | AP | (0,0) | STA17 | (0,-7.5) |  |  |  |  |  |  |  |
| 13 | AP | (0,0) | STA19 | (-2.5,-4.5) |  |  |  |  |  |  |  |
| 14 | AP | (0,0) | STA20 | (0.5,-2) |  |  |  |  |  |  |  |
| 15 | AP | (0,0) | STA25 | (3.5,-5) |  |  |  |  |  |  |  |
| 16 | AP | (0,0) | STA26 | (9,9.5) |  |  |  |  |  |  |  |
| 17 | AP | (0,0) | STA28 | (-8,-5.5) |  |  |  |  |  |  |  |
| 18 | AP | (0,0) | STA29 | (1.5,3.5) |  |  |  |  |  |  |  |
| Flow No. | Source | Source Location (meters) | Sink | Sink Location (meters) |  |  |  |  |  |  |  |
|  | Uplink Flows |  |  |  |  |  |  |  |  |  |
| 19 | STA1 | (5,-9.5) | AP | (0,0) |  |  |  |  |  |  |  |
| 20 | STA2 | (3.5,7.5) | AP | (0,0) |  |  |  |  |  |  |  |
| 21 | STA4 | (-4.5,0.5) | AP | (0,0) |  |  |  |  |  |  |  |
| 22 | STA5 | (-1.5,6) | AP | (0,0) |  |  |  |  |  |  |  |
| 23 | STA7 | (-9,-5) | AP | (0,0) |  |  |  |  |  |  |  |
| 24 | STA8 | (-8.5,8.5) | AP | (0,0) |  |  |  |  |  |  |  |
| 25 | STA22 | (0,-4.5) | AP | (0,0) |  |  |  |  |  |  |  |
| 26 | STA23 | (-1.5,7) | AP | (0,0) |  |  |  |  |  |  |  |
| 27 | STA25 | (3.5,-5) | AP | (0,0) |  |  |  |  |  |  |  |
| 28 | STA26 | (9,9.5) | AP | (0,0) |  |  |  |  |  |  |  |
| 29 | STA28 | (-8,-5.5) | AP | (0,0) |  |  |  |  |  |  |  |
| 30 | STA29 | (1.5,3.5) | AP | (0,0) |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Total Measured Throughput |  |  |  |  |  |

# 4.5 Outdoor Application with Dozens of Stations for Extended Range Wi-Fi (scenario #5)

Test case to demonstrate outdoor application for extended range Wi-Fi.

51 stations

One TGah AP is source and sink.

50 STAs are souces and sinks.

Traffic from AP to STAs

Downlink data flows for cellular offloading (for 25 stations)

Conventional downlink data flows (within limited rate condition) for extended range hot spot (for 25 stations)

Traffic from STAs to AP

Clicking on web link, file upload, video conferencing, VoIP et al.

PHY channel for each link

Channel model type applied : outdoor urban or sub-urban channel model for TGah

Locations of stations

Fixed locations with AP elevation of 5-10 m and STA elevation of 1-2 m

AP’s location : (0,0,10)

STAs’ locations : randomly distributed with normal distribution within a coverage 1km.

Meet requirements specified in PLR and Max. Delay per each flow

Total throughput condition

It is available to offer infinite load for this scenario with TCP flows if there is any TCP flows defined in this scenario.

Table 8. Flows in scenario #5.

| Flow No. | Source | Source Location (meters) | Sink | Sink Location (meters) | Channel | Application | Application Load (Mbps) | Rate Distribution | MSDU Size (B) | Max. Delay (ms) | Max. PLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Downlink Flows |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Total Measured Throughput |  |  |  |  |  |

# 4.6 Comparison Criteria

PHY data rate

Aggregated PHY data rate (downlink + uplink + STA-to-STA)

PHY Data rate of each flow in the simulation scenario

MAC SAP throughput (goodput)

Aggregated throughput (downlink + uplink + STA-to-STA)

Throughput of each flow in the simulation scenario

Packet Loss Rate for each flow in the simulation scenario

Lost packets include

Packets that exceed maximum latency requirement

Packets that are dropped after exceeding maximum number of re-tries

Specify number of antennas for each STA used in the simulation scenario

Specify number and frequency width of frequency channels used in the simulation scenario

Specify regulatory power limits considered in the simulation scenario.

# 4.5 Results Presentation Format

This format will be introduced here.

# 5. Summary of Functional Requirements

Table 9. Summary of functional requirements

| Requirement Number | Description | Requirement Statement | Status of Requirement | Notes (informative) |
| --- | --- | --- | --- | --- |
| R1 |  |  |  |  |
| R2 |  |  |  |  |
| R3 |  |  |  |  |
| R4 |  |  |  |  |
| R5 |  |  |  |  |
| R6 |  |  |  |  |
| R7 |  |  |  |  |
| R8 |  |  |  |  |

# 6. References

- 11-10-0001-13-0wng-900mhz-par-and-5c

- 11-08-0807-04-0vht-below-6-ghz-par-nescom-form-plus-5cs

- 11-03-0813-13-000n-functional-requirements

- 11-03-0802-23-000n-usage-models

- 11-08-0307-01-0vht-on-the-feasibility-of-1gbps-for-various-mac-phy-architectures

- 11-08-0535-00-0vht-phy-and-mac-throughput-analysis-with-80-mhz-for-vht-below-6-ghz

- 11-09-0071-01-00ac-discussion-on-functional-requirements

- 11-03-0814-31-000n-comparison-criteria

- 11-03-0940-04-000n-tgn-channel-models

- 11-09-0059-04-00ac-tgac-802.11ac-proposed-selection-procedure

- 11-09-0376-01-00ac-proposal-for-tgac-evaluation-methodology

- 11-09-0308-12-00ac-tgac-channel-model-addendum-document

- 11-09-0161-02-00ac-802.11ac-usage-model-document

- 11-09-0980-01-00ac-change-edits-for-enterprise-simulation-scenario

- 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document

- http://collaborate.nist.gov/twiki-sggrid/pub/SmartGrid/PAP02Objective3/NIST_PAP2_Guidelines_for_Assessing_Wireless_Standards_for_Smart_Grid_Applications_1.0.pdf

- 11-11-0299-00-00ah-tgah-use-cases-summary-and-aggregated-phy-rates-analysis

- 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document

- 11-11-0747-02-00ah-discussion-review-of-tgah-functional-requirements-and-evaluation-methodology

- 11-09-0451-16-00ac-tgac-functional-requirements-and-evaluation-methodology

- 16-08-004-05-00m- IEEE 802.16m Evaluation Methodology Document (EMD)

# Comments

As defined in Selection Procedure document (11-11/0238r2), TGah functional requirements document also include evaluation methodology (network simulation scenarios)

They are a small set of very essential and key requirements without which we cannot call the amendment TGah.

Each requirement in the FR-EM document had better be described as a normative text without any specific number as possible.

“e.g.” is used expression in PAR document. This meaning is that there may be additional qualifying bands below 1GHz, and the regulations may be changing in some regions.

In order to resolve some ambiguity on whether enumerated examples belong to TGah bands or TVWS bands, this sentence is reworded by Dalton’s suggestion.

By discussions at the conference call at 27th June, 2011, all the possible China bands are remained for TGah applications for the time being. Sun Bo (ZTE) may have a plan to inform TGah later if there is any meaningful change in China regulations.

Based on “15-10-0180-01-004g-current-status-of-japanese-regulatory-changes-regarding-950mhz-band.pdf”, the current band is 950.8-957.6MHz (1mW max power or 10mW from 954MHz). But, based on discussions with author of the above reference, by the end of year 2011 the spectrum will move to roughly 916-930 MHz while still maintaining 1MHz limit.

For the supporting bands, some of the bands introduced as examples in PAR document may not be appropriate for 11ah operation due to limited max bandwidth based on doc.11-11/0685r0. For example, China 470-510MHz has less than 200 KHz limit.

I think combining coverage and data rate into one requirement is suitable because it may be confusing otherwise.

Of course, it must be checked later based on an adopted path loss model in order to see this value can be achieved. In addition, there will be some specific simulation scenario with channel models applied in evalution methodoloy section in this document to check compliance to PAR. I think kind of normative text without many explanatory notes may be more suitable for functional requirements section from experiences in other task groups.

I’m reminded that this 100kbps which is described in PAR document was the result of compromise with 15.4g on the PHY rate aspect to get the PAR approved. So, I would suggest using “PHY data rate at least 100 Kbps” instead of MAC throughput at SAP. Since TGah is not trying to have higher MAC throughput, defining it as PHY rate should be sufficient for PHY/MAC design.

In addition, I would not chage the minimum data rate requirement as greater value than 100Kbps because 100Kbps is applied to most of use cases in the use case document. Only use cases (1d), (3a), (3b) specifies data rate over 100Kbps.

While extending coverage up to 2km was proposed by Yokogawa Electric specifically for use case (1d) with many metallic walls, most of TGah people attending the conferecall on 11th April don’t want to change coverage requirement which is already described as 1km in the PAR document.

In addition, the original proposer withdrew his proposal. In his subsequent submission (11-11/0547r0), required coverage for used case (1d) in typical cases is less than 500m.

Ron justified that 1km coverage is reasonable checking link budget in his document (11-11/0552r1).

Because regulatory conditions are highly depending on regions, considering regulatory transmission power limits is inevitable to describe the requirement for coverage and data rate. It needs to optimize the rate vs. range in a given band. PAR also says that the data rates defined in this amendment optimize the rate vs. range performance of the specific channelization in a given band.

While most of use cases only need 50~100 STAs, some use case (smart grid use case (1a) ) needs 6000 STA/AP capacity. Currently from WG11 standards, number of associations available is limited to 2007. With 2007 associations, the max size of the TIM is 251 octets. Since number of associations will have an impact on the system design it should be reflected in the functional requirements document. There is also a comment that extending the number of associations is inevitable if we support 11i. So, it needs to support a mode of operation in which the number of associations can extend beyond 2007 to cover smart grid use case, which is one of the original TGah applications. This value may be set as a concrete number later if TGah can agree later.

Because there were some comments that this sentence needs to be described in more detail, some phases are added. These are captured from "802.11 user experience" section in TGad functional requirements.

This phrase enumerates all the possible application types in TGah.

PAR says “maintaining the 802.11 WLAN user experience for fixed, outdoor, point-to-multi point applications.”

5C says “Compatibility with IEEE 802 requirements will result from keeping the MAC SAP interface the same as for the existing 802.11 standard. The proposed amendment shall introduce no 802.1 architectural changes. The MAC SAP definition shall not be altered, ensuring that all LLC and MAC interfaces are compatible to and in conformance with the IEEE 802.1 Architecture, Management and Internetworking standards. New managed objects shall be defined as necessary in a format and structure consistent with existing 802.11 managed objects.”

Compatibility with the existing 802.11 standard and its amendments (802.11i/w/s/k/v/u or other TGs) can be also included as one of maintaining 802.11 user experience. Does this mean that 802.11i/w/s/k/v/u shall be used in all the applications? No, it is just about compatibility.

This requirement for user experience is about maintaining the network architecture of the 802.11 system and compatibility to 802.11 management plane, not to PHY features of other task groups operating in other bands such as 11n, 11ac, 11ad, 11af and so on.

So, it does not mean that fast session transfer shall be supported which provides a seamless transfer of an active session from the Sub1GHz band to the 2.4/5GHz band, and vice versa, as similar as TGad.

FYI, while TVWS bands are used for 11af, there is no description about fast session tranfer or connectivity to 2.4/5GHz WLAN devices even in TGaf draft. Instead, it may be kind of vendor's options.

There is already a specific use case (2a) which needs coexistence with 15.4g. PAR document describes “provides mechanisms that enable coexistence with other systems in the bands including IEEE 802.15.4 and IEEE P802.15.4g”. 5C document describes need to make a coexistence assurance document which is meant for 15.4g as follows: The working group will create a CA document and specifically reference IEEE P802.15.4g as part of the WG balloting process. So, coexistence with IEEE802.15, IEEE802.15.4g and other systems in the bands is inevitable.

There was a debate on whether just a CA document is enough without any description about this in the FR-EM document. After checking the FR document in other task groups in WG11, there are some other instances describing the coexistence with other, such as those of TGac and TGad. In addition, it seems better for the FR document to inherit the PAR document.

Low throughput devices may desire larger sleep time, generally 15 minutes and in some extreme cases less a day. Most of TGah devices may be expected to have very long battery duration time.

I would include the enhanced power saving feature in functional requirements because it is kind of newly-introduced feature in TGah and may have a big impact on system design. About defining some specific number for duty cycle or battery life and so on, it may be better to describe in spec. framework document or TGah draft rather than in functional requirements.

This phrase “for sensor devices” is deleted because it may induce some unintended ambiguity.

Doppler value defined in 802.11 channel model document [9] may need to be moderated, which have already had agreement in TGac channel modeling discussions. Refer to [12].

It may be up to further discussions in TGah on whether downlink multi-user MIMO feature can be allowed in TGah or not.

It is also needed to check on whether second order modeling for phase noise is applicable for 900MHz bands.

Klauss may have a plan to present a submission at San Francisco meeting (July in 2011) on 3GPP-based interference modelling methodology.

Among rows in the following table, TGah-specific traffic models are described from #1 to #9. From #10, conventional traffic models which can be applied to TGah extended Wi-Fi usage are described.

Traffic models for backhaul link are not included in this table because most of backhaul network using TGah needs an interface to 802.15.4g devices which is very hard to model. In addition to that, it has been rarely coverd in WG11 simulation scenarios handling backhaul link because it does not have prioritized usage compared to other usage models. If we try to simulate backhaul network only consisting of 11ah devices, it may be possible to re-use the traffic models originally defined for sensor networks, in my personal thinking.

This value (1.56 bps at PHY) is obtained in [17] that all the needed information size for a STA at one shot (16808 byte) is divided by one of replacement cycle candidate (typically one day for smart grid application). Because this value is quitely low compared to other possible applications in TGah, it is needed to check on whether this value is enoughly meaningful.

While this value is decribed as 32000 in 11/299r0, I set this value to be 64 as it is described in the TGah use case document (11/0457r0).

This value is derived from the TGah use case document that industrial process automation requires latency of hundres of miliseconds.

Refer the traffic model “Clicking on web link”.

Refer the traffic model “Internet streaming video/audio”.

Refer the model “Internet streaming audio”.

Klaus may have a plan to propose an interference modelling for TGah network simulation (maybe in July 2011).

With larger number of clients, especially in an outdoor environments, it is more probable to have hidden nodes and overlapped BSS effect.

To take into consideration these, it may be desirable just to include it as an additional simulation scenario considering OBSS deployment, which is also an adopted approach in TGac discussions.

As already introduced in [19], it is desirable to set 4 or so simulation scenarios:

- From use case category 1 (sensors and meters), outdoor with an extremely large number of nodes and indoor/outdoor with a moderately large number of nodes

- From use case category 2 (backhaul sensor and meter data), backhaul network is not easy to simulate because it also needs 15.4g devise needs to be taken into consideration

- From use case category 3 (extended range Wi-Fi), outdoor with moderately high data rate.

In addition, OBSS scenarios for outdoor environments may be considered for a later step.

It is also needed to consider some simple scenario to check the PAR compliance.

Because regulatory conditions are highly depending on regions, considering regulatory transmission power limits is inevitable to describe the requirement for coverage and data rate. It needs to optimize the rate vs. range in a given band. PAR also says that the data rates defined in this amendment optimize the rate vs. range performance of the specific channelization in a given band.

Category 1 : video type application,

Category 2 : audio-type application, Category 3 : data type application.

It is needed to set a specific time duration to check this average data rate.

This value is derived from fact that the minimum required number of stations over all the use cases is 10.

All the stations are arranged circularly with a distance of 1km from the AP.

Because there is no document to refer to in other standars such 802.16n, 802.16m, 3GPP MTC, 802.15.4g, it is inevitable to define a new scanrios for smart grid network simulation.

It is needed to discuss in TGah on whether we allow varied replacement cycles in an smart grid network or not.

To gurantee simulation reliability, fidelity criterion will be introduced based on the methodology used in 802.16m EMD document [21].

Because there is no document to refer to in other standars such 802.16n, 802.16m, 3GPP MTC, 802.15.4g, it is inevitable to define a new scanrios for smart grid network simulation.

It is needed to discuss in TGah on whether we allow varied replacement cycles and multiple use cases in one sensor network or not.

To gurantee simulation reliability, fidelity criterion will be introduced based on the methodology used in 802.16m EMD document [21].

It is needed to discuss in TGah on whether we allow other conventional indoor Wi-Fi application as well as these traffic models in this scenario.

It is needed to discuss in TGah on whether we will also consider multi-story building effect or not.

Source location needs to be changed into 3-dimensional coordinate.

Sink locations need to be changed into 3-dimensional coordinates.

Because conventional hot spot scenario defined in 11n document (using channel model E) can not be applied to this scenario due to coverage different, it is inevitable to define a new scanrios for smart grid network simulation.

To gurantee simulation reliability, fidelity criterion will be introduced based on the methodology used in 802.16m EMD document [21].