## Slide 1: Secure Enablement and CVS without Persistent Association
Authors:
6-28-2011

## Slide 2: Motivation
FCC rules require secure transmission of
  White space map
  Contact Verification Signal
Current 802.11af draft requires a “secure association” to provide the necessary protection for transmission of the WSM and CVS
  Implication:
    All APs will need to be enablers to associate dependent STAs
    All APs will need accurate geo location
We aim to design a protocol that keeps the enabling AP(E-AP) function separate from the data serving AP (S-AP) function

## Slide 3: Proposed Enablement Flowchart
Key sent in an encrypted MPDU

## Slide 4: Operation of Enablement Procedure
D-STA associates with E-AP using a secure association procedure as required by the E-AP
D-STA requests enablement from the E-AP using the enablement procedure.
After obtaining enablement, D-STA creates a random key K and sends it to the E-AP
  The D-STA and E-AP both initialize a 64-bit counter CVS-WSMSeqNo to zero.
D-STA then disassociates from E-AP
D-STA may then associate with any other AP, even other dependent APs (this AP is called the serving AP)
All other communication from D-STA to E-AP use a “pull method” as described later

## Slide 5: Obtaining a CVS from E-AP
D-STA obtains a CVS by requesting one from E-AP
  CVS Request frame is a public action frame
  CVS Request is a good approach since it frees the E-AP from determining whether the D-STA is in sleep mode before sending CVS
D-STA obtains a CVS from E-AP as follows
  The D-STA forms a Nonce and a MIC by applying the AES-CCM Generation/Encryption process [1] using the key K to the concatenation of:
    The current CVS-WSMSeqNo,
    a single direction bit set to 0,
    and 39 zeroes (to form a 128-bit block).
  The CVS-WSMSeqNo and the MIC is sent in the CVS request public action frame.
When E-AP receives a CVS request, it forms the CVS (a public action frame) as follows:
  E-AP authenticates the transmitter of the CVS request through the MIC
  E-AP then forms a MIC for CVS message by concatenating applying the AES-CCM Generation/Encryption process o
    The received CVS-WSMSeqNo,
    a single direction bit set to 1
    and 31 zeroes
    The WSM-ID
  E-STA forms the body of the CVS as CVS-WSMSeqNo, | Encrypted WSM-ID | MIC
When D-STA receives CVS
  D-STA decrypts the CVS received and verifies if the CVS-WSMSeqNo corresponds to the number sent in the CVS request and then checks the WSM-ID

## Slide 6: Frame Formats CVS/CVS Request
CVS and CVS Request are Public Action Frames
  CVS-WSMSeqNo. Provides replay protection
CVS Request
CVS

## Slide 7: Operation if WSM changes
Operation when CVS indicates new WSM-ID
  D-STA requests the WSM similar to the way that it requests a CVS.
  WSM request message contains CVS-WSMSeqNo and MIC obtained by applying the AES-CCM Generation/Encryption process [1] to the concatenation of:
    The current CVS-WSMSeqNo,
    a single direction bit set to 0,
    and 39 zeroes
When E-AP receives a WSM request, it returns the WSM ( in a public action frame) as follows:
  E-AP authenticates the transmitter of the WSM request through the MIC
  E-AP then forms the MIC for the WSM message by concatenating
    The received CVS-WSMSeqNo,
    a single direction bit set to 1
    The WSM-ID, and WSM
    Some zero padding may be required
    The WSM message is formed with CVS-WSMSeqNo, Encrypted WSM and MIC

## Slide 8: Frame Formats WSM Request/WSM
Message formats for WSM request and WSM
Request
WSM

## Slide 9: References
[1] NIST SP-800-38C Recommendation for Block Cipher Modes of Operation: The CCM Mode for Authentication and Confidentiality