## Slide 1: Secure Enablement and CVS without Persistent Association
Authors:
October 2011
Name | Affiliations | Address | Phone | email
Santosh Abraham | Qualcomm Inc | 5775 Morehouse Dr., San Diego, CA | +1-858 651 6107 | sabraham@qualcomm.com
Steve Shellhammer | Qualcomm Inc | 5775 Morehouse Dr., San Diego, CA | +1-858-658-1874 | sshellha@qualcomm.com
Philip Hawkes | Qualcomm Inc | 77 King Street Sydney, New South Wales 2000 (Australia) | 61-2-9384-0203 | phawkes @qualcomm.com
Cameron McDonald | Qualcomm Inc | 77 King Street Sydney, New South Wales 2000 (Australia) | 61-2-9384-0204 | cameronm@qualcomm.com
Jouni Malinen | Qualcomm | Hermiankatu 6-8 D Tampere, Finland |  | jouni@qca.qualcomm.com

## Slide 2: Abstract
The submission provides techniques that allow a GDC dependent STA to remain enabled even if it disassociates from its GDC enabling STA. The amendment resolves an issue raised by CID 951 which highlights the need for Mode 1 APs. Due to the necessity of a secure association between a GDC dependent STA and its GDC enabling STA to obtain enablement and the requirement that an STA can have only one association, a GDC dependent STA cannot associate with a Mode 1 AP. This amendment proposes a method for a GDC Dependent STA to maintain a secure link with a GDC enabling STA while associated with another AP such as a Mode 1 AP.
951 | 4 | The FCC requirement for embedded geo-location limits the placement of Mode II APs indoors, restricting placement to be near a window or another location where GPS lock can be obtained. This severly limits the placement of APs indoors. The standard needs support for a low-rate enabler which can be placed near a window where it can obtain GPS lock and can provide enablment to all the Mode I AP and STAs throughout the building. In addition, this makes it possible for Mode I APs to be used, which reduces the complexity of these APs since they no longer require embedded GPS. | Add text from document IEEE 802.11-11/257. | 951

## Slide 3: Motivation
FCC rules require secure transmission of
  White space map (WSM)
  Contact Verification Signal (CVS)
  Encrypted transmission of WSM and CVS
To comply with the above, for the current 802.11af draft a GDC dependent STA requires a continuous “secure association” to an GDC enabling AP.
802.11 Revmb does not permit more than one association, the enabling AP will have to also provide data services
Therefore:
  All APs will need to be enablers to associate dependent STAs
      APs would have to be Mode II and accurate geo location capability
We present an augmentation to the current GDC enablement protocol that keeps the (GDC) Enabling AP(E-AP) function separate from the data serving AP (S-AP)

## Slide 4: Network Operation with Separate Enabler

## Slide 5: Proposed “Augmented” Enablement Flowchart
S. Abraham, Qualcomm Inc.

## Slide 6: Operation of Enablement Procedure
D-STA associates with E-AP using a secure association procedure as required by the E-AP
During the secure association the E-AP and D-STA generate an Enablement Key (EK) along with the PTK
D-STA requests enablement from the E-AP using the enablement procedure.
D-STA then disassociates from E-AP
D-STA may then associate with any other AP, even other dependent APs (this AP is called the serving AP)
All other communication from D-STA to E-AP use a “pull method” as described later

## Slide 7: Obtaining a CVS from E-AP
All messages between the E-AP and D-STA (after disassociation) use self protected action frames that are encrypted using the EK generated during the association
D-STA obtains a CVS by requesting one from E-AP
  CVS Request approach frees the E-AP from tracking the sleep state of the D-STA when sending the CVS
When E-AP receives a CVS request, it responds with a CVS containing the CVSIE if it is able to de-crypt the self protected action frame using the EK.
Operation when CVS indicates new WSM-ID
  D-STA sends self protected Channel Availability Query( CAQ) with reason result set to WSM
  D-STA uses self protected CAQ response frame to send the WSM

## Slide 8: Frame Formats
CVS Request:
  Only contains Category and Action field
Self protected CVS:
  Similar to the CVS public action frame, with category field indicating self protected
Self protected CAQ: For WSM
  Similar to CAQ public action frame with category field indicating self protected.

## Slide 9: Appendix
Definitions and Terminology

## Slide 10: FCC Terminology
Term | Definition
Mode I personal portable device | A personal/portable TVBD that does not use an internal geolocation capability and access to a TV bands database to obtain a list of available channels. A Mode I device must obtain a list of available channels on which it may operate from either a fixed TVBD or Mode II personal/portable TVBD. A Mode I device may not initiate a network of fixed and/or personal/portable TVBDs nor may it provide a list of available channels to another Mode I device for operation by such device.
Mode II personal portable device | A personal/portable TVBD that uses an internal geo-location capability and access to a TV bands database, either through a direct connection to the Internet or through an indirect connection to the Internet by way of fixed TVBD or another Mode II TVBD, to obtain a list of available channels. A Mode II device may select a channel itself and initiate and operate as part of a network of TVBDs, transmitting to and receiving from one or more fixed TVBDs or personal/portable TVBDs. A Mode II personal/portable device may provide its list of available channels to a Mode I personal/portable device for operation on by the Mode I device
Network initiation | The process by which a fixed or Mode II TVBD sends control signals to one or more fixed TVBDs or personal/portable TVBDs and allows them to begin communications.

## Slide 11: IEEE
Term | Definition | 
AP | An entity that contains one station (STA) and provides access to the distribution services, via the wireless medium (WM) for associated STAs. | From 802.11 Draft Revmb
Serving AP (S-AP) | AP that is associated with the STA providing connectivity to external networks. Serving AP may contain a GDC Enabling STA or a GDC Dependent STA | New
GDC Enabling STA | A STA that has the authority to control the operation of GDC dependent STAs after obtaining available spectrum for use at its own location. | From 11af Draft 1.02
Enabling AP (E-AP) | GDC enabling STA that is an AP | New
GDC Dependent STA (D-STA) | A STA that is under the control of Geo-location Database Controlled enabling STA | From 11af Draft 1.02

## Slide 12: Mode 1 APs are Permitted
An IEEE 802.11 AP provides access to the distribution system for associated STAs
Such a device may be an FCC Mode I device
This device may not enable other STAs by sending control signals to them to allow them to begin transmitting in the TVWS. That must be done by a Mode II Enabling AP