IEEE P802.11
Wireless LANs

| LB171 D1.0 2comment resolution (MAC CSM MLME) |
| --- |
| Date: 2011-07-08 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Zhou Lan | NICT | 3-4,Hikarino-oka, Yokosuka, 239-0847, Japan | +81-46-847-5097 | lan@nict.go.jp |
| Chen Sun | NICT |  |  |  |
| Yohannes Alemseged | NICT |  |  |  |
| Hiroshi Harada | NICT |  |  |  |

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor:  Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.   As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

# MAC CSM related comments

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 470 | 17.45 | 6.3.af5.1.1 | Hopefully the function is doing more than blindly sending a frame. Is this requesting that a new management schedule be installed? Is it requesting info on what the current schedule is? | If this is requesting info on the current management schedule, say so. But then why is the primitive called "CHANNELSCHEDULEMANAGEMENT"? Why not "CHANNELMANAGEMENTSCHEDULE"? |

Discussions:

This is not simply blindly sending out a frame for channel schedule information. It triggers a STA to start a transaction of sending and receipt of Channel Schedule Management Request/Response frames to obtain channel schedule information from an enabling STA. The name of the primitive should be consistent with that of other sections. No change should be made.

Propose: Rejected to CID 470  due to consistency of the naming with other primitives, no change is required.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 473 | 19.06 | 6.3.af5.2.1 | What is a "request to channel schedule management"? Is it a request to initiate management? Or a request to channel a schedule? Or to channel some management? | If this is about a request for information on a current channel management schedule, then say that. |

Discussions:

This sentence applies to the section of the .confirm primitive. Therefore, it describes the MAC behaviour of reporting the results of CSM to SME. Propose to change the sentence to “This primitive reports the result of Channel Schedule Management query.” to avoid misunderstanding.

Propose: Revised to CID 473 per discussions and editing instructions in 802.11-11/0918r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1050 | 17.57 | 6.3.af5.1.2 | If this is a confirmed primitive, it is strictly peer-to-peer, and the address of the peer must be specified. | Add address parameters as necessary to .request/.confim/.indication/.response. |
| 1053 | 21.17 | 6.3.af5.4.2 | I suppose there was a reason that ChannelScheduleManagement parameter is present in this primitive. But that reason is no apparent as the .confirm primitive doesn't include this parameter. | Add this parameter to the .confirm. Because the ChannelScheduleManagement parameter is present in the request, as well as the response, it's not clear exactly who communicates what. There is no indication of what the SME actually provides. Add this clarification here. |

Discussions:

As pointed out by the commenter, peerMACaddress is needed for all these primitives to indicate the source and destination of the frames. Also the ChannelScheduleManagement is needed for .confirm to let SME know the results. Propose to accept CID 1050 and revise 1053 by adding ChannelScheduleManagement to .confirm.

Propose: Accepted to CID 1050, per discussions and editing instructions in 802.11-11/0918r1.

Propose: Revised to CID 1053, per discussions and editing instructions in 802.11-11/0918r1.

# Editing instructions

6.3 MLME SAP Interface

6.3.93 Channel schedule management

6.3.93.1.2 Semantics of the service primitive

TGaf Editor: change  6.3.93.1.2 as follows:

The primitive parameters are as follows:

MLME-CHANNELSCHEDULEMANAGEMENT.request (

PeerMACAddress,

ChannelScheduleManagement,

Protected,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC address | Any valid individual MAC address | The address of the peer MAC entity to which the Channel Schedule Management frame was sent. |
| ChannelScheduleManagement | A set of information subfields | As described in 8.4.2.132 (Channel Schedule Management element) | As described in 8.4.2.132 (Channel Schedule Management element). |
| Protected | Boolean | true, false | Specifies whether the request is sent using a Robust Management frame. If true, the request is sent using the Protected ChannelScheduleManagement frame. If false, the request is sent using the ChannelScheduleManagement frame. |
| VendorSpecificInfo | A set of vendor specific elements | As defined in 8.4.2.28 (Vendor Specific element) | Zero or more elements. |

6.3.93.2 MLME-CHANNELSCHEDULEMANAGEMENT.confirm

6.3.93.2.1 Function

TGaf Editor: change the first paragraph of 6.3.93.2.1 as follows:

This primitive reports the result of a request to channel schedule management query.

6.3.93.2.2 Semantics of the service primitive

TGaf Editor: change 6.3.93.2.2 as follows:

The primitive parameters are as follows:

MLME-CHANNELSCHEDULEMANAGEMENT.confirm (

PeerMACAddress,

ChannelScheduleManagement,

ResultCode,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC address | Any valid individual MAC address | The address of the peer MAC entity from which the Channel Schedule Management frame was received. |
| ChannelScheduleManagement | A set of information subfields | As described in 8.4.2.132 (Channel Schedule Management element) | As described in 8.4.2.132 (Channel Schedule Management element). |
| ResultCode | Enumeration | SUCCESS, INVALID_PARAMETERS, UNSPECIFIED_FAILURE | Reports the result of a channel schedule management request. |
| VendorSpecificInfo | A set of vendor specific elements | As defined in 8.4.2.28 (Vendor Specific element) | Zero or more elements. |

6.3.93.4.2 Semantics of the service primitive

TGaf Editor: change 6.3.93.4.2 as follows:

The primitive parameters are as follows:

MLME-CHANNELSCHEDULEMANAGEMENT.response (

PeerMACAddress,

ChannelScheduleManagement,

VendorSpecificInfo

)

| Name | Type | Valid range | Description |
| --- | --- | --- | --- |
| PeerMACAddress | MAC address | Any valid individual MAC address | The address of the peer MAC entity to which the Channel Schedule Management frame was sent. |
| ChannelScheduleManagement | A set of information sub fields | As described in 8.4.2.132 (Channel Schedule Management element) | As described in 8.4.2.132 (Channel Schedule Management element). |
| VendorSpecificInfo | A set of vendor specific elements | As defined in 8.4.2.28 (Vendor Specific element) | Zero or more elements. |

# Text boxes

Abstract

This document contains proposed resolution of some of the comments categorized as MAC CSM in LB171 of P802.11af D1.0, shown in 802.11-11/0277r12. Proposed resolutions are based on 802.11af  draft text D1.02.

This submission provides resolution to comment CID 470, 473, 1050, 1053.