IEEE P802.11
Wireless LANs

| LB171 D1.0 2comment resolution (MAC CSM MLME Procedure) |
| --- |
| Date: 2011-07-08 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Zhou Lan | NICT | 3-4,Hikarino-oka, Yokosuka, 239-0847, Japan | +81-46-847-5097 | lan@nict.go.jp |
| Chen Sun | NICT |  |  |  |
| Yohannes Alemseged | NICT |  |  |  |
| Hiroshi Harada | NICT |  |  |  |

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor:  Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.   As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

# MAC CSM related comments

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 94 | 17.36 | 6.3.af5 | No protocol exchange figure is given | Supply a protocol exchange figure like Figure 6-af1 and Figure 6-af2 |

Discussions:

No other sections in current D1.01 provide figures. The description in this sub clause is sufficient to explain the transactions of the primitives. It is better to keep consistency with other sections.

Propose: Rejected to CID 94 per discussions in document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 61 | 54.39 | 10.af2 | "The STA may try request other RLS or the same RLS later on" nuh? | Change "The STA may try request other RLS or the same RLS later on" to "The STA may try sending this request to another RLS or it may wait and retry the same request to the same RLS." and it probably ought to say something about the minimum delay period (1us, 1 sec, 1 week). |

Discussions:

If the CSM request is rejected by a RLSS or a GDC enabling station, the STA that sent the CSM request may try the same STA, another STA or other RLSS. The waiting time however should be implementation dependent and need not be specified in the standard. Propose to remove this whole sentence to avoid misunderstanding.

Propose: Revised to CID 61, per discussions and editing instructions in document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 222 | 56.23 | 10.af2.2 | Be specific and do not allow reserved valued in the formulaton. | Replace "values ohter than 0 and 1" with an enumeration of valid values |
| 223 | 56.26 | 10.af2.2 | Be specific and do not allow reserved valued in the formulaton. | Replace "values ohter than 0 and 1" with an enumeration of valid values |
| 224 | 56.05 | 10.af2.2 | Be specific and do not allow reserved valued in the formulaton. | Replace "values ohter than 0 and 1" with an enumeration of valid values |
| 225 | 56.07 | 10.af2.2 | Be specific and do not allow reserved valued in the formulaton. | Replace "values ohter than 0 and 1" with an enumeration of valid values |

Propose: Accepted to CID 222, 223, 224, 225 without discussion, per editing instructions in document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 253 | 54.00 | 10.af2 | "The STA should choose a set of channels from.." Why a set of channels and not a complete list of channels? Also in the next sentence is the "set" (in my mind subset) related also to TV channels and WLAN channels? Also does "The STA" mean "The enabling STA"? | Please clarify. |

Discussions:

"A set of channels" doesn’t prohibit the enabling STA requesting the schedule information on a complete list of channels. It provides flexibility for an enabling STA to request schedule information only on the channels that are interesting, to reduce overhead of signalling. "The STA" in current draft means "The enabling STA". No modification on the draft text is required.

Propose: Accepted to CID 253, per discussion and editing instructions in document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 257 | 54.00 | 10.af2 | In these three paragraphs enabling STA can send information to another enabling STA. Why is this necessary since each enabling STA should be able to obtain this information on its own? Is this in the case when one of the enabling STAs can not reach database? | Please explain. |

Discussions:

An enabling STA may not have direct access to database, in that case it has to rely on another enabling STA that has direct internet access to obtain the schedule information. No modification on the draft text is required.

Propose: Accepted to CID 257, per discussion and editing instructions in document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 298 | 54.04 | 10.af2 | Is a STA required to use RLQP when there is an RLQP that is "reachable"? If a STA decides to use non-RLQP, then is there any guarantee that the request will eventually find a server that can respond to the query? | Clarify. |

Discussions:

RLQP is one option that a STA can use to obtain channel schedule information. An AP may use RLPQ Advertisement Protocol element as defined in 8.4.2.95 to indicate its capability of supporting RLQP. However, a STA after receiving the advertisement doesn’t have to use RLQP. It can use Channel Schedule Management action frame to obtain the channel schedule information. It is guaranteed that an enabling STA that sends enabling signal will have database access for channel availability and schedule information.

Propose: Accepted to CID 298, per discussion in document 11-11/0919r1. No modification to the draft text is required.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 299 | 54.24 | 10.af2 | What "channel schedule management query" are we talking about? | Please provide a reference and context for the reference. |

Propose: Accepted without discussion, per editing instructions in document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 445 | 54.05 | 10.af2 | The text talks frequently about Channel Schedule Management Request and Response frames, but no such frames are defined. | Define Channel schedule Management Request and Response frames. |

Discussions:

The Channel Schedule Management Request and Response frames are defined in 8.5.8.30. The reference of the section number should be provided. Propose to add references of the section number.

Propose: Revised to CID 445, per discussion and editing instructions in document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 475 | 20.28 | 6.3.af5.3.2 | This table includes a DialogToken row, though there is no such parameter in the list above. | Delete the DialogToken row. |

Propose: Accepted to CID 475, without discussion per editing instructions in this document 802.11-11/0919r1.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 938 | 54.28 | 10.af2 | "The STA should choose a set of channels from the available channels in the WSM to be included in the Channel Schedule Management Query." The STA can request Schedule Information on TV channel which is not available. In that case, if the channel is not available for 48 hours, what is included in response frame? | Add the following sentences in line 32 of 54 page : "When the requested channel is not available, Channel Availability Starting Time is omitted and the Channel Availability Duration is set to 0." |

Discussions:

As commented, there are two cases that need to be considered. Case 1, the channels are available at the time that the query response is about to be transmitted, and case 2, the channels are not available at that moment but may be available in a future time. Both cases are covered by the Channel Schedule Management function. Propose to delete the sentence for the first case.

Propose: Revised to CID 938 by deleting “from the available channels in the WSM”, per discussion and editing instructions in document 802.11-11/0919r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1111 | 54.20 | 10.af2 | What is "active mode". I suspect it is not the STA's power-saving state. | Describe this transition with reference to existing terminology. |

Discussions:

There is no “active mode” defined in the standard. However it is not necessary to mention power saving mode here. Propose to remove the sentence to avoid misunderstanding.

Propose: Revised to CID 1111 by deleting the whole sentence per discussion and editing instructions in document 802.11-11/0919r1.

# Editing instructions

10.10.6 Channel Schedule Management

TGaf Editor: change the first paragraph of 10.10.6 as follows:

Upon receipt of MLME-CHANNELSCHEDULEMANAGEMENT.request, the MLME shall schedule for transmission a CSM Request frame. If the parameter Protected of the MLME-CHANNELSCHEDULEMANAGEMENT.request has the value true, then the CSM Request frame as defined in 8.5.8.30(Channel Schedule Management frame format) shall be transmitted in a Protected Dual of Public Action frame, otherwise the CSM Request frame shall be transmitted in a Public Action frame.

TGaf Editor: change the third paragraph of 10.10.6  as follows:

Each time that an enabling STA with dot11ChannelScheduleManagementActivated set to true enters active mode, it should utilize the Channel Availability Query procedure as defined in 10.12.6.2 (Channel availability query (CAQ) Procedures) to obtain an available channel list with WSM. The STA should choose a set of channels from the available channels in the WSM to be included in the Channel Schedule Management Query a query request of CSM element as defined in 8.4.2.109. If the STA sets the Channel Schedule Management Mode field to zero, then the Channel Number field of the query shall be set to TV channels. If the STA sets the Channel Schedule Management field to one, then the Channel Number field of the query shall be set to WLAN channels.

TGaf Editor: change the fifth paragraph of 10.10.6 as follows:

An enabling STA can be is directed to transmit a CSM Request to a RLSS to query the schedule information on TV channels. By default, a RLSS shall be able to provide channel schedule information on TV channel. The RLSS may responds with Reason Result Code set to Request declined due to reasons such as overloaded requests. The STA may try sending this request to another RLSS or it may wait and retry the same request to the same RLSS.

10.10.6.2 Channel Schedule Management Responding STA

TGaf Editor: change the second, third, sixth and seventh paragraph of 10.10.6.2 as follows:

—Reason result code = values other than 0 and 1 2, 3, 4, 5, 6, 7, 8 and 9 as described in 8.4.2.10.132 (Channel Schedule Management element).

—CSM mode = values other than 0 and 1 2, 3, 4 and 5 as described in 8.4.2.10.132 (Channel Schedule Management element).

—Reason result code = values other than 0 and 1 2, 3, 4, 5, 6, 7, 8 and 9 as described in 8.4.2.132 (Channel Schedule Management element).

—CSM mode = values other than 0 and 1 2, 3, 4 and 5 as described in 8.4.2.132 (Channel Schedule Management element).

# Text boxes

Abstract

This document contains proposed resolution of some of the comments categorized as MAC CSM in LB171 of P802.11af D1.0, shown in 802.11-11/0277r12. Proposed resolutions are based on 802.11af  draft text D1.02.

This submission provides resolution to comment CID 94, 61, 222, 223, 224, 225, 253, 257, 298, 299, 445, 475, 938, 1111.