IEEE P802.11
Wireless LANs

| D0.1 Comment Resolution – CID 2163, 2714, 2715, 2716 |
| --- |
| Date: July 14, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Liwen | STMicroelectronics |  |  | Liwen.chu@st.com |

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 2163 | 8.5.4.2 | 59 | 59 | TR | The receiver can not decode Source Association ID. | Fix the problem. |
| 2714 | 8.5.4.3 | 60 | 12 | TR | The receiver can not decode Source Association ID. | Fix the problem. |
| 2715 | 8.5.13.2 | 60 | 60 | TR | The receiver can not decode Source Association ID. | Fix the problem. |
| 2716 | 8.5.13.3 | 61 | 12 | TR | The receiver can not decode Source Association ID. | Fix the problem. |

Discussion:

In 802.11 ac draft 1.0, A DLS/TDLS STA carries Association ID (as specified in 8.4.1.8) in DLS/TDLS related action frames so that its DLS/TDLS peer STA can figure out partial AID in VHT PHY header. In 8.4.1.8, the AID is defined as:

Association ID (AID)

Octets:                        2

Before AID field in DLS/TDLS STA DLS/TDLS related action frames, there are some IE fields. This means that a receiver can not differentiate the first octet of AID field from element ID.

A new AID IE should be defined.

Proposed Resolution Text:

##### 8.4.2.1 General

Insert the new elements shown below into Table 8-53 (Element IDs):

Table 8-53—Element IDs

| Element | Element ID | Length of indicated element (in octets) | Extensible |
| --- | --- | --- | --- |
| VHT Capabilities (see 8.4.2.100 (VHT Capabilities element)) | <ANA> | 14 |  |
| VHT Operation (see 8.4.2.101 (VHT Operation element)) | <ANA> | 7 |  |
| Extended(#1260) BSS Load (see 8.4.2.102 (Extended BSS Load element)) | <ANA> | 7 | Yes |
| Wide Bandwidth Channel Switch (see 8.4.2.103 (Wide Bandwidth Channel Switch element)) | <ANA> | 5 | Yes |
| VHT Transmit Power Envelope (see 8.4.2.104 (VHT Transmit Power Envelope element)) | <ANA> | 6-256 | Yes |
| Extended Power Constraint (see 8.4.2.105 (Extended Power Constraint element)) | <ANA> | 4-256 | Yes |
| AID (see 8.4.2.106 (AID element)) | <ANA> | 4 |  |

TGac editor: Add a new subclause to 8.4.2:

##### 8.4.2.106 AID element

The AID element includes the AID value assigned by an AP during association that represents the 16-bit ID of a STA. The format of the AID element is shown in Figure 8-acxx.

| Element ID | Length | Association ID (AID) |
| --- | --- | --- |

Octets:                  1                     1                                      2

Figure 8-acxx  AID element

The Assoociation ID is defined in subclause 8.4.1.8.

8.5.4.2 DLS Request frame format

TGac editor: Insert rows for Order 10 and 11 in Table 8-190 as follows:

##### Table 8-190—DLS Request frame Action field format

| Order | Information | Notes |
| --- | --- | --- |
| 10 | Association ID | The Association ID (as specified in 8.4.2.106) of the STA sending the frame is present if the dot11VHTOptionImplemented attribute is true |
| 11 | VHT Capabilities | The VHT Capabilities element is present if the dot11VHTOptionImplemented attribute is true |

##### 8.5.4.3 DLS Response frame format

TGac editor: Insert rows for Order 10 and 11 in Table 8-191 as follows:

##### Table 8-191—DLS Request frame Action field format

| Order | Information | Notes |
| --- | --- | --- |
| 10 | Association ID | The Association ID (as specified in 8.4.2.106) of the STA sending the frame is present if the dot11VHTOptionImplemented attribute is true |
| 11 | VHT Capabilities | The VHT Capabilities element is present if the dot11VHTOptionImplemented attribute is true |

8.5.13.2 TDLS Setup Request frame format

##### TGac editor: Insert rows for Order 18 and 19 in Table 8-230 as follows:

##### Table 8-230—Information for TDLS Setup Request frame

| Order | Information | Notes |
| --- | --- | --- |
| 18 | Association ID | The Association ID (as specified in 8.4.2.106) of the STA sending the frame is present if the dot11VHTOptionImplemented attribute is true |
| 19 | VHT Capabilities | The VHT Capabilities element is present if the dot11VHTOptionImplemented attribute is true |

8.5.13.3 TDLS Setup Response frame format

##### TGac editor: Insert rows for Order 18 and 19 in Table 8-231 as follows:

##### Table 8-231—Information for TDLS Setup Response frame

| Order | Information | Notes |
| --- | --- | --- |
| 19 | Association ID | The Association ID (as specified in 8.4.2.106) of the STA sending the frame is present if the dot11VHTOptionImplemented attribute is true |
| 20 | VHT Capabilities | The VHT Capabilities element is present if the dot11VHTOptionImplemented attribute is true |

# Text boxes

Abstract

This document provides resolution for the following CIDs on TGac D1.0:

CID 2163, 2714, 2715, 2716