IEEE P802.11
Wireless LANs

| D0.1 Comment Resolution – CID 2157, 2158 |
| --- |
| Date: June 27, 2011 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Liwen | STMicroelectronics |  |  | Liwen.chu@st.com |

| CommentID | Subclause | Page | Line | CommentType | Comment | SuggestedRemedy |
| --- | --- | --- | --- | --- | --- | --- |
| 2157 | 8.2.5.2 | 25 | 12 | TR | This Duration setting rule may create more collision. | Fix the problem. |
| 2158 | 8.2.5.2 | 25 | 15 | TR | This Duration setting rule may create more collision. | Fix the problem. |

Discussion:

In 8.2.5.2, for an NDPA frame, the Duration/ID field is set to the estimated time required to transmit the

subsequent NDP and VHT Compressed Beamforming frame response plus two SIFS intervals. And for a Beamforming Report Poll frame, the Duration/ID field is set to the estimated time required to transmit the VHT Compressed Beamforming frame response plus one SIFS interval. This may create more collision since such Duration setting can not cover the following VHT data frame. When the transmission is started with RTS/CTS frame, VHT beamforming frames are not considered.

Proposed Resolution Text:

8.2.5.2 Setting for single and multiple protection under enhanced distributed channel access (EDCA)

a) Single protection settings.

Change sub-bullet 1) and 2) as following:

1) For an RTS that is not part of a dual clear-to-send (CTS) exchange, the Duration/ID field is set to the estimated time, in microseconds, required to transmit the pending frame, plus one CTS frame, plus one ACK or BlockAck frame if required, plus any NDPA and NDPs required, plus any Beamform Report Poll if required, plus explicit feedback if required, plus applicable IFS durations.

2) For all CTS frames sent by STAs as the first frame in the exchange under EDCA and with the receiver address (RA) matching the MAC address of the transmitting STA, the Duration/ID field is set to one of the following:

i) If there is a response frame, the estimated time required to transmit the pending frame, plus one SIFS interval, plus the response frame (ACK or BlockAck), plus any NDPA and NDPs required, plus any Beamform Report Poll if required, plus explicit feedback if required,(#3039) plus an additional SIFS interval

ii) If there is no response frame, the time required to transmit the pending frame, plus one SIFS interval

Add the following sub-bullets:

7) For an NDPA frame, the Duration/ID field is set to the estimated time, in microseconds, required to transmit the pending frame, plus one ACK or BlockAck frame if required, plus any NDPs required, plus any Beamform Report Poll if required, plus explicit feedback if required, plus applicable IFS durations.

9.19.2.2 EDCA TXOPs

change bullet e) in P80 as following:

e) Any frames required for beamforming as specified in 9.26 (Sounding PPDUs) and 9,30.5 (VHT Sounding Protocol)

# Text boxes

Abstract

This document provides resolution for the following CIDs on TGac D1.0:

CID 2157, 2158