IEEE P802.11
Wireless LANs

| LB171 D1.02 comment resolution (MAC CSM frame format) |
| --- |
| Date: 2011-07-09 |
| Author(s): |
| Name | Company | Address | Phone | email |
| Zhou Lan | NICT | 3-4,Hikarino-oka, Yokosuka, 239-0847, Japan | +81-46-847-5097 | lan@nict.go.jp |
| Chen Sun | NICT |  |  |  |
| Yohannes Alemseged | NICT |  |  |  |
| Hiroshi Harada | NICT |  |  |  |

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor:  Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.   As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

Submission Note: Notes to the reader of this submission are not part of the motion to adopt.  These notes are there to clarify or provide context.

# MAC CSM related comments

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 187 | 33.54 | 8.4.2.af4 | "... Any secured container ..." not specific enough. | Name the alternatives (apart from the public action frame) to transfer the Channel Schedule Management element |
| 339 | 33.54 | 8.4.2.af4 | Please define secured container and how it operates. | As per comment. |
| 413 | 33.54 | 8.4.2.af4 | Is "any secured container" defined? | Does this simply mean "encrypted"? What else is a "secured container"? |
| 562 | 33.54 | 8.4.2.af4 | should explicitly describe secured containers in this section. Too ambiguous | explain all secured contains. |
| 596 | 33.54 | 8.4.2.af4 | "Channel Schedule Management element is transmitted in the public action frame or any secured container to indicate the channel scheduel change." What is "any secured container"? | Clarify or remove "any secured contatiner". |
| 669 | 33.54 | 8.4.2.af4 | description of any secured container should be provided. | clarify or remove any secured container |
| 760 | 33.54 | 8.4.2.af4 | what is a "secured container"? | clarify |
| 887 | 33.54 | 8.4.2.af4 | "Channel Schedule Management element is transmitted in the public action frame or any secured container to indicate the channel scheduel change." What is "any secured container"? | Clarify or remove "any secured contatiner". |

Discussions:

According to the FCC rules, all the channel availability and schedule information should be delivered in a secured manner. The current draft only specifies two methods to deliver the channel schedule information. One is a public action frame used by GAS protocol, the other is a regular public action frame. Both of them have the protected dual of action frame, which can be used after security negation is set up between the stations. The term “secured container” here particularly refers to the “protected dual of action frame”. Propose to change the term to “protected dual of action frame”.

Propose: Revised to CIDs 187, 413, 596, 669, 760 and 887,  per discussion and editing instructions in document 802.11-11/0943r0.

Propose: Rejected to CIDs 339 and 562 per discussion in 11-11/943r0. The term “secured container” here particularly refers to the “protected dual of action frame”. Propose to change the term to “protected dual of action frame”.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 247 | 33.55 | 8.4.2.af4 | Please explain here what "channel schedule change" represents. | As in comment. |

Discussions:

Channel schedule change means channel schedule information. It is not only the updated information of channel schedule. Propose to change to “channel schedule information” for clarification.

Propose: Revised to CID 247, per discussion and editing instructions in document 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 287 | 34.21 | 8.4.2.af4 | wrong preposition | change "of generating" to "for transmitting" change "for a query" to "within a query" - but you also need to specify what sort of query and I do not know that now. |

Discussions:

As commented, the wording needs improvement. Propose to change the sentence to “ for  transmitting a query request for channel schedule information”.

Propose: Revised to CID 287, per discussion and editing instructions in document 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 176 | 36.20 | 8.4.2.af4 | Description of Channel Schedule Descriptor info field missing. | Add a description of the Channel Schedule Description field. Note in this description that the minimal length of the field is 1 octett. Also change the minimal value of the length of the IE in Table 8-51 to "6" |
| 825 | 36.20 | 8.4.2.af4 | Missing description of Channel Schedule Descriptor field. | Add description of Channel Schedule Descriptor field after description of Device Identification Info field. |
| 1076 | 34.06 | 8.4.2.af4 | Try as I might, I found nothing that told me the format of the Channel Schedule description. OK, there were statements of what was in the descriptor, and (curiously) what was not in it, but no structure. | Define the structure and semantics of the Channel Schedule Descriptor field. |

Discussions:

The Channel Schedule Descriptor info field is defined in section 8.2.6.1.4. The reference should be provided in this sub clause. Propose to add section number of Channel Schedule Description as reference.

Propose: Revised to CIDs 176, 825, 1076, per discussion and editing instructions in document 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 188 | 34.29 | 8.4.2.af4 | Table 8-42af41: usage of result codes 10 -- 255 left open | make result codes 10 -- 255 reserved. Possibly assign a few result codes for vendor specific usage. |
| 744 | 34.26 | 8.4.2.af4 | "Table 8-42af41—Reason Result Code field values" Are values 10-255 reserved? It's better to add a row in this table indicating values 10-255 reserved | Add a row indicating values 10-255 reserved at the end of Table 8-42af41—Reason Result Code field values |
| 964 | 34.26 | 8.4.2.af4 | "Table 8-42af41—Reason Result Code field values" Are values 10-255 reserved? It's better to add a row in this table indicating values 10-255 reserved | Add a row indicating values 10-255 reserved at the end of Table 8-42af41—Reason Result Code field values |
| 709 | 34.62 | 8.4.2.af4 | There is no generic failure reason code and there are no reserved reason result codes in Table 8-42af41 | Define "10 Request declined for unknown reason", "11-255 Reserved" |

Propose: Accepted to CIDs 188, 744, 964, 709 without discussion, per editing instructions in document 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 248 | 35.12 | 8.4.2.af4 | "..channel availability is based on TV channel or WLAN channel." It is not clear here what it means to be based on the "TV channel" and what it means to be based on the "WLAN channel". Are available WLAN channels a subset of available TV channels? How is this decided whether to provide one set of channels or the other one? | As in comment. |

Discussions:

According to the current TGaf draft, all the channel availability and schedule information are provided by RLSS instead of directly from GDB. A RLSS has the function of mapping the channel availability and schedule information from TV channel to WLAN channel. Also RLSS is provided by operator, not regulator, therefore it is up to the operator to decide to provide the whole set of WLAN channel schedule information or only a set of channel schedule information based on the situation of operation, traffic load, interference etc.

Propose: Rejected to CID 248, per discussion in document 802.11-11/0943r0, No modification is needed to the draft text.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 530 | 35.00 | 8.4.2.af4 | What's the difference between Channel Availability Starting Time and the time that the channel is available? | Clarify. |
| 537 | 35.00 | 8.4.2.af4 | what is the difference between Channel Availability Starting Time and the time that the channel becomes available? | Clarify. |
| 606 | 35.00 | 8.4.2.af4 | what is the difference between Channel Availability Starting Time and the time that the channel becomes available? | Clarify. |
| 897 | 35.00 | 8.4.2.af4 | what is the difference between Channel Availability Starting Time and the time that the channel becomes available? | Clarify. |

Discussions:

"Channel Availability Starting Time" is the name of the field, and the content is the instant time that the channel becomes available. In order to avoid confusion, propose to change "Channel Availability Starting Time" to "Channel Availability Starting Time field".

Propose: Revised to CIDs 530, 537, 606 and 897, per discussion and editing instructions in document 802.11-11/0943r0. Replace “Channel Availability Starting Time” by “Channel Availability Starting Time field”.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 532 | 41.41 | 8.4.5.5 | According to current text in 10.af2, enabling STA queries RLS using RLQP | database -> RLS |
| 593 | 41.41 | 8.4.5.5 | According to current text in 10.af2, enabling STA queries RLS using RLQP | database -> RLS |
| 558 | 41.41 | 8.4.5.5 | enabling STA should query RLS, not database using RLQP. Conflicting description with 10.af2. | Fix |
| 608 | 41.41 | 8.4.5.5 | According to 10.af2, enabling STA queries RLS using RLQP | database -> RLS |
| 899 | 41.41 | 8.4.5.5 | According to 10.af2, enabling STA queries RLS using RLQP | database -> RLS |

Discussions:

CSM is confined between RLSS and mode II/fixed device or mode II/fixed device and mode II/fixed device. The query of a CSM should be sent only to RLSS or another enabling STA. Therefore, “database” should be changed to “RLSS or another enabling STA”. Propose to change “database ” to “RLSS or another enabling STA”.

Propose: Revised to CIDs 532, 593, 558, 608 and 899, per discussion and editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 490 | 34.00 | 8.4.2.af4 | The purpose of reason result code 1 is not clear. If a STA changes its location, it should obtain the new channel list first and then the new schedule information applicable for that new list. How the updated schedule is going to be useful? Too many reason result codes for "request declined", are these necessary? For example, why it is has to be separate code if the request is declined by an Enabling STA or by the RLS? | Clarify |
| 598 | 34.00 | 8.4.2.af4 | Reason Result Code differentiates that the channel schedule information is new or updated one. What are differences of new channel schedule information and updated channel schedule information? The update may mean addtion/deletion of the channel lit or schedule time change within the existing available channel list. It is not possible to differentiate these options. | Remove the options of new channel schedule information and updated channel schedule information. |
| 889 | 34.00 | 8.4.2.af4 | Reason Result Code differentiates that the channel schedule information is new or updated one. What are differences of new channel schedule information and updated channel schedule information? The update may mean addtion/deletion of the channel lit or schedule time change within the existing available channel list. It is not possible to differentiate these options. | Remove the options of new channel schedule information and updated channel schedule information. |

Discussions:

As commented, when STA changes its position, it needs to obtain the channel availability and schedule information on that new position. The reason result code 1 can be deleted. However it is needed to distinguish between the request to RLSS and enabling STA, because if the request is somehow failed on a RLSS, the STA may want to try an enabling STA that is controlled by another RLSS instead. Propose to keep reason/result code of 1 and change the meaning to a request to an enabling STA.

Propose: Revised to CIDs 490, 598 and 889, per discussion and editing instructions in document 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 491 | 35.00 | 8.4.2.af4 | The channel schedule management frame has too many modes, which may be unnecessary. For example, it is not clear why channel schedule management requires mode 0 or 1, if this mode is only meant to request the channel list (reason result code 0 or 1) without any schedule information. Why mode 4 with TV channel needs operating class? Furthermore, the channel schedule management with TV channel list can be easily incorporated with channel availability query procedure. | Clarify. Also, suggest to merge the request/response with TV channel list (modes 0, 2 and 4) to the channel availability query frame. The description of remaining modes can be simplified. For example, in all schedule information using WLAN channel, operating class field has to be included any way. |

Discussion:

Mode 0 and 1 has nothing to do with requesting a channel list. They are used to distinguish whether the request is for schedule information on TV channel or WLAN channel. Because TV channel doesn’t need operating class, it is needed to indicate whether the operating class field is present or not by using the mode field.

Propose: Rejected to CID 491, per discussions in document 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 540 | 36.18 | 8.4.2.af4 | Device identification info is of requesting STA. is it sufficient for a STA to obtain the channel schedule, for example, when enabling STA transtmits a request to another enabling STA? | Clarify. |
| 609 | 36.18 | 8.4.2.af4 | Device identification info is of requesting STA. is it sufficient for a STA to obtain the channel schedule, for example, when enabling STA transtmits a request to another enabling STA? | Clarify. |
| 900 | 36.18 | 8.4.2.af4 | Device identification info is of requesting STA. is it sufficient for a STA to obtain the channel schedule, for example, when enabling STA transtmits a request to another enabling STA? | Clarify. |

Discussions:

According to the FCC rules, a device must provide ID and location information only to obtain available channel list. Requesting schedule information without providing location info doesn’t violate the rule. It is specified in the draft that CAQ must be performed before CSM, and the position of a STA should not be changed  before CSM is performed. Propose to make no change to the draft text.

Propose: Rejected to CIDs 540, 609 and 900, per discussion in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 597 | 33.04 | 8.4.2.af4 | In the Channel Schedule Management element format, which fields are repeated, Device Identification Info and Channel Schedule Descriptor fields or only Channel Schedule Descriptor field? Only Channel Schedule Descriptor field needs to be repeated. | Clarify. |
| 888 | 33.04 | 8.4.2.af4 | In the Channel Schedule Management element format, which fields are repeated, Device Identification Info and Channel Schedule Descriptor fields or only Channel Schedule Descriptor field? Only Channel Schedule Descriptor field needs to be repeated. | Clarify. |
| 722 | 41.47 | 8.4.5.5 | Can the repeated number of variable fields in Figure 8-45af4 be parsed. Is it assumed that these variable field lengths are constant when a STA uses the same regulatory domain database? If a STA changes regulatory domains, how does it know the new field lengths? | Check that these fields can be parsed. |
| 1018 | 41.48 | 8.4.5.5 | It is not clear from the figure which fields are repeated. It is also not clear how the element is parsed given two variable length fields. | Clarify |

Discussions:

The Device Identification Info field is fixed size. Only the Channel Schedule Descriptor field is repeated. Propose to change Figure 80402p in a way to show the above two points.

Propose: Revised to CIDs 597, 888, 722 and 1018, per discussion and editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 599 | 34.42 | 8.4.2.af4 | Channel Schedule Management frame can deliver the schedule information of a channel which are not available when it is requested. Reason Result Code 3 indicates the success of "full channel schedule information" delivering. Then, this full channel means all of the TVWS channels regardless of the availablity at the point of being requested? It is not realistic to transfer all of the channel schedule information. | Clarify. |
| 890 | 34.42 | 8.4.2.af4 | Channel Schedule Management frame can deliver the schedule information of a channel which are not available when it is requested. Reason Result Code 3 indicates the success of "full channel schedule information" delivering. Then, this full channel means all of the TVWS channels regardless of the availablity at the point of being requested? It is not realistic to transfer all of the channel schedule information. | Clarify. |

Discussions:

As pointed out by the commenter, the full schedule information means all the available slots on the requested channel regardless the availability at the point of being requested. In order to indicate the updated schedule information on the requested channels, two cases should be separated, there are new slots added to the requested channels or there are some slots that are not available which should be deleted from the list. The results codes of these two cases should be given in the table. Propose to change Table 8-182h to indicate these two cases.

Propose: Revised to CIDs 599 and 890, per discussion and editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 761 | 34.53 | 8.4.2.af4 | what is "None WLAN information capability"? | Define |

Discussions:

It means that the RLSS or the enabling STA is not capable of providing schedule information based on WLAN channel. Propose to change to "no capability for providing schedule information on WLAN channel" for clarification.

Propose: Revised to CID 761, per discussion and editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 829 | 34.12 | 8.4.2.af4 | Are Device Identification Info and Channel Schedule Descriptor always present, even if the request is declined? | Clarify. |

Discussions:

Channel Schedule Descriptor provides the reason why the request is declined. It has to be present even if the request is declined. Propose to make no changes to the draft text.

Propose:  Rejected to CID 829, per discussion in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1019 | 41.65 | 8.4.5.5 | It does not make sense to descrive the 'value as variable' | Remove ", and the value is variable" |

Propose: Accepted to comment CID 1019 without discussion, per editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1077 | 35.56 | 8.4.2.af4 | "The optional Operating Class field is present in the Channel Schedule Descriptor" - if it's optional, how come the statement that it's present? | Remove "optional". Check and correct similar uses in this table. |
| 1232 | 35.00 | 8.4.2.af4 | Table 8-42af42: Operating Class field is not optional |  |

Propose: Accepted to CIDs 1077 and 1232 without discussion, per editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 710 | 34.06 | 8.4.2.af4 | Is the "Device Identification Info" field in Figure 8-42af6 the same as the "Device Identification Information" field in Figure 8-45af2? | Please use one consistent field name, or if these different fields different names. |

Propose: Accepted to CID 710 without discussion, per editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 1230 | 35.28 | 8.4.2.af4 | Inconsistent description of Channel Number | only 1 field |

Propose: Accepted to CID 1230 without discussion, per editing instructions in 802.11-11/0943r0.

| CID | Page | Clause | Comment | Proposed Change |
| --- | --- | --- | --- | --- |
| 175 | 36.18 | 8.4.2.af4 | Specify the minimal length of the device identification information field (=1). Same applies to the min. length of the channel schedule description. Otherwise, it is not clear, that each information field should be aligned to octett boundaries. This impacts the min. length of the channel schedule management information element (per Table 8-51) which is not correct even for the text as it is. | Insert "The minimal length of the Device Identification Info field is one octett" after "...schedule information." (line 20, page 36). Also change the minimal value of the length of the IE in Table 8-51 to "6" |
| 828 | 27.40 | 8.4.2.1 | length of Channel Schedule Management is incorrect. | Max length should be 257. Min length should be 4 + minimum device identification info length + minimum channel schedule descriptor length. |
| 1055 | 27.40 | 8.4.2.1 | Where does the Length limit of 255 come from? | Justify it or change to 257 |

Discussions:

The maximum length should be 257 and the minimum length should be 4. Propose to change Table 8-54 in this way.

Propose: Accepted to CIDs 175, 828 and 1055, per discussion and editing instructions in 802.11-11/0943r0.

## Editing instructions:

8.4 Management frame body components

8.4.2 Information elements

8.4.2.1 General

TGaf Editor: change Table 8-54as follows:

Table 8-54—Element IDs

| Element | Element ID | Length of indicated element (in octets) | Extensible |
| --- | --- | --- | --- |
| White Space Map (see 8.4.2.106 (White Space Map element)) | <ANA> | 3 to 255 | Yes |
| DSE Link Identifier (see 8.4.2.107 (DSE Link Identifier element)) | <ANA> | 8 or 14 | Yes |
| Channel Power Management Announcement (see 8.4.2.108 (Channel Power Management Announcement element)) | <ANA> | 3 to 257 |
| Channel Schedule Management (see 8.4.2.109 (Channel Schedule Management element)) | <ANA> | 4 to 255257 |
| Geodatabase Inband Enabling Signal (see 8.4.2.110 (Geodatabase Inband Enabling Signal element)) | <ANA> | 2 |
| Contact Verification Signal (see 8.4.2.111 (Contact Verification Signal element)) | <ANA> | 3 | Yes |

8.4.2.132 Channel Schedule Management element

TGaf Editor: Change the first paragraph of  8.4.2.132 as follows:

The Channel Schedule Management element is transmitted in the public action frame or any secured container a public action frame or a protected dual of public action frame to indicate the channel schedule change information.

TGaf Editor: Change Figure 8-402p of  8.4.2.132 as follows:

|  |  |  |  |  |  | Channel Schedule Descriptor field is These fields are repeated, as determined by the Length field. |
| --- | --- | --- | --- | --- | --- | --- |
|  | Element ID | Length | Reason Result Code | Channel Schedule Management Mode | Device Identification Information | Channel Schedule Descriptor |
| Octets: | 1 | 1 | 1 | 1 | variable 18 | Variable |

Figure 8-402p – Channel Schedule Management element format

TGaf Editor: Change the third paragraph of  8.4.2.132 as follows:

The Reason Result Code field indicates the reason for generating the Channel Schedule Management for a query request for transmitting a query request for channel schedule information. It also indicates the result of a response, whether the query is successful or not, and the reason if it is not successful. The value of this field is defined in Table 8-192 (Reason Result Code field values).

TGaf Editor: Change the last paragraph of  8.4.2.132 as follows:

The Device Identification Information field indicates the regulatory identification of the STA that is requesting the schedule information. The value of the field is defined in 8.2.6.1.2 (Device Identification Information).

TGaf Editor: after the last paragraph of  8.4.2.132, insert the following paragraph:

The Channel Schedule Descriptor field indicates the channels for which the schedule information is requested, and the channel schedule information is provided in the response. The value of the field is defined in 8.2.6.1.4 (Channel Schedule Descriptor).

TGaf Editor: change Table 8-182h as follows:

Table 8-182h—Reason Result Code field values

| Reason result code field values | Description |
| --- | --- |
| 0 | Request for a new channel schedule information from a Registered Location Secure Server. It happens the first time STAs try to obtain channel schedule information from Registered Location Secure Server. |
| 1 | Request for an updated channel schedule information from an enabling STA. Registered Location Secure Server. It happens when the STAs change locations and have to re-contact the Registered Location Secure Server for updated channel schedule information. |
| 2 | Success with full channel schedule information on the requested channels obtained. |
| 3 | Success with only schedule changes additional timeslots added on the requested channels obtained. |
| 4 | Success with timeslots deleted from the list of last query on the requested channels. |
| 45 | Success with no channel schedule changes from last query of the Registered Location Secure Server. |
| 56 | Request declined by the enabling STA for unspecified reason. |
| 67 | Request declined by the enabling STA because of None WLAN information capability no capability for providing schedule information on WLAN channel. |
| 78 | Request declined by Registered Location Secure Server for unspecified reason. |
| 89 | Request declined by Registered Location Secure Server because of None WLAN information capability no capability for providing schedule information on WLAN channel.. |
| 910 | Timeout. |
| 1011-255 | Reserved. |

TGaf Editor: change Table 8-182i as follows:

Table 8-182i—Channel Schedule Management Mode values

| Channel schedule management mode value | Operating class present | Description |
| --- | --- | --- |
| 0 | No | The Channel schedule information is based on the TV channel. The Reason and Result Code field is set to either zero or one. |
| 1 | Yes | The Channel Schedule information is based on the WLAN channel. The Reason and Result Code field is set to either zero or one. |
| 2 | No | The Channel Schedule information provided is based on the TV channel. Channel Availability Starting Time field is present in the Channel Schedule Descriptor and the time that the channel becomes available is provided. |
| 3 | Yes | The channel Schedule information provided is based on the WLAN channel. The Channel Availability Starting Time field is present in the Channel Schedule Descriptor and the time that the channel becomes available is present. |
| 4 | Yes | The Channel Schedule information provided is based on the TV channel. The Channel Availability Starting Time field is NOT present in the Channel Schedule Descriptor. |
| 5 | Yes | The channel Schedule information provided is based on the WLAN channel. The Channel Availability Starting Time field is NOT present in the Channel Schedule Descriptor. |
| 6-255 | Reserved. |

8.4.5.6 RLQP Channel Schedule Management element

TGaf Editor: change the first paragraph of 8.4.5.6 as follows:

The RLQP Channel Schedule Management element is used by an enabling STA to query the database RLSS or another enabling STA for channel schedule information.

TGaf Editor: change the third paragraph of 8.4.5.6 as follows:

The Length field indicates the length of the remaining element fields in octets, and the value is variable.

# Comments

8.4.5.6 RLQP CSM does not have protected dual, this statement is not correct.

# Text boxes

Abstract

This document contains proposed resolution of some of the comments categorized as MAC CSM in LB171 of P802.11af D1.0, shown in 802.11-11/0277r12. Proposed resolutions are based on 802.11af  draft text D1.02.

This submission provides resolutions for comment CID 187, 339, 413, 562, 596, 669 , 760, 887, 247, 287, 176, 825, 1076, 188, 744, 964, 709, 248, 530, 537, 606, 897, 532, 593, 558, 608, 899, 490, 598, 889, 491, 540, 609, 900, 597, 888, 722, 1018, 599, 890, 761, 829, 1019, 1077, 1232, 710, 1230, 175, 828, 1055.