## Slide 1: Group Addressed MSDUs in 802.11ac
Date: 2011-07-12
Authors:

## Slide 2: Abstract
The presentation provides means to improve the group addressed MSDUs transmission efficiency, and to reduce power consumption of the STAs.
The presentation solves the following CIDs: 2614, 2631, 2740, 3704, 2615, 2632, 3702, and 3705.
The group addressed frames transmission efficiency is improved:
  RTS CTS prior group addressed frames transmission
  TXOP of group addressed frames
  The power consumption of group addressed frames reception is reduced:
  The TA and (RA or frame type) indication in PLCP headers

## Slide 3: Recap, clause 9.3.6 group addressed MPDU transfer procedure
Clause 9.3.6 defines:“ In the absence of a PCF, when group addressed MPDUs in which the To DS field is 0 are transferred from a STA, only the basic access procedure shall be used. Regardless of the length of the frame, no RTS/CTS exchange shall be used.”
It is unclear what is basic access procedure
  Only one PPDU may be transmitted in a TXOP?
RTS CTS cannot be used prior group addressed MPDUs transmission
  The CCA sensing is only performed at the transmitter which may lead to transmission collisions and hidden node problems
  The larger transmission bandwidth makes collisions of the transmissions even more likely

## Slide 4: RTS CTS for Group Addressed
Enable RTS CTS signaling prior group addressed frames transmission
  RTS is addressed to an individual address of a STA in BSS
  The STA responds with CTS frame
  Group addressed frames are transmitted
The level of RTS CTS protection for group addressed frames is similar to protection level of MU MIMO transmissions
  In both cases data is transmitted to multiple devices and RTS CTS exchange is done with a single STA

## Slide 5: RTS CTS for group addressed frames
Both the RTS transmitter and CTS transmitter perform virtual carrier sensing in primary channel and CCA sensing in non-primary channels
  RTS CTS avoids collisions with ongoing transmissions
  RTS CTS is the only mechanism to avoid OBSS problems
  RTS CTS distributes NAV to non-primary channels to ensure the protection for the transmission

## Slide 6: TXOP for Group Addressed Frames
The TXOP enables transmission of multiple MPDUs with the same contention
  Reduced amount of contentions improve transmission efficiency
  NAV protection avoids transmission collisions
  The same mechanism (TXOP) is used for group addressed and individually addressed MPDUs
The group addressed frames should be transmitted to all receivers, i.e. transmission rate is typically low
  The aggregated MPDU may require very long transmission time

## Slide 7: Recap, Address Indication in PLCP Header
802.11ac PLCP header indicates:
  Individually addressed PPDU to single user (SU)
    The partial AID defines the BSSID and AID of the receiver
  Individually addressed aggregated PPDU (A-PPDU) to multiple users (MU)
    The Group ID defines the receivers
  Group addressed PPDU
    The partial AID set to 0 indicates group address MPDU transmission in any BSS
  The partial AID set to 0 indicates frame transmission in a IBSS
  The same partial AID value 0 should not be used for multiple frame type transmissions

## Slide 8: Challenges of the Address Indication in PLCP Header
Currently PLCP header has partial AID set to 0 for group addressed frames
  The same value is used for all frames transmission in IBSS
STAs cannot detect from PLCP header:
  Transmitter Address (BSSID)
  Is the PPDU transmitted in IBSS or is it group addressed frame transmitted in a BSS
The current format forces STAs to receive all group addressed PPDUs
  Device cannot filter frames from other BSSIDs

## Slide 9: Partial AID
All frames, individually and group addressed frames, use the same rule to generate the partial AID
Partial AID for group address is generated:
  AID = 0 (AID value 0 indicates group addressed frame)
  BSSID = BSSID
This enables to detect TA and that frame type is group addressed frame
  The power consumption of the devices is improved, because the STA filters unnecessary transmissions from other BSSs and IBSS
  No need to reserve new bit combinations

## Slide 10: Summary
The efficiency of the group addressed frames transmission is simple to improve in VHT BSSs
  The individually and group addressed MPDUs should have the same capabilities for frames transmission and reception