## Slide 1: S1G Spectrum Regulations in China
Date: 2011-07-18
Authors:
Slide 1

## Slide 2: Outline
Several S1G spectrum are available in China with different equipment regulation requirements.
Information on available spectrum and regulations in China are provided for 802.11ah discussion.
Slide 2

## Slide 3: Regulation in China
The mandate of “Micro-power (short range) technical requirements for wireless equipment ” is issued in Sept. 5, 2005 by Radio Administration Bureau of Ministry of Information Industry of China, and carried out in Oct. 1, 2005. [1] [2]
14 types of equipments and corresponding regulations are defined in the mandation, in which 12 types of equipments work on S1G spectrum.

## Slide 4: Equipment Categories and Regulations
 | Equipment Category | Spectrum / Max Tx Power/ Channel BW
1. | General Micro-power (short range) radio transmission equipment | 1-40MHz / 5mW
2. | General Wireless Remote Control Device (no interferece to broadcast and TV) | 470-566MHz ,614-787MHz / 5mW / 1MHz
3. | Wireless microphone, wirless civilian measureing equipment (no interferece to broadcast and TV) | (1)87-108 MHz / 3mW (2) 75.4-76 .0 MHz ,84-87MHz / 10 mW (3) 189.9-223 MHz / 10mW (4) 470-510MHz ,630-787MHz /50 mW / 200kHz
4. | Biomedical telemetry devices | 174-216MHz ,407-425MHz ,608-630MHz / 10mW
5. | Analog cordless telephone | 45-48.75MHz
6. | cranes or machinery for the wireless remote control devices to send | around 230 MHz 12 channel / 20mW /16kHz

## Slide 5: Cont.
 | Equipment Category | Spectrum / Max Tx Power/ Channel BW
7. | industrial wireless remote control device | around 419 MHz / 20mW /16kHz
8. | wireless data transmission equipment | around 228 MHz / 10mW /16kHz
9. | Electronic Hanging wireless transmission equipment | about 223 MHz / 50mW /50kHz about 450 MHz / 50mW /20kHz
10. | Wireless remote control in civilian equipment (excluding toys) | 314－316MHz，430-432MHz，433.00-434.79MHz/ 10mW/ 200kHz 779-787MHz /10 mw
11. | Wireless romete control for model and toys | about 26, 40, 72MHz / 750mW / 8 or 20kHz
12. | wireless intercom | about 409MHz/ 500mW / 12.5kHz

## Slide 6: General Spurious Radiation Limitations
Tx max power state
Tx idle state
Frequency Range | Test bandwidth | Limitation
30MHz～1GHz | 100kHz(3dB) | -36dBm
Frequency Range | Test bandwidth | Limitation
30MHz～1GHz | 100kHz(3dB) | -47dBm

## Slide 7: Major Frequency and Use Case Discussion
Frequency Band (MHz) | Max Tx Power (mW) | Channel BW | Possible 802.11ah use case Categories suited
314-316, 430-432, 433.00-434.79 | 10 | 200 kHz | 1
470-510 , 630-787 | 50 | 200KHz | 1, 3
470-566 ,614-787 | 5 | 1MHz | 1, 2
779-787 | 10 |  | 1, 2
802.11ah use case Categories in [3] :
  use case 1: Sensors and meters
  use case 2: Backhaul Sensor and use
  use case 3: Extended range Wi-Fi

## Slide 8: Conclusions
Each frequency band is suitable for 1-2 typical use case of 802.11ah.
Lots of spectrum resource is available in 470-566 MHz and 614-787 MHz in which regulations require no interefence to wireless broast and TV services. Usage of wireless broast and TV in this band in China need to be verified .
Max Tx power is about tens of mW for short distance usage, coverage of 802.11ah should be considered in system design.
Slide 9

## Slide 9: References
[1]http://www.miit.gov.cn/n11293472/n11295310/n11297428/11637344.html
[2] http://www.srrccn.org/srrc-approval-new2.htm
[3] 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document.pptx
Slide 10