## Slide 1: S1G Spectrum Regulations in China
Date: 2011-07-18
Authors:
Slide 1

## Slide 2: Outline
Several S1G spectrum are available in China with different equipment regulation requirements.
Information on available spectrum and regulations in China are provided for 802.11ah discussion.
Slide 2

## Slide 3: Regulation in China
The mandate of “Micro-power (short range) technical requirements for wireless equipment ” is issued in Sept. 5, 2005 by Radio Administration Bureau of Ministry of Information Industry of China, and carried out in Oct. 1, 2005. [1] [2]
14 types of equipments and corresponding regulations are defined in the mandation, in which 12 types of equipments work on S1G spectrum.

## Slide 4: Equipment Categories and Regulations (1)
 | Equipment Category | Spectrum / Max Tx Power/ Channel BW
1. | General Micro-power (short range) radio transmission equipment | 1-40MHz / 5mW
2. | General Wireless Remote Control Device (no interferece to broadcast and TV) | 470-566MHz ,614-787MHz / 5mW / 1MHz
3. | Wireless microphone, wirless civilian measureing equipment (no interferece to broadcast and TV) | (1)87-108 MHz / 3mW (2) 75.4-76 .0 MHz ,84-87MHz / 10 mW (3) 189.9-223 MHz / 10mW (4) 470-510MHz ,630-787MHz /50 mW / 200kHz
4. | Biomedical telemetry devices | 174-216MHz ,407-425MHz ,608-630MHz / 10mW
5. | Analog cordless telephone | 45-48.75MHz
6. | cranes or machinery for the wireless remote control devices to send | around 230 MHz 12 channel / 20mW /16kHz

## Slide 5: Equipment Categories and Regulations (2)
 | Equipment Category | Spectrum / Max Tx Power/ Channel BW
7. | industrial wireless remote control device | around 419 MHz / 20mW /16kHz
8. | wireless data transmission equipment | around 228 MHz / 10mW /16kHz
9. | Electronic Hanging wireless transmission equipment | about 223 MHz / 50mW /50kHz about 450 MHz / 50mW /20kHz
10. | Wireless remote control in civilian equipment (excluding toys) | 314－316MHz，430-432MHz，433.00-434.79MHz/ 10mW/ 200kHz 779-787MHz /10 mw
11. | Wireless romete control for model and toys | about 26, 40, 72MHz / 750mW / 8 or 20kHz
12. | wireless intercom | about 409MHz/ 500mW / 12.5kHz

## Slide 6: General Spurious Radiation Limitations
Tx max power state
Tx idle state
Frequency Range | Test bandwidth | Limitation
30MHz～1GHz | 100kHz(3dB) | -36dBm
Frequency Range | Test bandwidth | Limitation
30MHz～1GHz | 100kHz(3dB) | -47dBm

## Slide 7: TV & Broadcast Band in China (1)
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅰ | 1 | 48.5-56.5 | 52.5
 | 2 | 56.5-64.5 | 60.5
 | 3 | 64.5-72.5 | 68.5
 | 4 | 76-84 | 80
 | 5 | 84-92 | 88
Ⅱ | (87-108) for FM broadcast |  | 
A | z1 | 111.0-119.0 | 115
 | z2 | 119.0-127.0 | 123
 | z3 | 127.0-135.0 | 131
 | z4 | 135.0-143.0 | 139
 | z5 | 143.0-151.0 | 147
 | z6 | 151.0-159.0 | 155
 | z7 | 159.0-167.0 | 164
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅲ | 6 | 167-175 | 171
 | 7 | 175-183 | 179
 | 8 | 183-191 | 187
 | 9 | 191-199 | 195
 | 10 | 199-207 | 203
 | 11 | 207-215 | 221
 | 12 | 215-223 | 219
B | z8 | 223.0-231.0 | 227
 | z9 | 231.0-239.0 | 235
 | z10 | 239.0-247.0 | 243
 | z11 | 247.0-255.0 | 251
 | z12 | 255.0-263.0 | 259
 | z13 | 263-271.0 | 267
 | z14 | 271.1-279.0 | 275
 | z15 | 279.0-287.0 | 283
 | z16 | 287.0-295.0 | 291

## Slide 8: TV & Broadcast Band in China (2)
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅳ | 13 | 470-478 | 474
 | 14 | 478-486 | 482
 | 15 | 486-494 | 491
 | 16 | 492-5.2 | 498
 | 17 | 502-510 | 506
 | 18 | 510-518 | 514
 | 19 | 518-526 | 522
 | 20 | 526-534 | 530
 | 21 | 534-542 | 538
 | 22 | 542-550 | 546
 | 23 | 550-558 | 554
 | 24 | 558-566 | 562

## Slide 9: TV & Broadcast Band in China (3)
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz) | CH No. | Frequency Range (MHz) | Center Frequecy (MHz) | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅴ ` | 25 | 606-614 | 610 | 40 | 726-734 | 730 | 55 | 846-854 | 850
 | 26 | 614-622 | 618 | 41 | 734-742 | 738 | 56 | 854-862 | 858
 | 27 | 622-630 | 626 | 42 | 742-750 | 746 | 57 | 862-870 | 866
 | 28 | 630-638 | 634 | 43 | 750-758 | 754 | 58 | 870-878 | 874
 | 29 | 638-646 | 642 | 44 | 758-766 | 762 | 60 | 878-886 | 882
 | 30 | 646-654 | 650 | 45 | 766-774 | 770 | 61 | 886-894 | 890
 | 31 | 654-662 | 658 | 46 | 774-782 | 778 | 62 | 894-902 | 898
 | 32 | 662-670 | 666 | 47 | 782-790 | 786 | 63 | 902-910 | 906
 | 33 | 670-678 | 674 | 48 | 790-798 | 794 | 64 | 910-918 | 914
 | 34 | 678-686 | 682 | 49 | 798-806 | 802 | 65 | 918-926 | 922
 | 35 | 686-694 | 690 | 50 | 806-814 | 810 | 66 | 926-934 | 930
 | 36 | 694-702 | 698 | 51 | 814-822 | 818 | 67 | 934-942 | 938
 | 37 | 702-710 | 706 | 52 | 822-830 | 826 | 68 | 950-958 | 946
 | 38 | 710-718 | 714 | 53 | 830-838 | 834 |  |  | 
 | 39 | 718-726 | 722 | 54 | 838-846 | 842 |  |  | 

## Slide 10: Major Frequency Band and Use Case Discussion
Frequency Band (MHz) | Max Tx Power (mW) | Channel BW | Possible 802.11ah use Case Categories Suited
314-316, 430-432, 433.00-434.79 | 10 | 200 kHz | 1
470-510 , 630-787 | 50 | 200KHz | 1, 3
470-566 ,614-787 | 5 | 1MHz | 1, 2
779-787 | 10 |  | 1, 2
802.11ah use case categories in [3] :
  use case 1: Sensors and meters
  use case 2: Backhaul Sensor and use
  use case 3: Extended range Wi-Fi

## Slide 11: Conclusions
Each frequency band is suitable for 1-2 typical use case of 802.11ah.
Lots of spectrum resource is available in 470-566 MHz and 614-787 MHz in which regulations require no interefence to wireless broast and TV services. Usage of wireless broast and TV in this band in China need to be verified .
Max Tx power is about tens of mW for short distance usage, coverage of 802.11ah should be considered in system design.
Slide 9

## Slide 12: References
[1]http://www.miit.gov.cn/n11293472/n11295310/n11297428/11637344.html
[2] http://www.srrccn.org/srrc-approval-new2.htm
[3] 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document.pptx
Slide 10