## Slide 1: S1G Spectrum Regulations in China
Date: 2011-07-18
Authors:
Slide 1

## Slide 2: Outline
Several S1G spectrum are available in China with different equipment regulation requirements.
Information of available spectrum and regulations in China are provided for 802.11ah discussion.
Slide 2

## Slide 3: Regulation in China
The mandate of “Micro-power (short range) technical requirements for wireless equipment ” is issued in Sept. 5, 2005 by Radio Administration Bureau of Ministry of Information Industry of China, and carried out in Oct. 1, 2005. [1] [2]
14 types of equipments and corresponding regulations are defined in the mandate, in which 12 types of equipments work on S1G spectrum.

## Slide 4: Device Categories and Regulations (1)
 | Device Category | Spectrum / Max Tx Power/ Channel BW
1. | general micro-power (short range) radio transmission device (A-E) | 1-40MHz / 5mW
2. | general wireless remote control device (no interferece to broadcast and TV) | 470-566MHz ,614-787MHz / 5mW / 1MHz
3. | wireless microphone, wirless civilian measureing equipment (no interferece to broadcast and TV) | (1)87-108 MHz / 3mW (2) 75.4-76 .0 MHz ,84-87MHz / 10 mW (3) 189.9-223 MHz / 10mW (4) 470-510MHz (active Tx time < 5s) , 630-787MHz /50 mW / 200kHz
4. | biomedical telemetry devices (only in hospital and medical research organization) | 174-216MHz ,407-425MHz ,608-630MHz / 10mW
5. | analog cordless telephone | 45-48.75MHz
6. | wireless remote control devices dedecated to cranes or conveying machinery | 12 channels around 230 MHz / 20mW /16kHz

## Slide 5: Device Categories and Regulations (2)
 | Device Category | Spectrum / Max Tx Power/ Channel BW
7. | industrial wireless remote control device (only in factory buildings) | 13 channels around 419 MHz / 20mW /16kHz
8. | wireless data transmission device (only in buildings) | 14 channels around 228 MHz / 10mW /16kHz
9. | wireless data transmission device dedicated to electronic hanging balance | 5channels around 223 MHz / 50mW /50kHz 5channels around 450 MHz / 50mW /20kHz
10. | wireless remote control in civilian equipment (excluding toys) | 314-316MHz，430-432MHz，433.00-434.79MHz/ 10mW/ 200kHz 779-787MHz /10 mw
11. | wireless romete control for model and toys | around 26, 40, 72MHz / 750mW / 8 or 20kHz
12. | public walkie-talkie | 20channels around 409MHz/ 500mW / 12.5kHz

## Slide 6: General Spurious Radiation Limitations
Tx max power state
Tx idle state
Frequency Range | Test bandwidth | Limitation
30MHz～1GHz | 100kHz(3dB) | -36dBm
Frequency Range | Test bandwidth | Limitation
30MHz～1GHz | 100kHz(3dB) | -47dBm

## Slide 7: TV & Broadcast Band in China (1)
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅰ | 1 | 48.5-56.5 | 52.5
 | 2 | 56.5-64.5 | 60.5
 | 3 | 64.5-72.5 | 68.5
 | 4 | 76-84 | 80
 | 5 | 84-92 | 88
Ⅱ | (87-108) for FM broadcast |  | 
A | z1 | 111.0-119.0 | 115
 | z2 | 119.0-127.0 | 123
 | z3 | 127.0-135.0 | 131
 | z4 | 135.0-143.0 | 139
 | z5 | 143.0-151.0 | 147
 | z6 | 151.0-159.0 | 155
 | z7 | 159.0-167.0 | 164
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅲ | 6 | 167-175 | 171
 | 7 | 175-183 | 179
 | 8 | 183-191 | 187
 | 9 | 191-199 | 195
 | 10 | 199-207 | 203
 | 11 | 207-215 | 221
 | 12 | 215-223 | 219
B | z8 | 223.0-231.0 | 227
 | z9 | 231.0-239.0 | 235
 | z10 | 239.0-247.0 | 243
 | z11 | 247.0-255.0 | 251
 | z12 | 255.0-263.0 | 259
 | z13 | 263-271.0 | 267
 | z14 | 271.1-279.0 | 275
 | z15 | 279.0-287.0 | 283
 | z16 | 287.0-295.0 | 291

## Slide 8: TV & Broadcast Band in China (2)
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅳ | 13 | 470-478 | 474
 | 14 | 478-486 | 482
 | 15 | 486-494 | 491
 | 16 | 492-5.2 | 498
 | 17 | 502-510 | 506
 | 18 | 510-518 | 514
 | 19 | 518-526 | 522
 | 20 | 526-534 | 530
 | 21 | 534-542 | 538
 | 22 | 542-550 | 546
 | 23 | 550-558 | 554
 | 24 | 558-566 | 562

## Slide 9: TV & Broadcast Band in China (3)
Band | CH No. | Frequency Range (MHz) | Center Frequecy (MHz) | CH No. | Frequency Range (MHz) | Center Frequecy (MHz) | CH No. | Frequency Range (MHz) | Center Frequecy (MHz)
Ⅴ ` | 25 | 606-614 | 610 | 40 | 726-734 | 730 | 55 | 846-854 | 850
 | 26 | 614-622 | 618 | 41 | 734-742 | 738 | 56 | 854-862 | 858
 | 27 | 622-630 | 626 | 42 | 742-750 | 746 | 57 | 862-870 | 866
 | 28 | 630-638 | 634 | 43 | 750-758 | 754 | 58 | 870-878 | 874
 | 29 | 638-646 | 642 | 44 | 758-766 | 762 | 60 | 878-886 | 882
 | 30 | 646-654 | 650 | 45 | 766-774 | 770 | 61 | 886-894 | 890
 | 31 | 654-662 | 658 | 46 | 774-782 | 778 | 62 | 894-902 | 898
 | 32 | 662-670 | 666 | 47 | 782-790 | 786 | 63 | 902-910 | 906
 | 33 | 670-678 | 674 | 48 | 790-798 | 794 | 64 | 910-918 | 914
 | 34 | 678-686 | 682 | 49 | 798-806 | 802 | 65 | 918-926 | 922
 | 35 | 686-694 | 690 | 50 | 806-814 | 810 | 66 | 926-934 | 930
 | 36 | 694-702 | 698 | 51 | 814-822 | 818 | 67 | 934-942 | 938
 | 37 | 702-710 | 706 | 52 | 822-830 | 826 | 68 | 950-958 | 946
 | 38 | 710-718 | 714 | 53 | 830-838 | 834 |  |  | 
 | 39 | 718-726 | 722 | 54 | 838-846 | 842 |  |  | 

## Slide 10: Major Frequency Band and Use Case Discussion
Frequency Band (MHz) | Max Tx Power (mW) | Channel BW | Possible 802.11ah use Case Categories Suited
314-316, 430-432, 433.00-434.79 | 10 | 200 kHz | 1
470-510 , 630-787 | 50 | 200KHz | 1, 3
470-566 ,614-787 | 5 | 1MHz | 1, 2
779-787 | 10 |  | 1, 2
802.11ah use case categories in [3] :
  use case 1: Sensors and meters
  use case 2: Backhaul sensor and use
  use case 3: Extended range Wi-Fi

## Slide 11: Conclusions
Each frequency band is suitable for 1-2 typical use case of 802.11ah.
Lots of spectrum resource is available in 470-566 MHz and 614-787 MHz in which regulations require no interefence to wireless broast and TV services. Usage of wireless broast and TV in this band in China need to be verified.
Max Tx power is about tens of mW for short distance usage, coverage of 802.11ah should be considered in system design.
Slide 9

## Slide 12: References
[1]http://www.miit.gov.cn/n11293472/n11295310/n11297428/11637344.html
[2] http://www.srrccn.org/srrc-approval-new2.htm
[3] 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document.pptx
Slide 10