## Slide 1: Prohibiting Technology
Date: 2011-07-15
Authors:

## Slide 2: Abstract
Draft P802.11ac_1.0 forbids the use of TKIP and GCMP. This is problematic.

## Slide 3: IEEE Anti-Trust Policies
“Other kinds of violations can also arise in the standards process. For example, selecting one technology for inclusion in a standard is lawful, but an agreement to prohibit standards participants (or implementers) from implementing a competing standard or rival technology would be unlawful – although as a practical matter, a successful standard may lawfully achieve this result through the workings of the market.” (emphasis mine)
Draft P802.11ac_D1.0 prohibits both TKIP and GCMP.
  A protest was made over the exclusion of GCMP based on the policies of IEEE regarding unlawful anti-trust activity.

## Slide 4: Document 11-11/0896r0– status of protest
The opinion of IEEE legal counsel (emphasis mine):
  A standard can certainly prescribe a minimum functionality or feature set. A standard can also prohibit features that significantly interfere with the functionality or security of a prescribed feature.
  But if an additional function or feature does not significantly interfere with the performance of the minimum feature, then it is difficult to justify a standard's excluding that functionality.
  If there is a technical basis for the contemplated exclusion, then a discussion of that claimed basis should take place within the working group. If there was no intention to exclude a technology (but simply make clear that the standard does not require that technology), then the phrasing as written does not clearly accomplish the goal, and it should be rewritten.

## Slide 5: Do They Significantly Interfere with the Functionality or Security of 11ac?
TKIP – yes, it interferes with security
  The security assurance of its authentication component (Michael) is too weak for VHT– 2-20 vs. 2-32 for CCMP.
  RC4 (cipher used in TKIP) has known vulnerabilities. TKIP attempts to address them but no security proof exists. CCMP has a security proof.
GCMP– no, its functionality and security is superior to CCMP
  The security assurance of its authentication component (GHASH) is better than 802.11’s instantiation of CCMP– GCMP has a 128-bit tag, CCMP has a truncated 64-bit tag.
  GCMP performs authenticated encryption in one pass, CCMP uses two.
  Implementations of GCMP can be faster than CCMP in both hardware and in software.
  GCMP has a security proof.

## Slide 6: Conclusion
There is a valid technical reason to exclude TKIP.
  It is too slow
  It has an inacceptable security assurance.
There is no valid technical reason to exclude GCMP.
  GCMP does not interfere with the functionality or security of VHT
  GCMP is actually a superior cipher to CCMP.
We can resolve 25 GCMP comments in one of two ways:
  Remove the prohibition on GCMP and provide the reasons why TKIP is prohibited; or
  Strike the paragraph in its entirety! TKIP has been deprecated anyway.

## Slide 7: Going Further
Some VHT data rates cannot be supported by CCMP, even in hardware
  No stalls in the AES pipeline with GCMP.
A fast(er) software implementation of VHT
  Software implementations of GCMP can be accelerated with look-up tables at a modest cost in memory.
  Some vendors support a single “carryless multiply” operation that comprises the GHASH. This can be used to greatly increase the speed of a software implementation of GCMP.
We can resolve 4 more GCMP comments
  Add support for GCMP into 11ac draft, 11-10/1032r2 shows how!

## Slide 8: References
http://standards.ieee.org/develop/policies/antitrust.pdf
11-11-0896-00-0000-p802-11ac-draft-language-protest
11-10-1032-02-00ac-the-gcm-mode-of-aes
D. McGrew and J. Viega-- The Security and Performance of the Galois/Counter Mode (GCM) of Operation. INDOCRYPT 2004, LNCS vol 3348, Springer, pp. 343-355, 2004.
Presentation by Morris Dworkin (NIST) to SAAG at 69th IETF meeting, July 26th, 2007
http://www.ietf.org/proceedings/69/slides/saag-1/sld1.htm