## Slide 1: Considerations of Compatibility with 802.11v and 11k
Date: 2011-07-12
Authors:

## Slide 2: Abstract
Motivation
  As mentioned in recent FR-EM document(11-11-0905r1)[1] , compatibility with the existing 802.11 standard and its amendments (802.11i/w/s/k/v/u or other TGs) can be also included as one of maintaining 802.11 user experience(TGah R5), but it is not means that 802.11i/w/s/k/v/u shall be used in all the applications.
  As we discussed about network management of TGah (11-11-0672r0) [2] last meeting, IEEE 802.11v/k or IEEE 802.11u may only apply to some specific TGah Use Cases.
Purpose
  This presentation further discusses the requirements for 11v/k features in TGah Use Cases.

## Slide 3: 11ah network operation& management
15.4g-11ah
Router
11ah AP
Backbone network
Operator platform
Use Case 1
Use Case 2
Use Case 3

## Slide 4: Current Use Cases [3]
Use Case 1 : Sensors and meters
  1a: 11/17r5, slide 7 Smart Grid - Meter to Pole
  1c: 11/253, Environmental/Agricultural Monitoring
  1d: 11/260r1, slid 4 Industrial process sensors
  1e: 11/17r5, slid 17 Healthcare
  1f: 11/241r0, slide 3 Healthcare
  1g: 11/241r0, slid 5 Home/Building Automation
  1h: 11/242r0, slid 2 Home sensors
Use Case 2 : Backhaul Sensor and meter data
  2a: 11/14r2, slide 5 Backhaul aggregation of sensors
  2b: 11/260r1, slide 4 Backhaul aggregation of industrial sensors
Use Case 3 : Extended range Wi-Fi
  3a: 11/243r0 Outdoor extended range hotspot
  3b: 11/244r1 Outdoor Wi-Fi for cellular traffic offloading

## Slide 5: 11v and 11k Features for TGah
11v/k Related Network Optimization Functions
11v Related Power Saving Functions

## Slide 6: Network Optimization Functions for TGah
Network diagnostic and troubleshooting/Inventory/network “Health” Monitoring
Network diagnostic and troubleshooting and network inventory functions are useful for administrator to quickly respond to the poor network performance, by using event/diagnostic Reports (11v) and statistics (11k) features.
Network “Health” monitoring function can further help administrator knows network load and utilization at any time, but more features need to be supported.
Load balancing/ efficient channel utilization/ power and channel management
These functions are very useful in large-scale and densely located networks ( e.g. Smart Grid, building, Use Case3 ) to improve radio channel utilization and reduce interference.
Location services
These functions might be used for physical locate the broken/stolen/alarm sensors (especially in uninhabited area) for sensors/property recovery, location based troubleshooting and emergency services.

## Slide 7: Rank of 11v Power Saving Functions in TGah Use Cases
 | 11v Features | Use Case 1-Sensors and Meters |  |  |  |  | Use Case 2-Backhaul |  | Use Case 3-Extended Range | 
 |  | 1a Smart Grid | 1c env. agr. | 1d Industrial | 1e/1f Health care | 1g/1h Home building | 2a 15.4 /4g | 2b Industrial | 3a Hot spot | 3b Off load
1 | Proxy ARP, BSS Max Idle Period | H1 | H 1 | H 1 | H1 | H1 | H1 | H1 | H1 | H1
2 | Traffic Filtering Service, WNM Sleep Mode | H2 | H2 | H2 | H2 | H 2 | H2 | H2 | H2 | H2
3 | BSS Termination | L | L | L | L | L | M | M | M | M
4 | DMS, FMS, TIM Broadcast, Proxy ARP | M | M | M | H3 | M | H3 | M | M | M

## Slide 8
Conclusion: compatibility with 11v/k due to TGah Use Cases
Use Case 1 : Sensors and meters
  For large mount of battery operated sensors /meters are supported, the user and manufacturer want to extend the battery life of end devices as long as possible, only perform essential functions.
  If 11ah station function is implemented in each wireless sensor controller, then most of IEEE 802.11v/k features may not probably be implemented due to higher cost or other reasons, but some of power saving features in 11v may need to be implemented.
Use Case 2 : Backhaul Sensor and meter data
  For 11ah STA is an aggregator of leaf sensors, the information of sensors need to be collected by 11ah STA such as battery power status, location and traffic status , and then 11ah STA reports the information to 11ah AP for network management (e.g. load balance and troubleshooting).
  Some of IEEE 802.11v/k features may be supported by 11ah.
Use Case 3 : Extended range Wi-Fi
  It is an extension of traditional Wi-Fi. Operator need to operate& manage not only 11ahAP, but also 11ah stations by the proxy of 11ah AP , especially for 3b(cellular traffic offloading).
  Some of IEEE 802.11v/k features may be supported by 11ah.

## Slide 9: Next Step Consideration
FR-R5 Maintaining user experience - 11v/k
    Network operation & management can be considered into two categories:
  Network Optimization
- network diagnostic and troubleshooting/Inventory
- load balancing
- efficient channel utilization
- efficient power and channel management
- location services
- …
  Power Saving

## Slide 10: Next Step Consideration (cont’d)
    For 11ah applications, power saving is a priority, 11v related power saving scheme should be considered.
  Proxy ARP, BSS Max Idle Period,“Wake on WLAN ” are considered as essential functions in all 11ah Use Cases.
  For multicast traffic , scheme of DMS, FMS and TIM Broadcast can save more power for STA.
    For cost and other considerations, schemes of network optimization in 11v/k need to be simplified, or new schemes might be considered.
FR-R7 Enhanced Power Saving
    Reusing power saving scheme in 802.11 and 11v as more as possible is a principle.
    Some modification in 11v and new power saving schemes might be considered due to different 11ah Use cases.

## Slide 11: References
[1] TGah Functional Requirements and Evaluation Methodology Rev. 1, IEEE802.11-11/0905r1
[2] IEEE 802.11ah network operation & management consideration for functional requirement, IEEE 802.11-11//0672r0
[3] Potential Compromise for 802.11ah Use Case Document, IEEE802.11-11/0457r0
[4] IEEE 802.11v-2011
[5] IEEE 802.11k-2008