## Slide 1: TGai Authentication Protocol Proposal
Date: 2011-07-17
Authors:
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroshi Mano | ROOT INC. | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses the following phase.
Authentication and Association

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: Network Assumption
STA
STA
STA
AP
Network
Standalone
(Home/Small Office, No AS)
STA
STA
STA
AP
Network
Enterprise
(ISP/Large Office, with AS)
STA
STA
STA
AP
STA
STA
STA
AP
AS

## Slide 5: Key Sharing
Standalone
  A PMK is pre-shared between AP and an STA.
  Each STA has a different PMK.
Enterprise
  A PMK is pre-shared between AS and an STA.
  Each STA has a different PMK.
  A shared secret (AP-key) is pre-shared between AS and AP.
  Each AP has a different AP-key.
RADIUS

## Slide 6: Authentication Protocol Sequence(Standalone)
STA
AP
Beacon
(TS, aiCAP)
Probe Req.
Probe Resp.
(TS, aiCAP)
Assoc. Req.
(TS, Nonce, NAI, MIC)
Beacon and Probe Resp. deliver
the same information. To reduce occupied air-time, Probe should not be used.
Beacon/Probe Resp. delivers Timestamp
and ai capability indicator.
This Timestamp must be unique. So it’s
different from TSF. Any other unique
number such as ANonce in EAP can be
alternative.
Assoc. Req. delivers
TS: received timestamp
Nonce: unique random number
NAI: user ID (RFC2486)
MIC: Apply hash function to a part of the frame. Then HMAC hash function with PMK to the previous result. (RFC2104)
AP confirms the validity of each information. AP authenticates the STA by calculating and comparing MIC.
PTK is calculated by applying HMAC
to the Nonce with PMK.
PTK is calculated by applying HMAC
to the Nonce with PMK.
PTK shared
Assoc. Resp.
(TS, PTKVT, GTK, MIC)
Assoc. Resp. delivers
TS: timestamp included in the Req.
PTKVT: PTK validity time.
GTK: GTK is encrypted with PTK.
MIC: Apply HMAC hash function with PTK to a part of the frame. (HMAC: RFC2104)
STA confirms the validity of each
information. STA authenticates the AP by calculating
and comparing MIC.
Authentication, Key sharing, Association completed

## Slide 7: Current State Machine (IEEE802.11-2007)
NOTE 3—IEEE 802.11 Open System authentication provides no security, but is included to
maintain backward compatibility with the IEEE 802.11 state machine (see 11.3). (8.4.1.2.1 b))

## Slide 8: TGai State Machine
In real implementation
  STA: Skip transmitting Auth Req.
  AP: Process Open System authentication and association sequentially.
  These modifications are small.
  And can coexist with legacy system (state machine).
  We tried to implement on NetBSD, Linux and Android.
State 1:
Unauthenticated,
Unassociated
State 3:
Authenticated,
Associated
Sucessful
Association
Disassociation
Notification

## Slide 9: Protocol Features
1.5 round-trip frame exchange to complete authentication and PTK/GTK setup.
Mutual Authentication between AP and STA
  Both AP and STA check MIC in the Assoc frame.
  MIC is calculated by using PMK.
  So they can authenticate mutually.
PTK never on-the-air
  PTK is calculated by STA and AP separately.
  So PTK is never on-the-air.
Early PTK share
  PTK can be shared after the AP received Assoc. Request.
  So some information, GTK, upper layer information, can be encrypted even in the Assoc. Request.

## Slide 10: Security Consideration
Major Attacks
  Replay Attack
    By using timestamp, AP can eliminate replay attack.
  Man-in-the-middle Attack
    Prevented by “mutual authentication” and “PTK never on-the-air” features.
  Fake AP
    Prevented by “mutual authentication” feature.
Security Strength
  Security strength of this protocol depends on the strength of hash function.

## Slide 11: Authentication Protocol (Enterprise)
STA
AP
Beacon
(aiCAP, TS)
Probe Req.
Probe Resp.
(TS)
Assoc. Req.
(TS, Nonce, NAI, MIC1)
PTK shared
Assoc. Resp.
(TS, PTKVT, GTK, MIC4)
Authentication, Key sharing, Association completed
AS
Access Req.
(Nonce, NAI, MIC1, AD, MIC2 )
Access Approval
(PTKDD, MIC3)

## Slide 12: Out of Scope Issue
Protocol between AP and AS is out of scope of IEEE802.11.
So this should be discussed in IETF (AAA WG?).

## Slide 13: Authentication Process
AP
AS
STA
Association
Request
Authentication
Data
MIC1
hash
HMAC-hash
(PMK)
Association
Request
Authentication
Data
Access
Request
MIC1
Extract
MIC2
hash
HMAC-hash
(AP-key)
Access
Request
MIC2
Authentication
Data
MIC1
MIC2
MIC1
Extract
Extract
HMAC-hash
(AP-key)
HMAC-hash
(PMK)
Compare
Compare
Timestamp
Timestamp
Nonce
NAI…
Check Timestamp
Check User, Domain
Transmit
Transmit
Beacon
Probe Resp.
NAI
Nonce

## Slide 14: Authentication Process (Cont.)
AP
AS
STA
Association
Response
Authentication
Data
MIC4
hash
HMAC-hash
MIC3
Access
Request
Nonce
PTK
MIC1
Extract
HMAC-hash
(PMK)
Extract
HMAC-hash
(AP-key)
Hashed MIC1
PTKDD
XOR
Access
Approval
MIC3
HMAC-hash
(AP-key)
Access
Approval
MIC3
Compare
Extract
HMAC-hash
(AP-key)
MIC1
Hashed MIC1
HMAC-hash
(AP-key)
PTKDD
PTK
Extract
XOR
Association
Response
Authentication
Data (16byte)
MIC4
hash
HMAC-MD5
MIC4
Nonce
PTK
HMAC-hash
(PMK)
Compare
Extract
ENC(GTK)PTK
Transmit
Transmit

## Slide 15: Questions & Comments