## Slide 1: TGai Authentication Protocol Proposal
Date: 2011-07-22
Authors:
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroshi Mano | ROOT INC. | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses the following phase.
Authentication and Association

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3, 4

## Slide 4: Concept
STA
AP
Authentication, Key sharing, Association completed, use CCMP for data frames
4-way handshake,
no security
.11i authentication
.11i key sharing
Existing .11
STA
AP
Authentication, Key sharing, Association completed, use CCMP for data frames
handshake
Authentication
key sharing
.11ai
3(4) phases into 1.
No need to process
sequentially. These
can be processed
simultaneously.
Upper Layer Setup
(i.e. DHCP)

## Slide 5: Network Assumption
STA
STA
STA
AP
Network
Standalone
(Home/Small Office, No AS)
STA
STA
STA
AP
Network
Enterprise
(ISP/Large Office, with AS)
STA
STA
STA
AP
STA
STA
STA
AP
AS

## Slide 6: Pre-shared Information
Standalone
  A user ID and a PSK is pre-shared between AP and an STA.
  Each STA has a different user ID and a PSK.
  PMK is derived from PSK by existing method.
Enterprise
  A use ID and a PSK is pre-shared between AS and an STA.
  Each STA has a different use ID and a PSK.
  A shared secret (AP-key) is pre-shared between AS and AP.
  Each AP has a different AP-key.
  Each AP has at least one fixed reachable address. (i.e. fixed IP address)
Pre-shared Keys
  Pre-shared keys are distributed by other trust way, such as post-mail, memory card/stick, SIM card or over the trusted network as same as .11i pre-shared key distribution.
RADIUS

## Slide 7: Protocol Sequence Overview (Standalone)
STA
AP
Beacon
(ANonce, aiCAP)
Probe Req.
Probe Resp.
(ANonce, aiCAP)
Assoc. Req.
(ANonce, SNonce, NAI, MIC,
[ENC(ULI)])
PTK shared
Assoc. Resp.
(ANonce, Lifetime, MIC,
ENC(GTK, [ULI]))
Authentication, Key sharing, Association completed, use CCMP for data frames

## Slide 8: Beacon/Probe Response
AP transmits Beacon/Probe Resp. which includes .11ai capability indicator (aiCAP; new IE, new flag or new AKM suites in RSN IE) and ANonce (new IE).
ANonce must be unique number.
AP records ANonces and they expire in a certain period.
Beacon/Probe Response can include existing RSN IE for accommodating legacy devices.
(Probe request is not modified.)
STA
AP
Beacon
(ANonce, aiCAP)
Probe Req.
Probe Resp.
(ANonce, aiCAP)

## Slide 9: .11ai Association Request
A .11ai STA can know the AP supports .11ai association by aiCAP in Beacon/Probe resp.
The STA picks up and records ANonce from Beacon/Probe resp.
The STA generates SNonce which is unique number.
The STA calculate PTK as following. (same key hierarchy as described in 8.5.1.2 in IEEE802.11-2007)
  PTK  PRF-384(PMK, “Pair wise key expansion”, Min(AA, SPA) || Max(AA, SPA) || Min(ANonce, SNonce) || Max(ANonce, SNonce))
If the STA has upper layer information (ULI) to send, it can be encrypted by PTK(KCK, KEK or TK which key is better?).
The STA construct a .11ai Association request which includes the following information.
  aiCAP
  ANonce
  SNonce
  NAI
  ENC(ULI)
Calculate and append MIC. MIC is calculated by following method.
  Apply Hash function (i.e. SHA-1) to an appropriate part of the frame.
  Apply HMAC-hash function or Michael to the result with PTK, KCK, KEK or TK.
STA
AP
Assoc. Req.
(aiCAP, ANonce,
SNonce, NAI,
ENC(ULI), MIC)
Beacon
(ANonce, aiCAP)
Probe Req.
Probe Resp.
(ANonce, aiCAP)

## Slide 10: Authentication by AP
If the AP receives association request with aiCAP, the AP recognizes the STA requesting .11ai association.
The AP checks following information.
  ANonce: Search the ANonce list recorded. If the same ANonce is found, it’s success.
  NAI: Search user ID list. If the same user ID is found, it’s success and retrieve PMK for the user.
Now the AP has all of required information to calculate PTK. The AP calculate it.
The AP calculates and compares the MIC with PTK or key derived from PTK. If they matches, the authentication successes.
If encrypted ULI is included, the AP decrypts it and process it. (Don’t defined how to do yet.)
STA
AP
Assoc. Req.
(aiCAP, ANonce,
SNonce, NAI,
ENC(ULI), MIC)
PTK shared

## Slide 11: .11ai Association Response
The AP assigns an AID to the STA.
  It means AID is assigned only after successful authentication.
The AP constructs .11ai association response including the following information and transmits to the STA.
  aiCAP
  ANonce: included in the association request.
  Lifetime: PTK lifetime.
  GTK: Derived by existing method and encrypted by using PTK, KCK, KEK or TK.
  ULI: If available at that time. It can be encrypted.
    If need more time to response, set “send you later” indicator in ULI.
  MIC
STA
AP
Assoc. Resp.
(aiCAP, ANonce,
Lifetime,
ENC(GTK, [ULI]),
MIC)

## Slide 12: Authentication by STA
The AP checks the following information.
  ANonce: Identify the request to which the response correspond.
  MIC
If the MIC matches, the authentication successes.
Decrypt GTK and install.
If available, decrypt ULI and process.
Authentication and Association have been completed.
Data frames are encrypted by CCMP.
STA
AP
Assoc. Resp.
(aiCAP, ANonce,
Lifetime,
ENC(GTK, [ULI]),
MIC)
Authentication, Key sharing, Association complete
CCMP for data frames

## Slide 13: non-.11ai (legacy) STA and .11ai AP
Non-.11ai STA will ignore aiCAP and other .11ai specific IEs .
The STA just transmits legacy Authentication frame to the AP.
The AP can recognize the STA intends to connect by legacy method by receiving legacy Authentication frame.
The AP accommodates the STA as legacy device.

## Slide 14: .11ai STA and non-.11ai (legacy) AP
.11ai STA can recognize the AP does not support .11ai by no aiCAP in beacon or probe response.
The STA will connect to the AP by legacy method or search other AP.

## Slide 15: Current State Machine (IEEE802.11-2007)
NOTE 3—IEEE 802.11 Open System authentication provides no security, but is included to
maintain backward compatibility with the IEEE 802.11 state machine (see 11.3). (8.4.1.2.1 b))

## Slide 16: TGai State Machine
In real implementation
  STA: Skip transmitting Auth Req.
  AP: Process Open System authentication and association sequentially.
  These modifications are very small.
  And can coexist with legacy system (state machine).
  We tried to implement on NetBSD, Linux and Android.
Successful
.11ai Association or
Reassociation

## Slide 17: Protocol Features
1.5 round-trip frame exchange to complete authentication and PTK/GTK setup.
Mutual Authentication between AP and STA
  Both AP and STA check MIC in the Assoc frame.
  MIC is calculated by using PTK or a key derived from PTK.
  So they can authenticate mutually.
PTK never on-the-air
  PTK is calculated by STA and AP separately.
  So PTK is never on-the-air.
Early PTK share
  PTK can be shared after the AP received Assoc. Request.
  So some information, GTK, upper layer information, can be encrypted even in the Assoc. Request.

## Slide 18: Comparison with .11i
 | .11i | This Protocol
Authentication | Vary (Depend on EAP method) | MIC in Assoc. frames. Depend on MIC hash function strength.
Clear text on-the-air for key sharing | ANonce, SNonce, AA, SPA | 
Key hierarchy | 8.5.1 in IEEE802.11-2007 | 
AID assignment | Before authentication | After authentication
Upper Layer Resource assignment | After authentication Encrypted | 
Data Frame Encryption | CCMP | 

## Slide 19: EAPOL-Key Message 4
Key negotiation of this protocol is very similar to .11i.
But no message which corresponding to EPAOL-Key message 4.
Message 4 is just for confirmation that correct PTK is installed.
In our protocol, PTK is already checked before transmitting Assoc. resp.
If it does not match, the authentication fails.
And the AP can confirm that the STA received Assoc. resp. or not by ACK frame because Assoc. resp. is an unicast frame.
STA
AP
EAPOL-Key 1
(ANonce)
EAPOL-Key 2
(SNonce, MIC)
EAPOL-Key 3
(ANonce, GTK, MIC)
EAPOL-Key 4
(MIC)
STA
AP
Beacon/Probe resp.
(ANonce)
.11ai Assoc req.
(ANonce, SNonce, MIC)
.11ai Assoc resp.
(ANonce, GTK, MIC)
.11i
This Protocol
ACK

## Slide 20: Security Consideration
Major Attacks
  Replay Attack
  Fake AP
Security Strength
  Authentication strength of this protocol depends on the strength of hash function.

## Slide 21: Replay Attack
Malicious STA with different MAC address with correct STA.
  The authentication fails because of MIC mismatch.
Malicious STA with the same MAC address with correct STA.
  Replay long time after the correct association request.
    The authentication fails because the ANonce has been expired.
  Replay immediately after the correct association request.
    The malicious STA may receive the same frame as the correct STA. But the PTK is not included and the GTK is encrypted by PTK. The malicious STA don’t know the PTK. It cannot get any keys.
    Actually, the malicious STA don’t need to transmit replay association request. The information he can get is as same as just sniffing.

## Slide 22: Fake AP
Fake APs can not know the correct PTK and, of course, PMK.
PTKs are never on-the-air.
If a fake AP transmits a fake association response to a correct STA corresponding to a correct association request, the authentication by the STA fails because of the MIC mismatch.
The STA will retry or search other AP.

## Slide 23: Enterprise Network Model
We’re so sorry but we didn’t have enough time to revise the slides for enterprise network.
The old slides may make you confusing.
So we deleted these slides.
We’ll revise them ASAP and show in teleconferences and September session.

## Slide 24: Questions & Comments