## Slide 1: TGai Upper Layer Setup Proposal
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroshi Mano | ROOT INC. | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Date: 2011-07-17
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses the following phase.
Upper Layer Setup

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Upper Layer Information IE
We, IEEE802.11, should specify only a container IE which deliver upper layer information.
Because
  Our scope is L1 and L2.
  DHCP options are growing and difficult to follow.
  IP specific contents should be specified by IETF.
So we should make liaison to IETF and discuss in IETF.

## Slide 5: Introduction of an Example Solution
We intend to show just technical probability by this example.
Detailed specification should be discussed in IETF.

## Slide 6: DHCPv4
Usually 4 messages are exchanged in DHCPv4.
DHCPv4 allows multiple servers on a single subnet.
DHCPREQUEST is broadcasted to notify which server is selected.
Client
Server
DHCPDISCOVER
(Broadcast)
DHCPOFFER
(Unicast or Broadcast)
DHCPREQUEST
(Broadcast)
DHCPACK
(Unicast or Broadcast)

## Slide 7: FILS delivers DHCP messages
STA put a DHCP message to UpperLayer Information IE and transmit to AP.
AP picks up the DHCP message from Upper Layer Information IE, then constructs complete DHCP message and transmit it to DHCP Server.
And vice versa.
STA
AP
DHCP Server
FILS message
Upper Layer Info IE
DHCP message
DHCP message
FILS message
Upper Layer Info IE

## Slide 8: Modifications
Maximum length of IE is limited to 256 octet. So one DHCP message may be divided into multiple IEs.
If FILS uses only one round-trip message exchange, more modifications are required.

## Slide 9: One Round-trip DHCP modification
When AP starts up, AP transmit DHCPDISCOVER to DHCP Servers.
DHCP servers transmit DHCPOFFER to the AP.
The AP selects one DHCP server and broadcast DHCPREQUEST without IP address assignment.
The selected DHCP server transmits DHCPACK to the AP without IP address assignment.
STA transmits DHCPREQUEST in FILS message. This may or may not include specific (desired) IP address.
The AP transfer it to the selected DHCP server.
DHCP server assigns IP address even if the DHCPREQUEST does not include specific IP address.
The AP transfer it to the STA in FILS message.
DHCP modifications are red-lined.
STA
AP
DHCP
Server
1
2
3
4
5
8
DHCP
Server
6
7

## Slide 10: Questions & Comments