## Slide 1: TGai Upper Layer Setup Proposal
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroshi Mano | ROOT INC. | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Date: 2011-09-18
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses the following phase.
Upper Layer Setup

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Typical Sequence for Internet Access
STA
AP
DHCP
DHCP Server
Authentication, Association, Key negotiation
DNS Server
Gateway
Correspondent Node
Communication
ARP/ND
DNS
4 round-trips of frame exchanges between AP and STA before communication in addition to authentication, association and key negotiation
Proxy ARP/ND
Nodes on the Network

## Slide 5: Reduce Frame Exchanges
One of the target of TGai is to accommodate a lot of STAs simultaneously.
Each frame consumes air-time for IFSs regardless of the frame length.
So reducing the number of frame exchanges is effective for this target.

## Slide 6: Optimized Sequence for Internet Access with 1 Round-trip Association (11/1160r2)
STA
AP
DHCP Server
DNS Server
Gateway
Correspondent Node
Communication
AS
Virtually Simultaneous
(RADIUS for AAA)
Assoc. Req.
Assoc. Resp.
DHCP w/Rapid Commit Option
ARP/ND
DNS
Proxy ARP/ND
Nodes on the Network

## Slide 7: Delayed Upper Layer Response
STA
AP
Upper Layer Server 1
AS
(RADIUS for AAA)
Assoc. Req.
Assoc. Resp.
w/Upper Layer
Response 1
Upper Layer Request 1
Timeout
Upper Layer Server 2
Upper Layer Request 2
Upper Layer Response 1
Upper Layer Response 2
Action Frame
w/Upper Layer
Response 2

## Slide 8: Upper Layer Information IE (ULI IE)
Flags
Length: Variable
Element ID: x
1octet
1octet
Variable octet
Sub-IEs
1octet

## Slide 9: Flags
B0: Encryption
  0: Sub-IEs are not encrypted.
  1: Sub-IEs are encrypted.
B1: More Data
  0: Final ULI IE
  1: Continue to the next ULI IE
B2-B7: Reserved
Encryption
More Data
Reserved
B0
B1
B2
B3
B4
B5
B6
B7

## Slide 10: Upper Layer Type Sub-IE
Upper Layer Type:
  4: IPv4
  6: IPv6
Length: Variable
Sub-IE ID: 1
1octet
Variable octet
1octet
Upper Layer Type
1octet

## Slide 11: DHCP Sub-IE
DHCP message format is defined in RFC2131 (IPv4) and RFC3315 (IPv6). Some options are defined in other RFCs.
Length: Variable
Sub-IE ID: 2
1octet
Variable octet
DHCP Message (not include UDP/IP header)
1octet

## Slide 12: ARP Table Sub-IE
This IE includes pairs of IPv4 address and MAC address of nodes in the local network which the AP knows.
Length: Variable
Sub-IE ID: 3
1octet
Variable octet
1octet
IPv4 Address (4 octets)
MAC Address (6 octets)

## Slide 13: ND Sub-IE
This IE includes pairs of IPv6 address and MAC address of hosts in the local network which the AP knows.
Length: Variable
Sub-IE ID: 4
1octet
Variable octet
1octet
IPv6 Address (16 octets)
MAC Address (6 octets)

## Slide 14: DNS Sub-IE
DNS message format is defined in RFC1035.
Length: Variable
Sub-IE ID: 5
1octet
Variable octet
DNS Message (not include UDP/IP header)
1octet

## Slide 15: Padding Sub-IE
Padding for encryption if required.
Sub-IE ID: 0
1octet

## Slide 16: Sub-IEs Usage
Beacon/Probe Response
  Upper Layer Type Sub-IE
    Supported upper layer type.
Association Request
  Upper Layer Type Sub-IE
    Request which upper layer type to configure.
  DNS Sub-IE (optional)
    DNS query.
Association Response
  DHCP Sub-IE
    DHCPACK from the DHCP server.
  ARP Table Sub-IE (IPv4)
    ARP table
  ND Sub-IE (IPv6)
    ND configuration
  DNS Sub-IE (optional)
    DNS answer

## Slide 17: DHCP Proxy or Relay (Translation)
AP
Between STA and AP, same protocol can be used in any topology.
Backend DHCP topology is just implementation and operation matter.
It’s out of scope of TGai.
DHCP Proxy
FILS Module
DHCP Server
AP
DHCP Relay
FILS Module
DHCP Server
AP
DHCP Proxy
FILS Module
DHCP Server
AP
FILS Module
DHCP Server
DHCP Relay

## Slide 18: Pros and Cons
 | Pros | Cons
AP pass through Upper LayerPacket (977r1, 1167r0) | Keep Layer Manner Flexible | Limited Optimization (STA cannot generate ARP, DNS and most packets without IP address assignment)
Function Specific IE (977r2, 1108r1, 1047r1) | Optimized (Less packet exchange between STA and AP) | Layer Violation Limited Flexibility (Specified Upper Layer Protocols Only)
Which is better?

## Slide 19: Is DNS sub-IE needed?
From implementation point of view,
  Most DNS queries are generated by applications, not by system.
  So it’s hard to syncronize.
  But the capability should be specified.

## Slide 20: More Sub-IEs
Mobile IP
  Mobile IP registration request/response may be merged to association request/response.

## Slide 21: Questions & Comments