## Slide 1: TGai Upper Layer Setup Proposal
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroshi Mano | ROOT INC. | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Date: 2011-11-06
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses the following phase.
Upper Layer Setup

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Typical Sequence for Internet Access
STA
AP
DHCP
DHCP Server
Authentication, Association, Key negotiation
Gateway
Correspondent Node
Communication
ARP/ND
3 round-trips of frame exchanges between AP and STA before communication in addition to authentication, association and key negotiation
ARP/ND
Nodes on the Network

## Slide 5: Reduce Frame Exchanges
One of the target of TGai is to accommodate a lot of STAs simultaneously.
Each frame consumes air-time for IFSs regardless of the frame length.
So reducing the number of frame exchanges is effective for this target.

## Slide 6: Optimized Sequence for Internet Access with 1 Round-trip Association (11/1160r2)
STA
AP
DHCP Server
Gateway
Correspondent Node
Communication
AS
Virtually Simultaneous
(RADIUS for AAA)
Assoc. Req.
Assoc. Resp.
DHCP w/Rapid Commit Option
ARP/ND
Proxy ARP/ND
Nodes on the Network

## Slide 7: Delayed Upper Layer Response
STA
AP
Upper Layer Node 1
AS
(RADIUS for AAA)
Assoc. Req.
Assoc. Resp.
w/Upper Layer
Response 1
Upper Layer Request 1
Timeout
Upper Layer Node 2
Upper Layer Request 2
Upper Layer Response 1
Upper Layer Response 2
Action Frame
w/Upper Layer
Response 2

## Slide 8: Upper Layer Information IE (ULI IE)
Flags
Length: Variable
Element ID: x
1octet
1octet
Variable octet
Sub-IEs
1octet

## Slide 9: Flags
B0: Encryption
  0: Sub-IEs are not encrypted.
  1: Sub-IEs are encrypted.
B1: More Data
  0: Final ULI IE
  1: Continue to the next ULI IE
B2-B7: Reserved
Encryption
More Data
Reserved
B0
B1
B2
B3
B4
B5
B6
B7

## Slide 10: Upper Layer Type Sub-IE
Upper Layer Type:
  4: IPv4
  6: IPv6
Length: Variable
Sub-IE ID: 1
1octet
Variable octet
1octet
Upper Layer Type
1octet

## Slide 11: DHCP Sub-IE
DHCP message format is defined in RFC2131 (IPv4) and RFC3315 (IPv6). Some options are defined in other RFCs.
Length: Variable
Sub-IE ID: 2
1octet
Variable octet
DHCP Message (not include UDP/IP header)
1octet

## Slide 12: RA Sub-IE
DHCP message format is defined in RFC2131 (IPv4) and RFC3315 (IPv6). Some options are defined in other RFCs.
Length: Variable
Sub-IE ID: 3
1octet
Variable octet
Router Advertisement Message
(include IPv6 header)
1octet

## Slide 13: ARP Table Sub-IE
This IE includes pairs of IPv4 address and MAC address of the gateway (and optionally other hosts in the local network).
Length: Variable
Sub-IE ID: 4
1octet
Variable octet
1octet
IPv4 Address (4 octets)
MAC Address (6 octets)

## Slide 14: ND Sub-IE
This IE includes pairs of IPv6 address and MAC address of the gateway (and optionally other hosts in the local network).
Length: Variable
Sub-IE ID: 5
1octet
Variable octet
1octet
IPv6 Address (16 octets)
MAC Address (6 octets)

## Slide 15: Padding Sub-IE
Padding for encryption if required.
Sub-IE ID: 0
1octet

## Slide 16: Sub-IEs Usage
Beacon/Probe Response
  Upper Layer Type Sub-IE
    Supported upper layer type.
Association Request
  Upper Layer Type Sub-IE
    Request which upper layer type to configure.
Association Response
  DHCP Sub-IE
    DHCPACK from the DHCP server.
  ARP Table Sub-IE (IPv4)
    ARP table
  ND Sub-IE (IPv6)
    ND configuration

## Slide 17: IPv4 Behavior
STA transmits Assoc. Req. to AP with “IPv4 config required” IE.
  The IE is NOT DHCP message. Just indicate to request IPv4 configuration.
The AP authenticate the STA.
After successful authentication, the AP generates DHCPDISCOVER with RCO and transmit to DHCP server.
  “chaddr” field in DHCPDISCOVER is filled by STA’s MAC address.
The DHCP server replies DHCPACK (or DHCPOFFER)
The AP extracts DHCP message. The assigned IP address and some DHCP options and MAC address of the gateway are filled in an IE (or IEs). Then the AP transmits Assoc. Resp. with the IE(s) to the STA.
The STA setup its IPv4 layer.

## Slide 18: IPv6 Behavior
AP caches RA.
  AP can know DHCPv6 is required or not in the network by receiving RA.
STA transmits Assoc. Req. with “IPv6 configure required IE” to AP.
The AP authenticate the STA.
After successful authentication, the AP generates DHCP Solicit with RCO and transmit to DHCP server if DHCPv6 is required in the network.
  DUID-LLT or DUID-LL in DHCP Solicit is filled by STA’s MAC address.
The DHCP server replies DHCP Reply.
The AP extracts DHCP message. The RA and DHCP options are filled in an IE (or IEs). Then the AP transmits Assoc. Resp. with the IE(s) to the STA.
The STA setup its IPv6 layer.

## Slide 19: Comparison with Other Proposals
11-11/977r3 (Hitoshi)
11-11/1047r3 (Ping)
11-11/1108r1 (Gabor)
11-11/1167r0 (Hiroki)

## Slide 20: What’s in Common
Create new IE(s) for carrying upper layer setup information.
  Formats and contents are different.
The IE is carried by Auth/Assoc frames.
DHCP with Rapid Commit Option (RCO) can be used behind AP.
Upper Layer Setup capability is advertised in Beacon/Probe Response.
DHCP messages after initial setup (renew, release…) are transferred as data frame.

## Slide 21: Concept
Ping, Hiroki
  STA transmits DHCP message in IE.
Hitoshi, Gabor
  STA just requests to the AP, “give me IP address, etc...”.
STA
AP
DHCP Server
DHCP, RS/RA
STA
AP
DHCP Server
DHCP, RS/RA
Function Specific IE

## Slide 22: DHCP message carried in IE
MAC Header (14 octet)
IP Header (20 octet)
UDP Header (8 octet)
DHCP message body
Hitoshi
Ping
Hiroki
Gabor’s proposal doesn’t carry DHCP messages.

## Slide 23: Gateway MAC Address
In IPv4/IPv6 environment, MAC address of the gateway is required for communication in most cases.
ARP/ND requires IP address of STA.
So IP address must be assigned before starting ARP/ND.
This means IP address assignment (DHCP/RA) and ARP/ND must be processed sequencially in existing protocol.
Hiroki, Ping: DHCP/RA and ARP/ND must be processed seperately. So it requires 2-roundtrip frame exchanges.
Hitoshi, Gabor: It can be processed simultaneously. So it can be done in 1-roundtrip frame exchange.

## Slide 24: Flexibility
Hiroki
  Just defining capsulating IE.
  Don’t care about upper layer protocol in proposal.
  Supported protocols depends on implementation and operation(configuration).
  IEEE802.11 amendment is NOT required for other protocol support.
Ping
  Supported protocols are specified in ULM field definition.
  IEEE802.11 amendment is required for other protocol support.
Hitoshi, Gabor
  Supported protocols are specified in IE definition.
  IEEE802.11 amendment is required for other protocol support.

## Slide 25: Security Consideration
Hiroki, Ping
  STA can transmit any packets (with header) in the proposed IE.
  All upper layer messages before successful authentication must be fully inspected, because the AP should not transfer undesired packets.
  And also returning packet (CN->STA) must be fully inspected by AP.
Hitoshi, Gabor
  The upper layer information IE does NOT contain any upper layer packets.
  So the STA cannot transmit upper layer message to any hosts by the proposed IE.

## Slide 26: Questions & Comments