## Slide 1: TGai Upper Layer Setup Proposal
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | Allied Telesis R&D Center | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroshi Mano | Allied Telesis R&D Center | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Date: 2011-11-09
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai which addresses upper layer setup phase and comparison with other proposals.

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 4

## Slide 4: Typical Sequence for Internet Access
STA
AP
DHCP
DHCP Server
Authentication, Association, Key negotiation
Gateway
Correspondent Node
Communication
ARP/ND
3 round-trips of frame exchanges between AP and STA before communication in addition to authentication, association and key negotiation

## Slide 5: Reduce Frame Exchanges
One of the target of TGai is to accommodate a lot of STAs simultaneously.
Each frame consumes air-time for IFSs regardless of the frame length.
So reducing the number of frame exchanges is effective for this target.

## Slide 6: Optimized Sequence for Internet Access with 1 Round-trip Association (11/1160r3)
STA
AP
DHCP Server
Gateway
Correspondent Node
Communication
AS
Virtually Simultaneous
(RADIUS for AAA)
Assoc. Req.
w/ULI IEs
(could be
encrypted)
Assoc. Resp.
w/ULI IEs
(could be
encrypted)
DHCP w/Rapid Commit Option
ARP/ND

## Slide 7: New IEs
Upper Layer Type IE
DHCP IE
RA IE
ARP IE
NDP IE

## Slide 8: Upper Layer Type IE
Upper Layer Type:
  4: IPv4
  6: IPv6
Length: Variable
IE ID: xx
1octet
Variable octet
1octet
Upper Layer Type
1octet

## Slide 9: DHCP IE
DHCP message format is defined in RFC2131 (IPv4) and RFC3315 (IPv6). Some options are defined in other RFCs.
Length: Variable
IE ID: xx
1octet
Variable octet
1octet
Flags
1octet
DHCP Message (not include UDP/IP header)

## Slide 10: Flags in DHCP IE
B0: Type
  0: DHCPv4
  1: DHCPv6
B1: Fragment
  0: Final DHCP IE
  1: Continue to the next DHCP IE
B2-B7: Reserved
Type
Fragment
Reserved
B0
B1
B2
B3
B4
B5
B6
B7

## Slide 11: RA IE
DHCP message format is defined in RFC2131 (IPv4) and RFC3315 (IPv6). Some options are defined in other RFCs.
Length: Variable
IE ID: xx
1octet
Variable octet
Router Advertisement Message
(include IPv6 header)
1octet

## Slide 12: ARP IE
This IE includes pairs of IPv4 address and MAC address of the gateway (and optionally other hosts in the local network).
Length: Variable
IE ID: xx
1octet
Variable octet
1octet
IPv4 Address (4 octets)
MAC Address (6 octets)

## Slide 13: NDP IE
This IE includes pairs of IPv6 address and MAC address of the gateway (and optionally other hosts in the local network).
Length: Variable
IE ID: xx
1octet
Variable octet
1octet
IPv6 Address (16 octets)
MAC Address (6 octets)

## Slide 14: IEs Usage
Beacon/Probe Response
  Upper Layer Type IE
    Supported upper layer type.
Association Request
  Upper Layer Type IE
    Request which upper layer type to configure.
Association Response
  DHCP IE
    DHCPACK(IPv4)/DHCP Reply(IPv6) from the DHCP server.
  RA IE
    RA with IPv6 header.
  ARP IE (IPv4)
    ARP table
  NDP IE (IPv6)
    ND configuration

## Slide 15: IPv4 Behavior
AP transmits “IPv4 config available” IE in Beacon/Probe Response.
STA transmits Assoc. Req. to AP with “IPv4 config required” IE.
  The IE is NOT DHCP message. Just indicate to request IPv4 configuration.
The AP authenticate the STA.
After successful authentication, the AP generates DHCPDISCOVER with RCO and transmit to DHCP server.
  “chaddr” field in DHCPDISCOVER is filled by STA’s MAC address.
The DHCP server replies DHCPACK (or DHCPOFFER)
The AP extracts DHCP message. The DHCP message body and MAC address of the gateway are filled in IEs. Then the AP transmits Assoc. Resp. with the IEs to the STA.
The STA setup its IPv4 layer.

## Slide 16: IPv6 Behavior
AP caches RA.
  AP can know DHCPv6 is required or not by receiving RA.
AP transmits “IPv6 config available” IE in Beacon/Probe Response.
STA transmits Assoc. Req. with “IPv6 configure required IE” to AP.
The AP authenticate the STA.
After successful authentication, the AP generates DHCP Solicit with RCO and transmit to DHCP server if DHCPv6 is required in the network.
  DUID-LLT or DUID-LL in DHCP Solicit is filled by STA’s MAC address.
The DHCP server replies DHCP Reply.
The AP extracts DHCP message. The RA and DHCP message body are filled in IEs. Then the AP transmits Assoc. Resp. with the IEs to the STA.
The STA setup its IPv6 layer.

## Slide 17: Implementation Example for DHCPv4
WLAN driver
IP stack
Userland
WLAN driver
DHCP client
DHCP server
Configure to use IPv4 FILS
Setup
STA
AP
DHCP Server
IEs
Trigger
DHCP
Message
DHCP

## Slide 18: Comparison with Other Proposals
11-11/977r5 (Hitoshi)
11-11/1047r5 (Ping)
11-11/1108r1 (Gabor)
11-11/1167r0 (Hiroki)

## Slide 19: What’s in Common
Create new IE(s) for carrying upper layer setup information.
  Formats and contents are different.
The IE is carried by Auth/Assoc frames.
DHCP with Rapid Commit Option (RCO) can be used behind AP.
Upper Layer Setup capability is advertised in Beacon/Probe Response.
DHCP messages after initial setup (renew, release…) are transferred as data frame.

## Slide 20: Concept
Ping, Hiroki (Generic Container IE)
  STA transmits upper layer messages encapsulated as IE.
Hitoshi, Gabor (Function Specific IE)
  STA just requests to the AP, “tell me IPv4/IPv6 configuration.”.
STA
AP
DHCP Server
DHCP, RS/RA
STA
AP
DHCP Server
DHCP, RS/RA
Function Specific IE

## Slide 21: DHCP message carried in IE
MAC Header (14 octet)
IP Header (20 octet)
UDP Header (8 octet)
DHCP message body
Hitoshi
Ping
Hiroki
Gabor’s proposal doesn’t carry DHCP messages.

## Slide 22: DHCP without RCO
If the DHCP server does NOT support RCO,
  Hiroki, Ping
    2-roundtrip frame exchanges are required between STA and AP.
  Hitoshi, Gabor
    1-roundtrip frame exchange between STA and AP can complete upper layer setup.
Both upper layer setup latency and airtime occupation can be reduced.
STA
AP
DHCP Server
STA
AP
DHCP Server

## Slide 23: Gateway MAC Address
In IPv4/IPv6 environment, MAC address of the gateway is required for communication in most cases.
ARP/ND requires IP address of STA.
So IP address must be assigned before starting ARP/ND.
This means IP address assignment (DHCP/RA) and ARP/ND must be processed sequencially in existing protocol.
Hiroki, Ping: DHCP/RA and ARP/ND must be processed seperately. So it requires 2-roundtrip frame exchanges.
Hitoshi, Gabor: It can be processed simultaneously. So it can be done in 1-roundtrip frame exchange.

## Slide 24: Protocol Sequences
STA
AP
DHCP Server
Gateway
Virtually Simultaneous
DHCP w/Rapid Commit Option
ARP/ND
STA
AP
DHCP Server
Gateway
DHCP w/Rapid Commit Option
ARP/ND
Hiroki, Ping
Hitoshi, Gabor
IE(s)
Data Frame
IE(s)

## Slide 25: Flexibility
Hiroki, Ping
  Just defining container IE.
  Don’t care about upper layer protocol.
  Supported protocols depends on implementation and configuration.
  IEEE802.11 amendment is NOT required for other protocol support.
Hitoshi, Gabor
  Supported protocols are specified in IEs definition.
  IEEE802.11 amendment is required for other protocol support.

## Slide 26: Security Consideration
Hiroki, Ping
  STA can transmit any packets (with header) in their proposed IE.
  All upper layer messages before successful authentication must be fully inspected by AP, because the AP should not transfer undesired packets before successful authentication.
  And also returning packet (CN->STA) must be fully inspected by AP.
  Implementation will be complicated and it may easily cause security issues by mis-implementation and/or mis-configuration.
Hitoshi, Gabor
  The upper layer information IE does NOT contain any upper layer packets with headers.
  So the STA cannot transmit upper layer message to any hosts by the proposed IE.

## Slide 27: Comparison Summery
 | Gabor | Hitoshi | Ping | Hiroki
Can carry DHCP options? | N | Y | Y | Y
Can carry gateway MAC address simultaneously? | Y | Y | N | N
Is it unnecessary to modify IEEE802.11 for additional protocol support? | N | N | Y | Y
Is unnecessary full inspection by AP? | Y | Y | N | N
Y: preferable
N: unpreferable

## Slide 28: Questions & Comments

## Slide 29: Straw Poll
Which IE is better?
Generic container IE (Hiroki, Ping)
Function specific IE (Hitoshi, Gabor)
Abstain