## Slide 1: IP address configuration during association
Date: 2011-07-20
Authors:

## Slide 2: Abstract
One possible approach for IP configuration during association is presented here.

## Slide 3
Beacon (capability & type indication)
Association Req (IPaddr config IE, type)
Association Resp (IPv4 &/OR IPv6)
Passive scanning
802.1x (IPv4 &/OR IPv6)
DHCPd/Router
Data frames (use DHCP/RA to refresh IP)
Has to be backward compatible with existing mechanisms:
STA will receive RAs, and/or
STA will need to refresh its IP address using DHCP

## Slide 4
Association Req (IPaddr config IE, type)
Association Resp (IPv4 &/OR IPv6)
Active scanning
802.1x (IPv4 &/OR IPv6)
DHCPd/Router
Data frames (use DHCP/RA to refresh IP)
Probe Req (IPaddr config IE, type)
Probe Resp (IPaddr config IE, type)
See 11-11-0xxx-00-00ai for normative text

## Slide 5: Applicability
When network is v6 and with SLAAC deployed, IPv6 IE is static. IPv6 address config during assoc works for all these cases:
    AP is also the CPE (home environment)
    Router deep in the network
    Split MAC arch
When network deploys DHCP (v4 &/OR v6), applicability is limited
    Still works when AP is CPE running DHCPd
    MAY work when the DHCP server is a separate box
    Does NOT work in split MAC arch, when L2 AP terminates the association request (some vendors terminate the assoc req in the AC, in that case it may work)

## Slide 6
Association Req (IPaddr config IE, type)
Association Resp (IPv4 &/OR IPv6)
Router deep in the network
802.1x (IPv4 &/OR IPv6)
DHCPd/Router
Scanning (IPaddr config IE, type)
IF: • network is v6 and SLAAC, AP sees RA (before it receives the assoc req from the STA), can send IPv6 IE to STA in assoc resp
RA (Router Advertisement)

## Slide 7
Association Req (IPaddr config IE, type)
Association Resp (IPv4 &/OR IPv6)
DHCP server a separate box
802.1x (IPv4 &/OR IPv6)
DHCPd/Router
Scanning (IPaddr config IE, type)
IF: • network is v4 &/OR v6 supporting only DHCP for address config, then AP needs to contact DHCP beforehand

## Slide 8
Association Req (IPaddr config IE, type)
Association Resp (IPv4 &/OR IPv6)
DHCP server a separate box
802.1x (IPv4 &/OR IPv6)
DHCPd
Scanning (IPaddr config IE, type)
AP sends DHCP REQ for a pool of IP addresses
DHCPd delegates a pool of IP addresses to the AP, with given lifetime
new DHCP option needs to be defined for this to work
When lifetime expires, STA needs to contact DHCPd and renew IP its address. Problem: current DHCPd implementations store the MAC address of the requestor and do not renew the IP address if request comes from a different MAC address
 AP could send a new DHCP REQ to DHCPd and update the MAC address for a given IP address once it allocated that to a STA. Needs a new DHCP option.

## Slide 9
Association Req
Association Resp (IPv4 &/OR IPv6)
Split MAC architecture
DHCPd
Scanning (IPaddr config IE, type)
L2 AP
L3 AC
Same applicability restriction exists for the ProxyARP feature defined in 802.11v
If capability bits are set correctly (in this case to indicate that the feature is not supported by the AP), then there is no issue