## Slide 1: Network Selection Optimization
Date: 2011-07-20
Authors:

## Slide 2: Abstract
An optimized network discovery and selection is presented.

## Slide 3
Beacon (interworking capability)
ANQP (Table 8-176 infoID req)
ANQP Resp (ANQP IE)
SSID1
SSID2
Beacon (interworking capability)
ANQP (Table 8-176 infoID req)
ANQP Resp (ANQP IE)
Network Selection (SSID2)
Association Request
Current network selection procedure
- ANQP is unicast
- Each SSID is queried until a suitable network is found.
SSID3
ANQP (Table 8-176 infoID req)
ANQP Resp (ANQP IE)

## Slide 4
Beacon (interworking capability)
ANQP (Table 8-176 infoID req) broadcast
ANQP Resp (ANQP IE)
SSID1
SSID2
ANQP Resp (ANQP IE)
Network Selection (SSID2)
Association Request
Proposed optimized network selection procedure
SSID3
- ANQP to be sent to the broadcast address
AP answers if it can satisfy the condition in the request
ANQP responses are sent unicast
Saves (n-1)*RTT during the network selection procedure, n = nr of SSIDs queried, and the passive scanning period