## Slide 1: Optimized Network Selection
Date: 2012-03-15
Authors:

## Slide 2: Abstract
This presentation illustrates the network selection procedure and suggests changes to the current GAS protocol to reduce the network selection time, and calculates how much each improvement would reduce the network selection time.

## Slide 3
SSID1
SSID2
SSID3
t1
t2
t3
t4
t5
t1
t2
t3
t4
t5
t1
t2
t3
t4
t5
t1=time to generate the request
t2, t4=flight times
t3= time to process request and generate response
t5=time to process response
Tu=time for network discovery with GAS unicast Req
Tu = Ts+n(t1+t2+t3+t4+t5)=Ts+n(t1+t5+RTT+t3)
t2+t4=RTT
SCAN: Ts
Network Selection Procedure – Unicast GAS Request

## Slide 4
SSID1
SSID2
SSID3
t1
t2
t3
t4
t5
t1
t2
t3
t4
t5
t1
t2
t3
t4
t5
Tu = n(t1+t2+t3+t4+t5)=~n(2*t1+2*t2+t3)
Tuo=time for network discovery with GAS unicast Req, Optimised procedure
Tuo = Ts+n*t1+n*t5+t2+t3+t4=Ts+n(t1+t5)+RTT+t3
t2+t4=RTT
SCAN: Ts
Network Selection Procedure – Unicast GAS Req optimized

## Slide 5
SSID1
SSID2
SSID3
t1
t2
t3
t4
t5
t3
t2
t3
t4
Tb=time for network discovery with GAS broadcast Req
Tb = t1+t2+t3+t4+n*t5=~t1+RTT+t3+n*t5
t2+t4=RTT
No need to scan, just send GAS Req to broadcast address
Savings: Tu-Tb = Ts+(n-1)t1+(n-1)t3+(n-1)RTT
Tuo-Tb = Ts+ (n-1)t1
Tu=time for network discovery with Unicast GAS
Tuo=time for network discovery with optimised Unicast GAS
Tb=time for network discovery with Broadcast GAS
Network Selection Procedure – Broadcast GAS Request

## Slide 6
SSID1
SSID2
SSID3
t4
t5
t4
Tbr=Ts
Tbr=time for network discovery with broadcast req and resp
Saving: Tu-Tbr=n(t1+t5+RTT+t3)
Tuo-Tbr=n(t1+t5)+RTT+t3
Some STAs to perform passive scan, others active scan. Passive scan STAs would rely on other STAs to do active scan (send a broadcast GAS Req, which generates a GAS resp sent to broadcast address).
How to decide whether to perform active or passive scan?
Example pseudo code:
Let STA choose a random value p=(1..n), then x=random(y)modn; with y a random input to the number generator (eg exact time)
if x==p, do active scan,
else do passive scan
SCAN: Ts
Network Selection Procedure – Broadcast GAS Response

## Slide 7: Motion
Add the following text to section 6.3 of the SFD
STAs may send GAS initial request messages to broadcast addresses
Moved: Gabor Bajko
Seconded: Jarkko Kneckt
Result: 7/5/12, motion fails