## Slide 1: Public Safety Ad Hoc Requirements
Date: 2011-07-18
Authors:

## Slide 2: Public Safety Broadband Network
Spectrum in the 700 MHz band has been licensed by the FCC to carry a nationwide public safety broadband network [FCC-release].
In July of 2009 the 3GPP Long Term Evolution (LTE) was selected as the next generation technology for public safety communications.
Because the initial thrust of LTE has been on data services, voice over LTE is still in its infancy.

## Slide 3: Requirements for Public Safety (PS) Network
Public safety mission critical requirements include:
  Push to talk (e.g. < 500 ms connection time)
  Low latency voice (e.g. < 100 ms)
  Talkaround when fixed infrastructure coverage is unavailable
  Security with encryption
  Simultaneous voice and data
Network size
  Cluster of tens of devices in close range (within 20-30 meters)
  Interconnect clusters that may be separated by 100 meters

## Slide 4: Possible Talkaround Approach
What are the concerns for EDCA based Layer 2 in terms of mission-critical delay-sensitive VoIP?
Do L3 and 802.11s QoS schemes interact in a detrimental way?
Does the industry have any experience with peer-to-peer VoIP?
802.11s
IP
VoIP
Layer 2 mesh
Layer 3
Application
Per-hop drop in throughput; added delays and jitter
Peer-to-peer VoIP

## Slide 5: Additional Questions
Are there any scalability issues to consider?
Are there any successful implementation of peer-to-peer security? Powersave?
Does HCCA offer benefits? Are there any chipsets supporting HCCA?
Benefits over the Bluetooth approach?

## Slide 6: Bluetooth Evolution
v1.2 | v2.0 + EDR | v2.1 + EDR | V3.0 + HS
November 2003 | November 2004 | July 2007 | April 2009
Cell phone, headsets, notebooks, car kits, printers, GPS, cameras, MP3 players | New applications include: stereo headphones, sunglasses, radios, picture frames, PMPs |  | New applications include: high speed data transfers and video downloads
2.4 to 2.4835 GHz – AFH across 79 channels at 1600 hops per second |  |  | 802.11 channels
Class 1: 100 meter (100 mW); Class 2: 10 meter (2.5 mW); Class 3: 1 meter (1 mW) |  |  | 100 mW, 1W, 4W
GFSK (1 Mbps) | GFSK (1Mbps), π/4 DQPSK (2 Mbps), 8DPSK (3 Mbps) |  | OFDM with BPSK, QPSK,16-128QAM
TDMA multiple access |  |  | 
Manual pairing and security settings |  | Automatic discovery/security settings via SSP | 
Battery life 1x |  | Battery life 5x improvement | Battery life depends on radio in use
GFSK = Gaussian frequency shift keying
π/4 DQPSK = pi/4 rotated differential quaternary phase shift keying
8DPSK = 8 phase differential phase shift keying
AFH = adaptive frequency hopping
EDR = enhanced data rate
HS = high speed
SSP = secure simple pairing

## Slide 7: Bluetooth Considerations
Optimized for voice – all layer 2; apparent single layer efficiency
Synchronized Piconets
Piconet/Scatternet architecture appears to be scalable, at least on the surface
Authentication and encryption
Has there been any work in TGs evaluating 802.11s vs. Bluetooth for voice service?

## Slide 8: References
FCC press release regarding approval to deploy interoperable broadband networks for first responders, May 12 2010 http://hraunfoss.fcc.gov/edocs_public/attachmatch/DOC-298124A1.pdf
NPSTC (National Public Safety Telecommunications Council) http://www.npstc.org/committeeTC.jsp
APCO (Association of Public Safety Communications Officials) http://www.apco2011.org