## Slide 1: Public Safety Ad Hoc Requirements
Date: 2011-07-18
Authors:

## Slide 2: Public Safety Broadband Network
Spectrum in the 700 MHz band has been licensed by the FCC to carry a nationwide public safety broadband network [FCC-release].
In July of 2009 the 3GPP Long Term Evolution (LTE) was selected as the next generation technology for public safety communications.
Because the initial thrust of LTE has been on data services, voice over LTE is still in its infancy.

## Slide 3: UHF Spectrum, Including White Space Bands
Chart: 
| 54 | 60 | 66 | 76 | 82 | 174 | 180 | 186 | 192 | 198 | 204 | 210 | 470 | 476 | 482 | 488 | 494 | 500 | 506 | 512 | 518 | 524 | 530 | 536 | 542 | 548 | 554 | 560 | 566 | 572 | 578 | 584 | 590 | 596 | 602 | 608 | 614 | 620 | 626 | 632 | 638 | 644 | 650 | 656 | 662 | 668 | 674 | 680 | 686 | 692
FCC White Spaces | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
ECC White Spaces | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Low-700 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Hi-700 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
MHz
Low 700 MHz band
High 700 MHz band
US (FCC) White Spaces
54-72, 76-88, 174-216, 470-692 MHz
European (ECC) White Spaces (470-790 MHz)
Acquired by AT&T
Band12
Band17
Band12
Band17
ECC = Electronic Communications Committee
A
B C
D E
A
B C
A
B
A
B

## Slide 4: High 700 MHz Band
D-Block
Public Safety Broadband (763-768, 793-798 MHz)
Public Safety Narrowband (769-775, 799-805 MHz), local LMR
758
763
775
788
793
805
MHz
Guard band
Guard band
LMR = land mobile radio
Band 13
Band 13
Band 14
Band 14

## Slide 5: Requirements for Public Safety (PS) Network
Public safety mission critical requirements include:
  Push to talk (e.g. < 500 ms connection time)
  Low latency voice (e.g. < 100 ms)
  Talkaround when fixed infrastructure coverage is unavailable
  Security with encryption
  Simultaneous voice and data
Talkaround network consideration
  Clusters of tens of devices within 20-30 meters
  Interconnect clusters that may be separated by ~100 meters

## Slide 6: Possible Talkaround Approach
Peer-to-peer VoIP operating over 802.11s layer 2
Mobile mesh nodes
802.11s
IP
VoIP
Layer 2 mesh
Layer 3
Application
Per-hop drop in throughput; added delays and jitter
Peer-to-peer VoIP

## Slide 7: Questions for TGs Participants
Concerns regarding mission-critical VoIP?
Does the industry have any experience with VoIP over 802.11s? Peer-to-peer VoIP (or non-IP voice service) over 802.11s?
Are there any successful implementations of peer-to-peer security? Powersave?
Are there any scalability issues to consider?
Does HCCA offer benefits? Are there any chipsets supporting HCCA?
Has the group done any work comparing 802.11s to Bluetooth?

## Slide 8: Bluetooth Evolution
v1.2 | v2.0 + EDR | v2.1 + EDR | V3.0 + HS
November 2003 | November 2004 | July 2007 | April 2009
Cell phone, headsets, notebooks, car kits, printers, GPS, cameras, MP3 players | New applications include: stereo headphones, sunglasses, radios, picture frames, PMPs |  | New applications include: high speed data transfers and video downloads
2.4 to 2.4835 GHz – AFH across 79 channels at 1600 hops per second |  |  | 802.11 channels
Class 1: 100 meter (100 mW); Class 2: 10 meter (2.5 mW); Class 3: 1 meter (1 mW) |  |  | 100 mW, 1W, 4W
GFSK (1 Mbps) | GFSK (1Mbps), π/4 DQPSK (2 Mbps), 8DPSK (3 Mbps) |  | OFDM with BPSK, QPSK,16-128QAM
TDMA multiple access |  |  | 
Manual pairing and security settings |  | Automatic discovery/security settings via SSP | 
Battery life 1x |  | Battery life 5x improvement | Battery life depends on radio in use

## Slide 9: Bluetooth Considerations
Optimized for voice
  Layer 2 only – synchronous operation for voice
Synchronized Piconets
Piconet/Scatternet architecture appears to be scalable, at least on the protocol/architecture level
Authentication and encryption
Is the architecture scalable to large Scatternets?

## Slide 10: References
FCC press release regarding approval to deploy interoperable broadband networks for first responders, May 12 2010 http://hraunfoss.fcc.gov/edocs_public/attachmatch/DOC-298124A1.pdf
NPSTC (National Public Safety Telecommunications Council) http://www.npstc.org/committeeTC.jsp
APCO (Association of Public Safety Communications Officials) http://www.apco2011.org