## Slide 1: Using Upper Layer Message IE in TGai
Name | Affiliations | Address | Phone | email
Ping Fang | Huawei Technologies Co., Ltd. | Bldg 7, Vision Software Park, Road Gaoxin Sourth 9, Nanshan District, Shenzhen, Guangdong, China, 518057 | +86 755 36835101 | ping.fang@huawei.com
Zhiming Ding | Huawei Technologies Co., Ltd. | Bldg 7, Vision Software Park, Road Gaoxin Sourth 9, Nanshan District, Shenzhen, Guangdong, China, 518057 | +86 755 36835837 | dingzhiming@huawei.com
Xiandong Dong | Huawei Technologies Co., Ltd. | Bldg 7, Vision Software Park, Road Gaoxin Sourth 9, Nanshan District, Shenzhen, Guangdong, China, 518057 | +86 755 33913618 | dongxiandong@huawei.com
Date: 2011-07-17
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai which Upper Layel Message IEs are used in order to concurrent EAP, DHCP and 4-Way handshake.

## Slide 3: Usual network architecture & initial link setup
AP
AP
STA
DHCP Server
AS
Router
Internet
User Device
WiFi Access Network
Internet
1 Discovery & Association
2 EAP authentication
3 IP address Assignment
4 After link setup
5 Move
6 Possible Fast transition
11r Interface

## Slide 4: Our scope and essential principle
AP
AP
STA
DHCP Server
AS
Router
Internet
User Device
WiFi Access Network
Internet
11r Interface
We work on here
We shall not change this!
Key hierarchy must not be changed!

## Slide 5: How to reduce rounds on air interface?
Concurrent EAP procedure, DHCP procedure, 4-Way handshake and AID assigning.
  EAP messages and DHCP messages are encapsulated into the Authentication frames as Upper Layer Message IEs if the FILS procedure is indicated.
  The 4-way handshake function are merged into the Authentication frames.
  The Association frames are removed. The functions of the Association frames are moved to Authentication frames. The key point is that the AID is delivered together with the GTK through the third message of the 4-way handshake.

## Slide 6: Upper Layer Message IE
New Upper Layer Message IE may be defined as below
Upper layer message IE element format
Element ID
length
Upper layer message
ULM body
ULM
Type
1:EAP
2:DHCP
…
1 Oct.
Special value
254
2 Oct.

## Slide 7: How to compatible with old STAs
Authentication frames must be kept.
Add a new enumerative value to the field Algorithm in Authentication frame which means using FILS procedure.
Definitions in 11mb:
1 = Open systen
2 = Shared Key
3 = Fast BSS Transition
4 = FILS

## Slide 8: Modifications
Maximum length of IE is limited to 256 octet. So one EAP or DHCP message may be divided into multiple IEs. But if a special EID is defined with the meaning the length field is in two octets, a single IE can carry a whole upper layer message.
Association frames are not ignored if FILS is called.
4-Way handshake procedure is concurrent with EAP procedure if FILS is called.

## Slide 9: Questions & Comments