## Slide 1: Supported Operating Band
Date: 2011-07-20
Authors:

## Slide 2: Abstract
This submission proposes to use a public action frame to query the AP to find the frequency bands it operates in.
It also allows APs operating in multiple frequency bands to advertise themselves using only one of the frequency bands

## Slide 3: Supported Operating Band ANQP InfoID
The Supported Operating Band element provides information on the frequency bands supported by the hotspot. This element allows hotspots supporting more than one frequency band to advertise itself only on one of its supported frequency bands. This circumvents the need for multi-band supported STAs to search all frequency bands and the need to perform ANQP pre-associations per frequency band.

## Slide 4
 | Info ID | Length | Preferred Band | Operating Band #1 | Operating Band #2 (optional) | … | Operating Band #N (optional)
Octets: | 2 | 2 | 1 | 1 | 1 | … | 1
The Info ID is set to the value in Table 2 for Supported Operating Band.
The Length field is set to the value of 1 plus the total number of the Operating Band fields.
The Preferred Band field indicates the frequency band for the STA to operate after ANQP pre-association. The value of the Preferred Band field is set to one of the values in Table below.
The Operating Band #1 field tells the STA the frequency bands supported by the AP.
Meaning | Value
2.4GHz (default) | 0
5GHz (any) | 1
5170-5330 MHz | 2
5490-5719 MHz | 3
5735-5835 MHz | 4
Reserved | 5 … 255
Preferred Band field definition

## Slide 5
Operating band supported by hotspot | Value |  | Operating band supported by hotspot | Value
2.4GHz | 0 |  | 2.4GHz, 5170-5330 MHz | 9
5GHz (all sub-bands) | 1 |  | 2.4GHz, 5490-5719 MHz | 10
5170-5330 MHz | 2 |  | 2.4GHz, 5735-5835 MHz | 11
5490-5719 MHz | 3 |  | 2.4GHz, 5170-5330 MHz, 5490-5719 MHz | 12
5735-5835 MHz | 4 |  | 2.4GHz, 5170-5330 MHz, 5735-5835 MHz | 13
5170-5330 MHz, 5490-5719 MHz | 5 |  | 2.4GHz, 5490-5719 MHz, 5735-5835 MHz | 14
5170-5330 MHz, 5735-5835 MHz | 6 |  | ⁞ | ⁞
5490-5719 MHz, 5735-5835 MHz | 7 |  | Reserved | 15… 254
2.4GHz, 5GHz (all sub-bands) | 8 |  | Skip | 255
Operating Band #1 field definition
The reserved values in the Tables allow for future bands such as 60GHz and TV White Space to be specified.