## Slide 1: Comments Resolution on CID 3749
Slide 1
Date: 2011-07-21
Authors:
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Comment
3749 | Yang, Xun | 8.2.4.6.3 | 23.36 | If the Unsolicited MFB subfield is set to 1 and FB Tx Type subfield is set to 0, the unsolicited MFB refers to either an unbeamformed VHT PPDU or transmit diversity using an STBC VHT PPDU. That is, when the bit FB Tx Type sets to 0, it is not clear whether the received PPDU was using STBC or not. | Add a STBC-diversity FB bit together with the MFB bit to indicate whether the unsolicited MFB refers to a transmit diversity using an STBC VHT PPDU or not. Change the definition of MFB =1 and FB Tx Type =0 to refer to unbeamformed VHT PPDU only. See submission 11-11-xxxx-xx-00ac-resolution-to-comments-xxx for more details.

## Slide 3: Discussion
FB Tx Type in VHT format HT Control field:
  FB Tx Type subfield is set to 0 to indicate unbeamforming or transmit diversity when this field is in the unsolicited MFB frame
Only FB Tx Type cannot indicate all the possibilities clearly
Further, the transmitter has two choices to transmit the PPDU without beamforming:
  Unbeamforming without transmit diversity
  Unbeamforming with transmit diversity
  There should be difference between SNRs in the MFB field
  The transmit diversity gain and receive diversity gain are very large compared to multiplexing

## Slide 4: Discussion (Cont)
Scenario:
  2*2
  1 stream with STBC vs 2 streams (multiplexing)
  Channel model: C, Distance: 15m,
  BW: 20MHz
  MCS: PER<0.1
  SNR-MCS curve:

## Slide 5: Proposed Solution
Reuse one bit in VHT format HT control field to indicate STBC:
  STBC FB Type:
    0: transmission without STBC
    1: transmission with STBC
  Change the definition of FB Tx Type accordingly
  Location of the bit is in MSI:
    Traditional MSI (3 bits):
    Modified MSI format:
    (still 3 bits)
B3
B4
B5
Implementation specific
B3
B4
B5
Implementation specific
STBC FB Type
Note –The bit provides no change to the existing MSI sequence, only add a constraint for the choice of MSI.