IEEE P802.11
Wireless LANs

| TLV Structure comments |
| --- |
| Date: 2011-08-11 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Peter Ecclesine | Cisco Systems |  | +1-408-527-0815 | pecclesi@cisco.com |

## Interpretation of a Motion to Adopt

A motion to approve this submission means that the editing instructions and any changed or added material are actioned in the TGaf Draft.  This introduction is not part of the adopted material.

Editing instructions formatted like this are intended to be copied into the TGaf Draft (i.e. they are instructions to the 802.11 editor on how to merge the text with the baseline documents).

TGaf Editor: Editing instructions preceded by “TGaf Editor” are instructions to the TGaf editor to modify existing material in the TGaf draft.  As a result of adopting the changes, the TGaf editor will execute the instructions rather than copy them to the TGaf Draft.

LB 171 CIDs 1163, 1165:

| 1163 | E.3.1 | 134.15 | A little interpretation would not go amis. What does each column signify? In particular, should say that the length is the value in the length field, not the overall length of the TLV structure. Also the existence of (bits) in table E-15 raises ambiguity when absent. | As in comment And add (octets) under Length where (bits) not present |
| --- | --- | --- | --- | --- |
| 1165 | E.3.1.2 | 134.14 | I don't know what <ANA>.1 means. The type is an unsigned integer, so I fail to understand how it can hold a decimal number. | Perhaps add the following to E3.1: "The syntax 'n.m' means that the TLV has type m, and is embedded in the value field of a TLV of type n." |

Discussion:

LB 171 CID 1165 asks for the definition of <ANA>.1 as Type is an unsigned integer (32 bits) and could not hold a decimal n.m number. CID 1163 asks for the definition of the Length field to be clarified, especially where some fields are defined as bit fields. The stated length of the Type field is one byte.

Clearly the Draft 1.0 Type and Length must change to convey a broader range of values, and Type has to include more values than a single octet can represent. We propose to make Type an unsigned integer whose maximum value is 65 535, and the length of the Type field is two octets. It is easier to require that the Length field express all lengths in octets, and rewrite the Map ID value field, than it is to specify and implement a mixed syntax for TLV. We propose to replace <ANA>.x syntax with <ANA.x> syntax, and request the ANA assign consecutive values for <ANA>, <ANA.1>, <ANA.1.1>, <ANA.2>, etc.

Propose Revised for CIDs 1163 and 1165, refining definitions for TLV Type and Length fields and Type numbering per discussion and editing instructions in 11-11/1111r0.

Proposed Resolution:

Accept changes to P802.11af draft based on discussion and editing instructions in 11-11/1111r0:

TGaf Editor: change 8.2.6 TLV Values as follows:

The following TLV encodings may be used for parameters in MAC Management messages (8.3.3 (Management frames), 8.4 (Management frame body components) and 8.5 (Action frame format details)). TLV tuples with Type values not specified in this standard or specified as "reserved" shall be discarded. The STA shall discard any TLV tuple with an unknown value for Ttype number. The general form of TLV table is shown in Table 8-14a (General TLV values).

| General TLV values |
| --- |
| Name | Type | Length | Value | Scope |
|  | <ANA> | variable | Single or Compound TLVs. |  |

The length of the Type field shall be two octetsone byte.The format of the Length field shall be an unsigned number whose length is indicated by each TLV entry.

NOTE-Uniqueness of TLV Type values is assured by identifying the groups of IEEE 802.11 entities (MAC management messages) that share references to specific TLV encodings. Disjoint collections of TLVs are formed that correspond to each such functional grouping. Each set of TLVs that are explicitly defined to be members of a compound TLV structure form additional collections. Unique type values are assigned to the member TLV encodings of each collection.

An additional collection, the Common encodings, is defined that consists of TLV encodings that are referenced by more than one of the functional groups. The Type values of the TLV members of this collection are assigned to assure uniqueness across all collections. This is the only collection for which global uniqueness is guaranteed.

In cases where a collection contains TLV encodings that are PHY-specification-specific, subcollections are formed that contain these TLV encodings. Type values assigned to members of each subcollection are assigned so that the values are unique within the subcollection and with non-PHY-specification-specific members of the collection. Type values are not unique across PHY-specific subcollections.

TLV Type values are assigned in accordance with the following rules:

- Common encoding types start at 149, subsequent values are assigned in descending order.

- For individual collections, non-PHY-specification-specific encodings start at 1, subsequent values are assigned in ascending order.

- For individual collections, non-PHY-specification-specific encodings start at 150, subsequent values are assigned in ascending order.

- Unless otherwise indicated, bit 0 is the LSB of the least significant byte for all TLVs with length of multiple bytes.

The format of the Length field shall be an unsigned number whose length is indicated by each TLV entry’s Type.

A Single TLV has a Value that represents a single octet field, and a Compound TLV has a Value that represents more than one octet fields.

TGaf Editor: Change Table 8-14e Device Identification Information value field as follows:

| Name | Type | Length | Value | Scope |
| --- | --- | --- | --- | --- |
| FCC ID | <ANA>.1> | 14 | The device identification contains the 14 octet FCC ID of the device. | GDC_CAQ, US |
| Device Serial Number | <ANA>.2> | 4 | The Device Serial Number field is set to the manufacturer's serial number. This field is present only if the Device Class field (Table 8-14c (Device Class definition)) is equal to 1 (Personal/portable AP STA) or 2 (Fixed STA); otherwise, this field is not present. | GDC_CAQ, US |

TGaf Editor: Change Table 8-14h Channel Schedule Descriptor value field as follows:

| Name | Type | Length | Value | Scope |
| --- | --- | --- | --- | --- |
| Operating Class (optional) | <ANA>.1> | 1 | The Operating Class field is set to the number of the operating class of the channel, which is defined in Annex E.1 (Country information and operating classes). | RLS_CSM, US |
| Channel Number | <ANA>.2> | 1 | The Channel Number field is set to the number of the channel, which is subject to the value of Channel Schedule Management Mode field. If the Channel Schedule Management Mode field indicates the schedule information is based on WLAN channel, the channel number is a channel from the STA's operating class as defined in Annex E.1 (Country information and operating classes); otherwise, the Operating Class compound TLV will not be present and the Channel Number is a positive integer value as defined in Annex D.1 (External regulatory references) to indicate the available TV channel for WLAN operation. | RLS_CSM, US |
| Channel Availability Starting Time (optional) | <ANA>.3> | 8 | The Channel Availability Starting Time field indicates the starting time in Coordinated Universal Time (UTC) from when the channel indicated in the Channel Number field is available for operation. When this field is not present, the station will take the time that the response element is received as the starting time of the channel availability. | RLS_CSM, US |
| Channel Availability Duration | <ANA>.4> | 2 | The Channel Availability Duration field indicates the duration in minutes of the availability of the channel that indicated in the Channel Number field. | RLS_CSM, US |

TGaf Editor: Change Table 8-14j WSM information value field as follows:

| Name | Type | Length | Value | Scope |
| --- | --- | --- | --- | --- |
| Device Class | <ANA>.1> | 1 | The Device Class field is set to a value to identify the type of device to which the WSM is applied. If it is set to 0, it indicates Personal/Portable non-AP STA. If it is set to 1, it indicates Personal/Portable AP STA. If it is set to 2, it indicates Fixed STA. | GDC_WSM, US |
| Map ID | <ANA>.2> | 1 | Map ID field is an identifier of WSM information field format and the format of the Map ID bits is defined in Table 8-14k (Map ID value field). | GDC_WSM, US |
| Channel Availability | <ANA>.3> | 2 or 3 | The Channel Availability field indicates available channel information. The value of this field is defined in Table 8-14l (Channel Availability value field). This field is repeated as determined by the Length field in WSM element. | GDC_WSM, US |

TGaf Editor: Change Table 8-14k Map ID value field as follows:

| Name | Type | Length(bits) | Value | Scope |
| --- | --- | --- | --- | --- |
| Map ID parametersType | <ANA>.2.1> | 1 | Type bit is one bit in length and Bit 0: Type indicates whether the following channel list is a full channel list or a partial channel list. If the Type bit is set to 1, the following channel list is a full channel list and if the Type bit is set to 0, the following channel list is a partial channel list. Bits 1-7: Map version identifies the version of the WSM. | GDC_WSM, US |
| Map version | <ANA>.2.2 | 7 | Map version is 7 bits in length and identifies the version of WSM. | GDC_WSM, US |

TGaf Editor: Change Table 8-14l Channel Availability value field as follows:

| Name | Type | Length | Value | Scope |
| --- | --- | --- | --- | --- |
| Channel Number | <ANA>.3.1> | 1 | The Channel Number field is a positive integer value that indicates where the TV channel is available for WLAN operation. The length of the Channel Number field is 1 octet. When the Channel Number and Maximum Power Level pairs are repeated, they shall be listed in ascending TV channel order. | GDC_WSM, US |
| Maximum Power Level | <ANA>.3.2> | 1 | The Maximum Transmit Power Level field indicates the maximum power, in dBm, allowed to be transmitted on the Channel Number. | GDC_WSM, US |
| Validity (Optional) | <ANA>.3.3> | 1 | The Validity field indicates the time duration in minutes for which the Channel Number is available with the allowed Maximum Power Level, where the Validity is provided for each available Channel Number. If the Device Class value is set to 0, the Validity field is not present. If else, the Validity field for each Channel Number shall be provided. | GDC_WSM, US |

TGaf Editor: Globally where TLVs are described, change the length of the TLV Type field from 1 octet to 2 octets

# Text boxes

Abstract

Proposed resolutions for CIDs 1163 and 1165. Editing instructions are based on P802.11af Draft 1.02.