## Slide 1: Example of IP address assignment using Generic Upper Layer Message IE
Date: 2011-08-16
Authors:
Name | Affiliations | Address | Phone | email
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com

## Slide 2: Principles
Keep the layered network architecture.
IEEE802 network is running under various upper layer protocols.
  IEEE802 should be a generic framework of link layers for upper layers.
Upper layers are responsible for their own addressing architectures.
  For example, IETF is still extending DHCPv4/v6 protocols. Should we catch up their discussion forever??
Therefore, a mission of TGai is to provide a framework enabling upper layer (e.g. IPv4) to use their own protocol. (e.g. DHCPv4)

## Slide 3: Generic Upper Layer Message IE
The IE is proposed in order that management frames convey upper layer messages.
This proposal solves problems:
  Multiple upper layers (IPv4, IPv6 etc.)
  bigger messages than maximum IE size (255)
See 11-11-1003-02-00ai-upper-layer-data-on-management-frames for the detail.

## Slide 4: TGai Simplified Ideal Scenario
Association Request
Association Response
STA
AP
Beacon
How about IPv4/IPv6?

## Slide 5: IPv4’s case
IPv4 uses DHCPv4 for IP address assignment.
RFC4039 “Rapid Commit Option for the Dynamic Host Configuration Protocol version 4 (DHCPv4)” enables 2-message exchange.
  Only DHCPDISCOVER and DHCPACK are used.
  DHCPOFFER and DHCPREQUEST are omitted.
TGai should not define IP address management process:
  Lease time management
  Behavior of renewing lease
  Error recovery
  … all other things DHCP does
There are reasons TGai should not be involved in upper layer discussion:
  IPv4 has another minor methods like RARP, PPPoE…

## Slide 6: IPv4’s case using RFC4039
Association Request
Association Response
STA
AP
Beacon
DHCPDISCOVER with Rapid Commit Option (RFC4039) tells that STA needs IP address.
DHCPACK tells that DHCP server assigns IP address.
TGai-capable dhcp process starts.
dhcp process sends a packet via MLME interface, not a normal interface.

## Slide 7: IPv6’s case
IPv6 has two major methods:
  Stateless Address Autoconfiguration aka SLAAC (RFC4862)
  DHCPv6 (RFC3315)
There are lot of reasons TGai should not be involved in upper layer discussion:
  ‘SLACC attack’ is a famous problem.
  DHCPv6 is being extended actively in IETF DHC WG.

## Slide 8: IPv6’s case using SLAAC (RFC4862)
Association Request
Association Response
STA
AP
Beacon
Router Solicitation tells that STA needs configuration data.
Router Advertisement tells configurations of this network.
Router Advertisement tells that STA should use SLAAC.

## Slide 9: TGai Evaluation
TGai can assume an ideal IPv4 environment for TGai system evaluation.
  AP has DHCP server function.
  AP’s IEEE802.11 function cooperates with its DHCP server.
IETF and each manufacturer can make effort to apply TGai to various environments.
  Management of IP address pool?
  New configuration options?

## Slide 10: Additional Example: Complex case 1
Association Request
Association Response
STA
AP
Beacon
DHCPDISCOVER tells that STA needs IP address
DHCPACK tells that DHCP server assigns IP address
DHCP Server
DHCPDISCOVER
DHCPACK

## Slide 11: Additional Example: Complex case 2
Association Request
Association Response
STA
AP
Beacon
DHCPDISCOVER tells that STA needs IP address
DHCPACK tells that DHCP server assigns IP address
Action
Action
DHCPOFFER.
Some reason makes DHCP choose 4-way handshake…
DHCPREQUEST
This should be a decision of upper layer’s designer.

## Slide 12: Conclusion
Keep the layered architecture.
  TGai should provide generic framework for upper layers.
  TGai should not define parameters for upper layers.
  TGai should not be involved in discussion about upper layer’s problems, solutions and developments.
TGai can provide Generic Upper Layer Message IE for IP address assignment.
This presentation also shows how Generic Upper Layer Message IE is used for IPv4/v6 address assignment.
  IPv4/v6 already has almost enough function for our purpose.

## Slide 13: Discussion