IEEE P802.11
Wireless LANs

| Multi-floor indoor evaluation scenario |
| --- |
| Date: 2011-08-19 |
| Author: |
| Name | Company | Address | Phone | Email |
| Klaus Doppler | Nokia | 2054 University Ave, Suite 600 Berkeley, CA 94703 | +15104232458 | Klaus.doppler@nokia.com |

ABSTRACT

This submission proposes a multi-floor indoor scenario to be added to the functional requirements and the evaluation methodology for TGah. This scenario is a stress test for Use case group 3 Extended range WiFi [1] for extended home coverage. According to [3] by 2013 50% of US households will have a WiFi home network which is reflected by this scenario.

Indoor Application with Dozens of Stations for Extended Range Wi-Fi

Test case to demonstrate the operation of extended range Wi-Fi in apartment buildings with up to 50% of the apartments equipped with a Wi-Fi AP [3]. The scenario consists of 4 floors with 20 apartments in each floor. The floor layout is similar to the one used in [2].

Figure 1 Floor layout representing 20 apartments inside a single floor of a 4 floor apartment building [2].

10/20/40 TGah AP

APs are randomly placed at random positions inside apartments;

One AP per apartment

Traffic from AP to STAs

Internet File transfer

Traffic from STAs to AP

Internet File transfer

PHY channel for each link

Channel model type applied: multi-floor indoor model for TGah with floor attenuation applied

Locations of stations

20/40/80 STA randomly distributed in apartments with AP present.

STA are associated to AP in apartment

Throughput per AP

5th percentile of flow throughput cumulative distribution function

# References

- 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document

- TR 36.922 V10.0.0 3GPP Technical Specification Group Radio Access Network; Evolved Universal Terrestrial Radio Access (E-UTRA); TDD Home eNode B (HeNB) Radio Frequency (RF)  requirements analysis (Release 10)

- Nathan Safran, 802.11n: Laying the groundwork for the digital home, Forrester Research, March, 2009