## Slide 1: Fast Re-authentication in TGai
Name | Affiliations | Address | Phone | email
George Cherian | Qualcomm | 5775 Morehouse Dr, San Diego, CA, USA | 858-651-6645 | gcherian@qualcomm.com
Date: 2011-09-06
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai. Proposes EAP based Fast Re-authentication for Fast Initial Link Setup

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3

## Slide 4: Advantages of using EAP
EAP allows multiple authentication protocols to be supported without having to pre-negotiate a specific one
Allows authentication server to control which authentication protocol is used without the authenticator being fully configured
  Authenticator can act as a “pass through”
  Authenticator acts only on the outcome of authentication (say, deny access etc.)
Simplifies credential management
  Stored between authentication server and client
EAP is required for interworking with 3GPP EPC and WiMAX
  Pointed out in 1047r2

## Slide 5: Use of EAP for FILS
What is the issue in using EAP for FILS?
  EAP authentication typically requires a minimum of two roundtrips
Proposed Solution
  Use of EAP-RP (EAP Reauthentication protocol) for FILS
    RFC 5296
    Preserves all the benefits of EAP
    Re-authentication is completed using a single pair of messages
    Can interwork with cellular technologies when single credential is used (for WiFi and cellular) to access the network

## Slide 6: Overview of EAP-RP
STA
Auth1
Full EAP Method Exchange
Auth2
MSK, EMSK
rRK, rIK
AS
MSK, EMSK
rRK, rIK
EAP Success
(MSK)
EAP Success
Initial EAP Exchange
MSK
EAP Req/Identity
EAP Resp/Identity
EAP Re-auth Initiate (authenticated with rIK)
EAP Re-auth Finish (authenticated with rIK)
rMSK
rMSK
EAP-RP Exchange
(rMSK)
rMSK
EAP Re-auth Finish (authenticated with rIK)

## Slide 7: Key Hierarchy for ERP

## Slide 8: Questions & Comments