## Slide 1: Fast Re-authentication in TGai
Name | Affiliations | Address | Phone | email
George Cherian | Qualcomm | 5775 Morehouse Dr, San Diego, CA, USA | +1 (858)-651-6645 | gcherian@qualcomm.com
Jouni Malinen | Qualcomm | Hermiankatu 6-8 D Tampere, Finland |  | jouni@qca.qualcomm.com
Santosh Abraham | Qualcomm | 5775 Morehouse Dr, San Diego, CA, USA | +1 (858)-651-6107 | sabraham@qualcomm.com
Menzo Wentink | Qualcomm | Straatweg 66-S, Breukelen, Netherlands | +31-346-259-656 | mwentink@qualcomm.com
Date: 2011-09-06
Authors:

## Slide 2: Abstract
This document describes a technical proposal for TGai. Proposes EAP based Fast Re-authentication and simultaneous IP address acquisition

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | May be
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3, 4

## Slide 4: Introduction
Several contributions are under consideration for FILS authentication & IP address assignment
  See TGai contributions: 0767, 0976, 1047, 1124 etc.
Key principles followed in this contribution:
  Use of DHCP
    Use of DHCP Rapid commit
    DHCP is widely used for obtaining the IP address (also see 1047r2)
    DHCP exchanges must be protected
  Use of EAP
    Builds on existing EAP framework in 802.11
    Retains currently standardized 802.1x security architecture
    See additional advantages of using EAP in a later slide
How to reduce the message rounds
  Use of EAP-RP (EAP Reauthentication protocol)
  Concurrent use of EAP-RP & DHCP Rapid Commit

## Slide 5: Advantages of using EAP
EAP allows multiple authentication protocols to be supported without having to pre-negotiate a specific one
Allows authentication server to control which authentication protocol is used without the authenticator being fully configured
  Authenticator can act as a “pass through”
  Authenticator acts only on the outcome of authentication (say, deny access etc.)
Simplifies credential management
  Stored between authentication server and client
EAP is required for interworking with 3GPP EPC and WiMAX
  Pointed out in 1047r2

## Slide 6: Use of EAP for FILS
What is the issue in using EAP for FILS?
  EAP authentication typically requires a minimum of two roundtrips
Proposed Solution
  Use of EAP-RP (EAP Reauthentication protocol) for FILS
    RFC 5295/5296
    Preserves all the benefits of EAP
    Re-authentication is completed using a single pair of messages
    Can interwork with cellular technologies when single credential is used (for WiFi and cellular) to access the network
    STA is expected to be authenticated with the authentication server at least one time during its lifetime.

## Slide 7: Overview of EAP-RP
STA
Auth1
Full EAP Method Exchange
Auth2
MSK, EMSK
rRK, rIK
AS
MSK, EMSK
rRK, rIK
EAP Success
(MSK)
EAP Success
Initial EAP Exchange
MSK
EAP Req/Identity
EAP Resp/Identity
EAP Re-auth Initiate (authenticated with rIK)
EAP Re-auth Finish (authenticated with rIK)
rMSK
rMSK
EAP-RP Exchange
(rMSK)
rMSK
EAP Re-auth Finish (authenticated with rIK)

## Slide 8: Key Hierarchy for ERP
rRK, rIK is maintained by Authentication Server and STA (not passed to Access Point)
rMSK is passed to AP during ERP

## Slide 9: Fast Reauthentication with IP address assignment
[Step-0] Full authentication may happen using an AP or using a cellular system.
[step 2] AP transmits the Beacon/Probe Resp. which includes .11ai capability indicator for ERP & simultaneous IP addr assignment. AP changes Anonce frequent enough
[step-3] STA generates rMSK using [RFC 5296] before sending Assoc-Req
rMSK = KDF (K, S), where K = rRK and
S = rMSK label | "\0" | SEQ | length
[step-4] STA packs the following messages as IEs of Association-Request
  EAP Re-auth Initiate [Message Integrity using rIK]
  DHCP Discover with Rapid Commit [Encrypted using KEK]
  EAPOL-Key (Snonce, Anonce)
[step-4] STA applies message integrity on the combined payload that include EAP-Re-Auth, DHCP-Discover & EAPOL-Key using KCK
[step-5] AP holds the DHCP & EAPOL-Key message until it receives rMSK from AS
[step 8b] AP performs MIC for DHCP & EAPOL Key messages and decrypt DHCP

## Slide 10: Questions & Comments

## Slide 11: Appendix

## Slide 12: Why not just use 802.11r?
Scalability
  11r is used primarily in the context of fast-handoff from one AP to another
  STA may have a large interval (with no WiFi connectivity) after leaving the first AP (where the STA had a connectivity) before it connects to a new AP
  Caching the information for a large number of STAs over a large period of time is not scalable
Interworking with cellular network
  If the STA had used cellular system for IP connectivity and then move to WiFi, 11r will not be helpful to expedite the link-setup