## Slide 1: Fast Authentication in TGai
Name | Affiliations | Address | Phone | email
George Cherian Santosh Abraham Hemanth Sampath | Qualcomm | 5775 Morehouse Dr, San Diego, CA, USA | +1 (858)-651-6645 +1 (858)-651-6107 +1(858)-658-1848 | gcherian@qualcomm.com sabraham@qualcomm.com hsampath@qualcomm.com
Jouni Malinen | Qualcomm | Hermiankatu 6-8 D Tampere, Finland |  | jouni@qca.qualcomm.com
Menzo Wentink | Qualcomm | Straatweg 66-S, Breukelen, Netherlands | +31-346-259-656 | mwentink@qualcomm.com
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Hiroshi Mano | ROOT INC. | 7-21-11 Nishi-Gotanda, Shinagawa-ku, Tokyo 141-0031 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Mark RISON | CSR | Cambridge Business Park, Cowley Road, Cambridge CB4 0WZ UK | +44-1223-692000 | Mark.Rison@csr.com
Marc Emmelmann | Fraunhofer FOKUS | Kaiserin-Augusta-Alle 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Date: 2011-09-06
Authors:

## Slide 2: Abstract
This document proposes EAP-RP based Fast authentication and simultaneous IP address acquisition for FILS

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | May be
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 3, 4

## Slide 4: Background
Previous contributions such as 11/0976r3 to 11ai for FILS feature:
  Single pair of messages of authentication
  Use of Beacon/ProbeResp to send Anonce
  Use of Association Req/Resp to send ULI
Other contributions such as 11/1047 have proposed using EAP framework for FILS
We propose EAP-RP based Fast authentication and simultaneous IP address acquisition for FILS

## Slide 5: Introduction
Key principles followed in this contribution:
  Use of DHCP
    Use of DHCP Rapid commit
    DHCP is widely used for obtaining the IP address (also see 1047r2)
    DHCP exchanges must be protected
  Use of EAP
    Builds on existing EAP framework in 802.11
    Retains currently standardized 802.1x security architecture
    See additional advantages of using EAP in a later slide
  STA will execute full EAP authentication as part of the initial setup/provisioning
    Full EAP authentication can be considered as “out-of-the-box setup procedure”
    EAP-RP based re-authentication is used for FILS when the STA visits that network
How to reduce the message rounds
  Use of EAP-RP (EAP Reauthentication protocol)
  Concurrent use of EAP-RP & DHCP Rapid Commit

## Slide 6: An example of how the solution is applied for FILS
Use case: Hot-spot pass through:
  A user passes by (several, non overlapping) publicly accessible WiFi hot-spots (e.g. ATTwifi at Starbucks)
  While having connectivity, the user up-&downloads e-mails, twitter / facebook messages etc
Step-1: User buys an STA, performs full EAP authentication as part of initial setup with a network (say, ATTwifi )
  In this example, let’s say, the network allows the EAP session to be maintained for one year
  Step-2 [this step repeated afterwards]: The user passes by (several, non overlapping) publicly accessible WiFi hot-spots (e.g. ATTwifi at Starbucks)
  STA will perform Fast-Initial-Link setup with the ATTwifi network using EAP-RP

## Slide 7: High Level Concept*
STA
AP
4-way handshake,
no security
.11i authentication
.11i key setup
Existing .11
STA
AP
Fast Authentication & Upper Layer Setup (DHCP)
.11ai
4 phases into 1.
No need to process
sequentially. These
can be processed
simultaneously.
Upper Layer Setup
(i.e. DHCP)
* Slide merged from 11/0976r3

## Slide 8: Advantages of using EAP
EAP allows multiple authentication protocols to be supported without having to pre-negotiate a specific one
Allows authentication server to control which authentication protocol is used without the authenticator being fully configured
  Authenticator can act as a “pass through”
  Authenticator acts only on the outcome of authentication (say, deny access etc.)
Simplifies credential management
  Stored between authentication server and client
EAP is required for interworking with 3GPP EPC and WiMAX
  Pointed out in 1047r2

## Slide 9: Use of EAP for FILS
What is the issue in using EAP for FILS?
  EAP authentication typically requires a minimum of two roundtrips
Proposed Solution
  Use of EAP-RP (EAP Reauthentication protocol) for FILS
    RFC 5295/5296
    Preserves all the benefits of EAP
    Re-authentication is completed using a single pair of messages
    Can interwork with cellular technologies when single credential is used (for WiFi and cellular) to access the network

## Slide 10: Overview of EAP-RP
STA
Auth1
Full EAP Method Exchange
Auth2
MSK, EMSK
rRK, rIK
AS
MSK, EMSK
rRK, rIK
EAP Success
(MSK)
EAP Success
Initial EAP Exchange
MSK
EAP Req/Identity
EAP Resp/Identity
EAP Re-auth Initiate (authenticated with rIK)
EAP Re-auth Finish (authenticated with rIK)
rMSK
rMSK
EAP-RP Exchange
(rMSK)
rMSK
EAP Re-auth Finish (authenticated with rIK)

## Slide 11: Key Hierarchy for ERP
rRK, rIK is maintained by Authentication Server and STA (not passed to Access Point)
rMSK is passed to AP during ERP

## Slide 12: Fast Reauthentication with IP address assignment
[Step-0] Full authentication may happen using an AP or using a cellular system.
[step 2] AP transmits the Beacon/Probe Resp. which includes .11ai capability indicator for ERP & simultaneous IP addr assignment. AP changes Anonce frequent enough
[step-3] STA generates rMSK using [RFC 5296] before sending Assoc-Req
rMSK = KDF (K, S), where K = rRK and
S = rMSK label | "\0" | SEQ | length
[step-4] STA packs the following messages as IEs of Association-Request
  EAP Re-auth Initiate [Message Integrity using rIK]
  DHCP Discover with Rapid Commit [Encrypted using KEK]
  EAPOL-Key (Snonce, Anonce)
[step-4] STA applies message integrity on the combined payload that include EAP-Re-Auth, DHCP-Discover & EAPOL-Key using KCK
[step-5] AP holds the DHCP & EAPOL-Key message until it receives rMSK from AS
[step 8b] AP performs MIC for DHCP & EAPOL Key messages and decrypt DHCP

## Slide 13: Appendix

## Slide 14: Why not just use 802.11r?
Scalability
  11r is used primarily in the context of fast-handoff from one AP to another
  STA may have a large interval (with no WiFi connectivity) after leaving the first AP (where the STA had a connectivity) before it connects to a new AP
  Caching the information for a large number of STAs over a large period of time is not scalable
Interworking with cellular network
  If the STA had used cellular system for IP connectivity and then move to WiFi, 11r will not be helpful to expedite the link-setup