IEEE P802.11
Wireless LANs

| D1.0 Comment Resolution – TXOP for Group-Addressed Frames |
| --- |
| Date: 2011-09-14 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Reza Hedayat | Cisco Systems | 2200 E. G. Bush Turnpike, Richardson, TX 75082, USA |  | rehedaya at cisco.com |

Baseline document: 11ac D1.0.

The document proposes resolutions for the following CIDs:

MAC: 2615, 2632, 2741, 3705.

| 2615 | Kafle, Padam | N | 72.52 | 9.3.6 |  |  |  | The group addressed frames delivery should be capable to use TXOPs. The TXOPs is basic structure to allocate transmission resources for frames delivery and lack of TXOP support, the efficiency of the group addressed frames delivery is reduced. Typically frames are transmitted from multiple group addresses and delivery requires multiple contentions and avoids efficient operation of the 802.11ac networks. | Define TXOP for group addressed frames ot increase transmission efficiency of the VHT BSS. | Disagree. See Doc 1198. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| D2632 | Kakani, Naveen | Y | 72.52 | 9.3.6 |  |  |  | It is unclear what the statement: "In the absence of a PCF, when group addressed MPDUs in which the To DS field is 0 are transferred from a STA, only the basic access procedure shall be used." The group addressed frames delivery should be capable to use TXOPs. The TXOPs is basic structure to allocate transmission resources for frames delivery and lack of TXOP support, the efficiency of the group addressed frames delivery is reduced. For instance, a contention to obtain channel access is needed per group address. Typically frames are transmitted from multiple group addresses and delivery requires multiple contentions and avoids efficient operation of the 802.11ac networks. | Define TXOP for group addressed frames to increase transmission efficiency of the VHT BSS. | Disagree. See Doc 1198. |
| 2741 | Kneckt, Jarkko | Y | 72.53 | 9.3.6 |  |  |  | It is unclear what the statement: "In the absence of a PCF, when group addressed MPDUs in which the To DS field is 0 are transferred from a STA, only the basic access procedure shall be used." The group addressed frames delivery should be capable to use TXOPs. The TXOPs is basic structure to allocate transmission resources for frames delivery and lack of TXOP support, the efficiency of the group addressed frames delivery is reduced. For instance, a contention to obtain channel access is needed per group address. Typically frames are transmitted from multiple group addresses and delivery requires multiple contentions and avoids efficient operation of the 802.11ac networks. | Define TXOP for group addressed frames ot increase transmission efficiency of the VHT BSS. | Disagree. See Doc 1198. |
| 3705 | Varshney, Prabodh | Y | 72.53 | 9.3.6 |  |  |  | It is unclear what the statement: "In the absence of a PCF, when group addressed MPDUs in which the To DS field is 0 are transferred from a STA, only the basic access procedure shall be used." The group addressed frames delivery should be capable to use TXOPs. The TXOPs is basic structure to allocate transmission resources for frames delivery and lack of TXOP support, the efficiency of the group addressed frames delivery is reduced. For instance, a contention to obtain channel access is needed per group address. Typically frames are transmitted from multiple group addresses and delivery requires multiple contentions and avoids efficient operation of the 802.11ac networks. | Define TXOP for group addressed frames ot increase transmission efficiency of the VHT BSS. | Disagree. See Doc 1198. |

Proposed resolution: Disagree. Since this subject is not particularly tied to VHT activity TGac follows the baseline standard. On the other hand, there has been a great focus on group-addressed and groupcast frames in TGaa, and in order to avoid conflict it is more efficient to raise this comment for further discussion in TGaa.