IEEE P802.11
Wireless LANs

| D1.0 Comment Resolution – Various PHY CIDs |
| --- |
| Date: 2011-09-14 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Reza Hedayat | Cisco Systems | 2200 E. G. Bush Turnpike, Richardson, TX 75082, USA |  | rehedaya@cisco.com |
| Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134, USA |  | brianh@cisco.com |

Baseline document: 11ac D1.0.

The document proposes resolutions for the following CIDs:

PHY: 2366, 2367, 3201,	 3390, 3451.

| 2366 | Hart, Brian | N | 114.45 | 22.2.3 |  |  |  | 22.2.3 is great work, but arguably this detailed math is out of place so early in the clause. As well, there are great overlaps with Table 22-6 and section 22.3.14 | Find a new home for this material; and merge with related material to reduce duplication. E.g. in Table 22-6, replace f_c,idx1 by f_P20,idx etc. Extend table to have an extra column: e.g. CBW20, P20, formulas - , S20, formulas CBW40, P40, formulas - , S40, formulas CBW80, P80, formulas - , S80, formulas etc | Agree in principle. See Doc 11/1199. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Proposed resolution: Agree in principle. The equations in 22.2.3 are only referenced in 22.3.7 (Mathematical description of signals), hence it’s proposed to be moved there. Corrections are made to Table 22-6. However, no additional column is added to Table 22-6, since the equations and text explaining primary and secondary channels are lengthy and putting them in table would perhaps reduces readability of the table. Instead, those equations are proposed to be within the same sub-clause as in Table 22-6. The mathematical description of the primary and secondary channels are now within the same sub-clause as the mathematical description of signals in 22.3.7 (Mathematical description of signals). See editing instructions below.

| 3201 | Ponnampalam, Vish | N | 114.00 | 22.2.3 |  |  |  | The purpose of this text is to define primary/secondary channel indices for various BWs. The current text attempts to do this through equations. It is very complicated. A more elegant way would be to replace equations with tables. Each table would correspond to a given channel BW and would provide the primary/secondary channel indices for given values of N_20MHz and the primary 20MHz channel index. | Revise entire section as per comment. | Agree in principle. See Doc 11/1199. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Proposed resolution: Agree in principle. The equations in 22.2.3 are only referenced in 22.3.7 (Mathematical description of signals), hence it’s proposed to be moved there. However, these equations are not inserted in a table as the commenter proposes, since the equations and text explaining primary and secondary channels are lengthy and putting them in table would perhaps reduces readability of the table. Instead, those equations are proposed to be moved to the same sub-clause as in Table 22-6. See editing instructions below.

| 2367 | Hart, Brian | N | 115.05 | 22.2.3 |  |  |  | N_20MHz is also defined in 22.3.8.1.4 | Remove 1 definition and update via xref | Agree. See Doc 11/1199. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Proposed resolution: Agree. See editing instructions below that removed the definition in 22.3.8.1.4 and references the new place where N_20MHz is defined, in 22.3.7 (Mathematical description of signals).

| 3390 | Rosdahl, Jon | Y | 116.14 | 22.2.3 |  |  |  | What about CBW20 and CBW40 for NON_HT? | Clarify | Agree. See Doc 11/1199. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Proposed resolution: Agree. See editing instructions below.

| 3451 | Shi, Wei | Y | 116.00 | 22.2.3 |  |  |  | Table 22-2 is missing entries for NON_HT CBW20 and NON_HT CBW40. Is there any reason why they are not included? They are valid options. | Please clarify and add. | Agree. See Doc 11/1199. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Proposed resolution: Agree. See editing instructions below.

TGac Editor: Change as follows

22.2.3 Effects of CH_BANDWIDTH parameter on PPDU format

Move the text and equations, starting from the first paragraph in this sub-clause all the way to the paragraph before Table 22-2, to 22.3.7 (Mathematical description of signals)

TGac Editor: Note that there are two Table 22-2 (one in P116, below table, and another in P117, ref to D1.0), which needs to be fixed.

Table 22-2 (PPDU format as a function of CH_BANDWIDTH parameter) shows the PPDU format as a function

of the CH_BANDWIDTH parameter.

TGac Editor: Insert the following two rows to Table 22-2 as shown.

Table 22-2— PPDU format as a function of CH_BANDWIDTH parameter

| FORMAT | CH_BANDWIDTH | PPDU format |
| --- | --- | --- |
| VHT | CBW80+80 | The STA transmits a VHT format packet of 80+80 MHz bandwidth. |
| NON_HT | CBW20 | The STA transmits the packet using the Clause 17 format using the primary 20 MHz channel. |
| NON_HT | CBW40 | The STA transmits the packet using the Clause 17 format in each of the two adjacent 20 MHz channels. If the VHT BSS BW is wider than 40 MHz, then the transmission shall use the primary 40 MHz channel. The 20 MHz channel higher in frequency is rotated +90º relative to the 20 MHz channel lower in frequency as defined in Equation (22-11). |
| NON_HT | CBW80 | The STA transmits the packet using the Clause 17 format in each of the four adjacent 20 MHz channels. If the VHT BSS BW is wider than 80 MHz, then the transmission shall use the primary 80 MHz channel. The three 20 MHz channels higher in frequency are rotated +180º relative to the 20 MHz channel lowest in frequency as defined in Equation (22-12). |

TGac Editor: Change as follows

22.3.7 Mathematical description of signals

For a description of the conventions used for the mathematical description of the signals, see 17.3.2.5 (Mathematical

conventions in the signal descriptions).

For description on subcarrier indices over which the signal is transmitted for non-HT and HT PPDUs, see

19.3.7 (Mathematical description of signals).

For a 20 MHz VHT PPDU transmission, the 20 MHz is divided into 64 subcarriers. The signal is transmitted

on subcarriers -28 to -1 and 1 to 28, with 0 being the center (DC) carrier.

For a 40 MHz VHT PPDU transmission, the 40 MHz is divided into 128 subcarriers. The signal is transmitted

on subcarriers -58 to -2 and 2 to 58.

For an 80 MHz VHT PPDU transmission, the 80 MHz is divided into 256 subcarriers. The signal is transmitted

on subcarriers -122 to -2 and 2 to 122.

For a 160 MHz VHT PPDU transmission, the 160 MHz is divided into 512 subcarriers. The signal is transmitted

on subcarriers -250 to -130, -126 to -6, 6 to 126, and 130 to 250.

For a non-contiguous 80+80 MHz VHT PPDU transmission, each 80 MHz frequency segment is divided into

256 subcarriers. In each frequency segment, the signal is transmitted on subcarriers -122 to -2 and 2 to 122.

TGac Editor: Move the text and equations from 22.2.3 (Effects of CH_BANDWIDTH parameter on PPDU format) to here

The transmitted signal is described in complex baseband signal notation. The actual transmitted signal is related

to the complex baseband signal by the relation shown in Equation (22-7).

Table 22-6—Center frequency of a PPDU transmitted in frequency segment i_{Seg}

| dot11CurrentChannel Bandwidth | CH_BANDWIDTH | f_c^{(i_{Seg})} |
| --- | --- | --- |
|  |  | i_{Seg}=0 | i_{Seg}=1 |
| 20MHz | CWB20 | f_{CH,start}+5 × f_{ P20,idx} | - |
| 40MHz | CWB20 | f_{CH,start}+5 × f_{P20,idx} | - |
|  | CWB40 | f_{CH,start}+5 × f_{c,idx1} | - |
| 80MHz | CWB20 | f_{CH,start}+5 × f_{P20,idx} | - |
|  | CWB40 | f_{CH,start}+5 × f_{P40,idx} | - |
|  | CWB80 | f_{CH,start}+5 × f_{c,idx1} | - |
| 160MHz | CWB20 | f_{CH,start}+5 × f_{P20,idx} | - |
|  | CWB40 | f_{CH,start}+5 × f_{P40,idx} | - |
|  | CWB80 | f_{CH,start}+5 × f_{P80,idx} | - |
|  | CWB160 | f_{CH,start}+5 × f_{c,idx1} | - |
| 80+80 MHz | CWB20 | f_{CH,start}+5 × f_{P20,idx} | - |
|  | CWB40 | f_{CH,start}+5 × f_{P40,idx} | - |
|  | CWB80 | f_{CH,start}+5 × f_{P80,idx} | - |
|  | CWB160 | f_{CH,start}+5 × f_{P80,idx} | f_{CH,start}+5 × f{S80,idx} |

TGac Editor: Change as follows

22.3.8.1.4 L-SIG definition

TGac Editor: Change the definition of N_{20MHz} in P140L13 to:

where

N_{20MHz}	is defined in 22.3.7 (Mathematical description of signals)