IEEE P802.11
Wireless LANs

| D1.0 Comment Resolution – 22.3.6 Timing-ralated parameters |
| --- |
| Date: 2011-09-14 |
| Author(s): |
| Name | Affiliation | Address | Phone | email |
| Illsoo Sohn | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1882 | Illsoo.sohn@lge.com |
| Yongho Seok | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang-Shi, Kyungki-Do, 431-749, Korea | +82-31-450-1947 | yongho.seok@lge.com |

Abstract

This document provides resolutions for the following comments to 11ac spec draft D1.0:

CIDs 2391 and 2392.

222.3.6 Timing-related parameters

| 2391 | 22.3.6 | 130.57 | Unfortunately this definition is inconsistent with P135L49, where the meaning of Nu is adjusted throughout the PPDU | Resolve the inconsistency; either: a) e.g. define NU = Nu,preVHT or Nu,VHT; Nu,VHT = NUM_USERS b) Provide two versions of eqn 22-9: one for pre-VHT modulation (1user, 1STS, Nu and Nsts not used), and one for VHT-modulation |
| --- | --- | --- | --- | --- |
| 2392 | 22.3.6 | 130.60 | Refer to TXVECTOR parameter; also u=0,1,2,3 should be 0,1,..Nu-1. Ditto for NSS. But of course this is then inconsistent with P135L58 wher the meaning of N_STS,u is adjusted throughout the PPDU | As in comment for range of u; and resolve the inconsistency; either: a) e.g. define Nsts,u = Nsts,preVHT or Nsts,u,VHT; Nsts,u,VHT = NUM_STS b) Provide two versions of eqn 22-9: one for pre-VHT modulation (1user, 1STS, Nu and Nsts not used), and one for VHT-modulation |

##### Proposed resolution:

Agree in principle. As the commenter pointed out, the meanings of Nu, NSTS, and Nss are different for pre-VHT modulated fields and VHT modulated fields. The definitions of Nu, NSTS, and Nss need to be clarified. Also, the definitions should be consistent in subclause 22.3.6 and subclause 22.3.7.

##### Editing Instructions

22. Very High Throughput (VHT) PHY specification

22.3 VHT PLCP sublayer

22.3.6 Timing-related parameters

Editor: Please make the following changes and add a new note in Table 22-5—Frequently used parameters:

| Frequently used parameters |
| --- |
| Symbol | Explanation |
| Nu | For pre-VHT modulated fields, Nu=1. For VHT modulated fields, Nu represents the number of users in the transmission (equal to the TXVECTOR parameter NUM_USERS). |
| NSTS, NSTS,u | For pre-VHT modulated fields, NSTS,u=1(See NOTE2). For VHT modulated fields, NSTS,u is the number of space-time streams for user u, u=0,1,2,3. For SU packets, NSTS = NSTS,0. For MU packets, NSTS is undefined. |
| NSTS,total | For VHT modulated fields, NSTS,total is total number of space-time streams in a packet. For pre-VHT modulated fields, NSTS,total is undefined. Note that NSTS,total = NSTS for SU packets. |
| NOTE1-- pre-VHT modulated fields refer to the L-STF, L-LTF, L-SIG and VHT-SIG-A fields, while VHT modulated fields refer to the VHT-STF, VHT-LTF, VHT-SIG-B and Data fields NOTE2--For pre-VHT modulated fields, u is 0 only since Nu=1 |

22.3.7 Mathematical description of signals

Editor: Please make the following change in notations below equation (22-19):

Nu 	For pre-VHT modulated fields, Nu=1. For VHT modulated fields, Nu represents the number of users in the transmission (equal to the TXVECTOR parameter NUM_USERS).

NSTS,u	For pre-VHT modulated fields, NSTS,u=1. For VHT modulated fields, NSTS,u is the number of space-time streams (equal to the TXVECTOR parameter NUM_USERS) for user u, u=0,1,2,3.