## Slide 1: The Purpose and Justification of WAPI Comparing Apples to Apples, not Apples to Lemons
Date: 2011-09-14
Authors:

## Slide 2: Abstract
This document identifies flaws in the analysis of WAPI and RSN by the proponents of WAPI. It demonstrates that WAPI has a limited applicability to WLANs due to its limited support of user credentials and deployment scenarios. It sums up the Purpose and Justification for WAPI.

## Slide 3: Authentication and Key Management
Protocols used in WAPI and RSN perform authentication of a client and a server over an untrusted connection
  WAPI uses WAI, RSN uses EAP
WAI and EAP both perform mutual authentication and derive a secret key*
  WAI performs a Diffie-Hellman and authenticates that exchange using the Digital Signature Algorithm. Only supports certificates as a credential.
  EAP is an extensible authentication protocol and allows use of many different credentials.
* Using an EAP method that is appropriate for use in a WLAN– see 802.11 standard for description

## Slide 4: Authentication and Key Management
Both use 2 party protocols for authentication and derivation of a shared key
Each side uses different actors to effect the 2 party protocol
RSN Components
  STA: a device, the “client side” of EAP
  AP: a STA, therefore a device, that provides access to a DS
  AS: an entity that provides authentication services, the “server side” of EAP
WAPI Components:
  ASUE: a device containing the “client side” of WAI
  AE: an entity that provides authentication services, the “server side” of WAI
  ASE: an entity that performs a certificate status check

## Slide 5: The Simplistic and Naïve View
There are 3 boxes!
Boxes correspond to each other in a 1:1 manner
The “Centralized AS Case”
ASUE
AE
ASE
STA
AP
AS
RSN
WAPI
???
???
???

## Slide 6: The Simplistic and Naïve View
The “AP-integrated AS Case”
  ASE and AE functionality are co-located on one device
  “The AE and integrated ASE need certificates. However, in this scenario a single certificate per AP is sufficient and can be shared by the AE and ASE”*
ASUE
AE
ASE
STA
AP
AS
RSN
WAPI
???
???
* Direct quote from “WAPI and 802.11 Authentication and Key Management” by H.R. Thomann

## Slide 7: The Simplistic and Naïve View
The “Centralized AS Case”
  Incorrectly assumes that the AS and the ASE are functionally equivalent
The “AP-integrated AS Case”
  “The AE and integrated ASE need certificates. However, in this scenario a single certificate per AP is sufficient and can be shared by the AE and ASE”
  This belies a fundamental misunderstanding of certificate use and the whole point of certificate validation
    The ASE is supposed to provide an assurance to the ASUE that the AE’s certificate is valid
    If the ASUE trusts the ASE’s certificate then it trusts the AE’s certificate and therefore there is no point in the ASE!
    If the ASE and AE share a certificate, the statement of the ASE on its certificate (the AE’s certificate) is not trustworthy

## Slide 8: What is the ASE in WAPI?
ASE receives certificates, nonces and MAC addresses of the ASUE and AE
  The nonces and MAC addresses are not signed and have no integrity check. The ASE makes no comment on the validity of this data
  The ASE only checks whether the two certificates are valid
    Its range of responses is limited to certificate validity only
    It cannot know whether the ASUE or AE possess the private keys whose analogs are in the certificates it is evaluating
The ASE only performs certificate validation*
  It performs no other function
  It does not take part in mutual authentication of the ASUE and AE
* The representative of the Swiss NB agrees with this

## Slide 9: What is the AS in RSN?
An entity that performs the server side of EAP
The AS contains a credential that it uses to authenticate itself to the client side of EAP, the STA
The AS authenticates the client side of EAP using the client’s credential
The AS establishes a shared and secret key with the client
The AS does not do certificate validation*
* The representative of the Swiss NB agrees with this

## Slide 10: AS in RSN and ASE in WAPI
Given
  The ASE in WAPI only does certificate validation
  The AS in RSN does many things but none of them involve certificate validation
Lemma
  There is no functional overlap between these the ASE in WAPI and the AS in RSN
Logical Conclusion
  The AS in RSN is not analogous to the ASE in WAPI

## Slide 11: Implications of AS != ASE
The Simplistic and Naïve View is invalid
  The “AS box” and “ASE box” perform different functions and do not match up
  The AS (server side of EAP) corresponds to the AE (server side of WAI)
  The ASE has no analog in RSN. There is no box to match up!
  The AP in RSN is a device with a radio that provides access to the DS (there is actually an analog in the WAPI specification but it has no role in security)
ASUE
AE
ASE
STA
AP
AS
RSN
WAPI

## Slide 12: Implications of AS != ASE
The “AP-integrated AS Case” for WAPI falls apart
  An ASE cannot be integrated into an AE because the certificate trust model is voided– reduces to self-signed certs or pointless ASE
  WAPI does not and cannot support such a thing
For RSN, an AS can be integrated into the AP, in fact this is the natural order of things
STA
AP
AS
RSN
WAPI
NOT SUPPORTED!

## Slide 13: Supported Scenarios for RSN and WAPI
WAPI acknowledges the existence of an AP– the device in which the AE resides
The STA and ASUE correspond to similar functions
The AP/AS and AP/AE correspond to similar functions
STA
AP
AS
RSN
ASUE
ASE
WAPI
AP
AE

## Slide 14: Supported Scenarios for both RSN and WAPI
WAPI only supports one scenario
  A client, the ASUE whose analog is the STA in RSN
  A server, the AE whose analog is the AS in RSN
  An AP that contains the AE
  An ASE that has no analog in RSN
RSN supports the WAPI scenario
  A client, the STA whose analog is the ASUE in WAPI
  A server, the AS whose analog is the AE in WAPI
  An AP that contains the AS
RSN supports EAP methods that do ECDH and ECDSA

## Slide 15: RSN Supports Additional Scenarios
Multiple credential support
  Username/password credentials on the client
  Shared passwords/psks using a zero knowledge cryptographic proof
  Token cards providing 2-factor client authentication
Aggregation of the AS services of multiple APs
  Attractive when using a credential, like username/password, that have particular scaling problems in large deployments
Proponents of WAPI take issue with aggregation of AS services
  Which might be relevant to the NP and CRM discussion if WAPI supported such scenarios

## Slide 16: Purpose and Justification of WAPI
WAPI supports one scenario only; RSN supports the identical scenario identically
  WAPI is a duplication of a subset of RSN functionality
  The security differences are minimal and where they exist they are to the detriment of WAPI
WAPI fails to address the issues its proponents have aggregated AS services
  If the alleged “loopholes” were valid then their proposed solution does nothing to address them!
  It is pointless to continue discussion of alleged shortcomings in a scenario of RSN that WAPI does not and cannot support
WAPI has no purpose and justification

## Slide 17: References
“WAPI and 802.11 Authentication and Key Management”– H.R Thomann