## Slide 1: 802.11ah Channel Access Improvement
Date: 2011-09-19
Authors:

## Slide 2: Abstract
This presentation proposes a high level concept of improvement to 802.11ah channel access.

## Slide 3: 802.11ah Use Case Categories [1]
802.11ah defines three use case categories
  Use Case 1 : Sensors and meters
  Use Case 2 : Backhaul sensor and meter data
  Use Case 3 : Extended range Wi-Fi
Use Case 1 and 3 have different traffic characteristics
  Use Case 1: small packet size and low duty-cycle
  Use Case 3: large packet size and high duty-cycle
Coexistence issue between Use Case 1 and Use Case 3

## Slide 4: Coexistence Issue between Use Case 1 and Use Case 3
A low duty-cycle STA (Use Case 1) suffers from high duty-cycle STA (Use Case 3)
  When the channel utilization is high due to hotspot or cellular offloading applications, sensors may experience a long channel access delay  power consumption increases
Data-Ack
Sensor STA wakes up and tries to send a packet
DIFS
CW back-off =3
1) STA-2 waits until the channel is idle
(Idle Channel Wait Time)
DIFS
Data-Ack
2) STA-2 loses contention and waits again until the channel is idle
CW back-off =4
STA-1
(hotspot: high duty-cycle traffic)
STA-2
(sensor: low duty-cycle traffic)

## Slide 5: Proposed Channel Access Enhancement
Give the highest priority to low duty-cycle (sensor) traffic for channel access
  Sensor traffic has a very low duty-cycle compared to other hotspot or cellular offloading applications  does not hurt high-duty cycle applications
  Reducing the channel access delay is critical to sensors for a long battery life
  Redefine/remap EDCA access categories (AC) to give sensor traffic the highest priority
Data-Ack
Data-Ack
Data-Ack
1) Sensor STA wakes up and tries to send a packet
DIFS
CW back-off =3
2) STA-2 waits until the channel is idle
(Idle Channel Wait Time)
DIFS
3) STA-2 wins the contention
CW back-off =4
STA-1
(hotspot: high duty-cycle traffic)
STA-2
(sensor: low duty-cycle traffic)
AIFS[non-sensor]
AIFS[sensor]
DIFS
4) Sensor STA goes back to sleep until next packet transmission time
5) Hotspot STA continues transmissions

## Slide 6: Summary
802.11ah Use Case 1 (sensor) and Use Case 3 (extended range Wi-Fi) have different traffic characteristics
Need to address the coexistence issue between the sensor use case and the extended range Wi-Fi use case
We propose to redefine/remap EDCA access categories (AC) to give sensor traffic the highest priority

## Slide 7: References
[1] Rolf de Vegt, “Potential Compromise for 802.11ah Use Case Document,” 11-11/457r0.