## Slide 1: Active Scanning Improvement
Date: 2011-09-19
Authors:

## Slide 2: Abstract
The presentation addresses how to improve active scanning in the context of TGai providing Fast Initial Link Set-Up

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Marc Emmelmann, FOKUS

## Slide 4: Overview
Limiting time spent in active scanning  return after 1st AP has been found
Improvements for 5GHz operation  receiving enabling signal via other channel

## Slide 5: Limiting time spent in active scanning  return after 1st AP has been found

## Slide 6: Limiting time spent in active scanning
Main idea: return from active scanning immediately after the 1st AP has been found.
Not possible right now:
  scan until „ProbeTimer reaches MaxChannelTime [and] process all received probe responses“ unless the channel is continuously idle [11Revmb-D9, 10.1.4.3.3]
  Go through all channels
Idea: If a MIB variable is set (e.g.: dot11FILSscanFor1stApOnly is set to 1), the scanning returns after having detected the 1st AP.
  Values of MaxChannelTime are ignored
  Remaining channels to be scanned are ignored
We currently have methods of selecting to look only for specific APs via [11Revmb-D9, 6.3.3.2.2]
  SSID List (11k)
  AccessNetworkType (11u)
  HESSID (11u)
Shall we add an “ignore” field which contains SSIDs or ESSIDs which should not be considered for aborting the scan (e.g.: start a 2nd scan because we did not like what we got in the first place)
Note: 11k is in large parts optional. Are the manditory AccessNetoworkType and HESSID infos enough for us?

## Slide 7: Actions (1)
Request to Editor:
  Elaborate if it is required to comply to a special framework for MIB variables used / newly defined by TGai (naming, format, potential hierarchy)
Motion:
  Move the author(s) of 11/1232 to present draft amending text to TGai,
    that text to be further considered to an additional vote to adopt the text as part of the TGai draft
    that text focusing on the following features within the scope of TGai:
      Returning from active scanning after having found the 1st AP
      Having that feature selectively enabled via a MIB variable
  Moved: Seconded:
  Yes: No: Abstain:

## Slide 8: Improvements for 5GHz operation  receiving enabling signal via other channel

## Slide 9: Main Idea
Enable active scanning on 5GHz channels
Main idea: retrieve the “enabling signal” containing information on which regulated channels can be used, on a different channel
  Either non-radar channels in 5GHz
  On other frequencies (2.4GHz, 60GHz, etc.)
After being enabled for operation on a particular channel, directly start an active scan

## Slide 10: Regulation
FCC: CHAPTER I--FEDERAL COMMUNICATIONS COMMISSIONPART 15--RADIO FREQUENCY DEVICES
ECC/DEC/(04)08 (2005/513/EC) (2007/90/EC): ECC Decision of 09 July 2004 on the harmonised use of the 5 GHz frequency bands for the implementation of Wireless Access Systems including Radio Local Area Networks (W AS/RLANs)

## Slide 11: FCC 15.15(b) General technical requirements
“Except as follows, an intentional or unintentional radiator must be constructed such that the adjustments of any control that is readily accessible by or intended to be accessible to the user will not cause operation of the device in violation of the regulations.“
 The AP has to determine itself (without user configuration) on which 5GHz channel it may operate on (= do not trust user input)

## Slide 12: FCC 15.202 Certified operating frequency range
„Client devices that operate in a master/client network may be certified if they have the capability of operating outside permissible part 15 frequency bands, provided they operate on only permissible part 15 frequencies under the control of the master device with which they communicate. Master devices marketed within the United States must be limited to operation on permissible part 15 frequencies. Client devices that can also act as master de- vices must meet the requirements of a master device. For the purposes of this section, a master device is defined as a device operating in a mode in which it has the capability to transmit without receiving an enabling signal. In this mode it is able to select a channel and initiate a network by sending enabling signals to other devices. A network al- ways has at least one device operating in master mode. A client device is de- fined as a device operating in a mode in which the transmissions of the device are under control of the master. A de- vice in client mode is not able to initiate a network.“
 does not specify the „enabling signal“
 does not say that the enabling signal must be received on the channel the Master/Client will operate on
 We currently have two sanity checks: a) Maser announces enabling signal on channel it operates on (=beacon)  malicious devices can easily be detected; b) Slave has to hear an active master on the operating channel
 currently, the enabling signal is NOT received via an encrypted / verified channel (it is the regular beacon). Why is there a need to do an encryption if the enabling signal is received via another channel?
 Attn.: There might be another issue: an enabling signal on, e.g. 2.4GHz channel travels further than on on a 5GHz channel  enabling on a larger (not permissible?) area

## Slide 13: ECC/DEC/(04)08 (2005/513/EC) (2007/90/EC)
ECC Decision of 09 July 2004 on the harmonised use of the 5 GHz frequency bands for the implementation of Wireless Access Systems including Radio Local Area Networks (W AS/RLANs)
§1: „With regard to DFS, a WAS/RLAN device shall operate in either Master Mode or Slave Mode. WAS/RLAN devices operating in Slave Mode (Slave Device) can only operate in a network controlled by a WAS/RLAN device operating in Master Mode (Master Device).“
§1: „Every Master Device will use the Radar Interference Detection function in order to check for any co-channel radar signal prior to use a channel but also during normal operation. In addition to this Radar Interference Detection function, every Master Device shall also implement a channel selection mechanism to ensure a near uniform spread of the loading of available spectrum. The Slave Devices shall not transmit before having received an appropriate enabling signal from a Master Device. Slave Devices with a power level of 200 mW e.i.r.p. or above shall have their own Radar Interference Detection function.“
 does not say anything about the enabling signal (e.g. the channel it is transmitted on)

## Slide 14: Certification & Political Issues
Currently, 5GHz and 2.4 GHz devices are separately tested for certification
Currently, devices are tested for DFS (radar) compliance by generating an artificial radar signal and check the behavior of the master (AP) and in particular the behavior of slaves (non-AP STAs) under the control of the master.
Do we mandate a new (combined) certification process?
Some interest groups might be unwilling to adopt something new (e.g. radar companies defending their business area)

## Slide 15: Related 802.11 Work
Concept of 802.11af White space map might be used to realize this

## Slide 16: Thoughts
If we directly start a transmission on the 5GHz channel after having received an enabling signal on a different signal, may I disturb a Quite Period that the Master scheduled on the 5GHz channel for DFS?
 Our approach may involve a very tight coupling of the enabling signal on another channel, and the behavior of on the 5GHz  only send the enabling signal if we are not in sensing mode with Master
Alternative approach:
  in the enablement signal, include timing information when to expect the next beacon on the channel to later operate on.
  Then the STA could go to that channel just when the beacon arrives and conduct a passive scan.
  BUT this makes the process still lengthy since we have to wait for the beacon to arrive. We just might optimize the performance if we have a number of channels (and beacon arrival times) to choose from
  Note: this can only help to improve performance in an implementation specific manner as we have to start a new MLME-scan after having received this information. Such scan would have to be executed in a time constrained manner  implementation specific
  Could create an entirely new scan which tries to a) receive enablement signal, and b) passivly verify this information WHILE a) and b) are atomic within a single MLME service primitive  thereby we could impose timing constraints  enablement signal on non-5GHz channel only a „hint“  can continue to use existing certivication procedures

## Slide 17: Actions (2)
Motion:
  Move the author(s) of 11/1232 to present further details on how to enable active scanning in 5GHz operation channels
Moved: Seconded:
Yes: No: Abstain:
Motion
  Move the Chair to request a joint session with IEEE 802.11 REG SC in November to discuss regulatory issues involved in enabling active scanning in 5GHz by “providing enablement via another channel”
Moved: Seconded:
Yes: No: Abstain:

## Slide 18: Action (3)
Motion:
  Move the author(s) of 11/1232 to present further details on a new scanning MLME service primitive which
    Waits or queries for the reception of an enablement signal containing information on APs operating on this or other channels including information when to expect the beacon to be broadcasted
    Verifies the existence of the APs announced via the enablement signal via (passive) scanning
    Where both of the above steps are conducted by one MLME service primitive as one atomic action
    Imposing performance constrains on the novel service primitive
Moved: Seconded:
Yes: No: Abstain:

## Slide 19: References
11-10/922r2: Achievable gains in AP discovery (Marc Emmelmann, Fraunhofer FOKUS)
11-10/965r1: Potential performance improvement with fast initial link set-up (Marc Emmelmann, Fraunhofer FOKUS & Root Inc.)
11-11/1237: TGai Key Technical Ideas (M. Emmelmann, Fraunhofer FOKUS)