## Slide 1: Passive Scanning Improvement
Date: 2011-09-20
Authors:

## Slide 2: Abstract
This presentation addresses how to improve passive scanning in the context of TGai providing Fast Initial Link Set-Up

## Slide 3: Conformance w/ Tgai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1
Marc Emmelmann, FOKUS

## Slide 4: State of the Art Passive Scanning
Scan through all available channels
STA “shall listen to each channel scanned for no longer than a maximum duration defined by the MaxChannelTime“ [11REVmb-D4, Cls 11.1.3.1]

## Slide 5: Main Idea – Stop after having found the 1st “suitable” AP
Only possible in vendor specific implementations:
  “shall listen to each channel scanned for no longer than a maximum duration defined by the MaxChannelTime“ [11REVmb-D4, Cls 11.1.3.1]  does not prohibit a STA to quit bevor MaxChannelTime
  Still have to go through all channels
  BUT: currently, there is not option to the MLME-SCAN.request primitive forcing this behavior.
Idea: If a MIB variable is set (e.g.: dot11FILSscanFor1stApOnly is set to 1), the scanning returns after having detected the 1st AP.
  Remaining channels to be scanned are ignored
We currently have methods of selecting to look only for specific APs via [11Revmb-D9, 6.3.3.2.2]
  SSID List (11k)
  AccessNetworkType (11u)
  HESSID (11u)
Shall we add an “ignore” field which contains SSIDs or ESSIDs which should not be considered for aborting the scan (e.g.: start a 2nd scan because we did not like what we got in the first place)
Note: 11k is in large parts optional. Are the manditory AccessNetoworkType and HESSID infos enough for us?

## Slide 6: Action (1)
Request to Editor:
  Elaborate if it is required to comply to a special framework for MIB variables used / newly defined by TGai (naming, format, potential hierarchy)
Motion:
  Move the author(s) of 11/1233 to present draft amending text to TGai,
    that text to be further considered to an additional vote to adopt the text as part of the TGai draft
    that text focusing on the following features within the scope of TGai:
      Returning from passive scanning after having found the 1st AP
      Having that feature selectively enabled via a MIB variable
  Moved: Seconded:
  Yes: No: Abstain:

## Slide 7: References
11-10/922r2: Achievable gains in AP discovery (Marc Emmelmann, Fraunhofer FOKUS)
11-10/965r1: Potential performance improvement with fast initial link set-up (Marc Emmelmann, Fraunhofer FOKUS & Root Inc.)
11-11/1237: TGai Key Technical Ideas (M. Emmelmann, Fraunhofer FOKUS)